## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: IEEE802.15.3: Proposed amendments to the TG3-MAC.
Date Submitted: 18th June, 2001
Source: Dr. Rajugopal Gubbi Company: Broadcom, corp
Address: 400, E-Caribbean Drive, Sunnyvale, CA 95084
Voice: +1.408-543-3470, FAX: +1.408-543-3470, E-Mail: rgubbi@Broadcom.com
Re: [ ]
Abstract: This presents proposed amendments to the TG3-MAC
Purpose: To provide an improvement to the current version of the 802.15.3 MAC
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that these viewgraphs becomes the property of IEEE and may be made publicly available by P802.15

## Slide 2: Overview
Transmit power control (TPC)
Power save operation
Fragmentation and de-fragmentation
Priority management
Modification to Implied-ack
peer discovery
Frame exchange rules
Delayed-ack expedite request
Changes to FC
Changes to chan-time request command
Changes to stream mgmt command
Moving tx-rate limitations from clause-7 to clause 8
Broadcast Device-Info table periodically

## Slide 3: What is being presented?
SIMPLE schemes to the remaining open items (except auth/sec) in the draft
A list of changes to fix the holes in the current schemes and enhance performance
Some of the schemes proposed here are modified versions of the proposals by others either through a formal doc or through discussions on the reflector.

## Slide 4: Transmit power control (1)
In the lines of work in TGh
A table of transmit power levels must be specified
Each DEV must be able to request the current tx-power level of its peer (only in the frames destined to the requestor)
Each DEV must be able to request one out of the specified tx-power levels for the frames destined to the requestor
Protocol must be flexible to allow each DEV to use different tx-power levels for different dest-DEVs
One simple TPC scheme (FMTP) and a sophisticated scheme (AMTP) are proposed

## Slide 5: Transmit power control (2)
PNC broadcasts the maximum tx power level in the beacon. PNC uses channel status from each DEV to decide this.
A DEV that has simple TPC implemented (FMTP: Fixed maximum transmit power level) simply sets all its transmissions to the level broadcasted by PNC
A DEV that has sophisticated TPC implemented (AMTP: Adjustable maximum transmit power level) chooses the minimum of the requested power level and the limit indicated by the PNC in its beacon.
DEV with AMTP may maintain a separate tx power level for each of its dest-peer

## Slide 6: Power Save (1)
Three states of power management, (a) Active state (b) Snooze state and (c ) Sleep state
In Active state the DEV is awake all the time
In Snooze state the DEV will be in the low power mode. The snooze state is used during any time slot when there is no tx or rx allocated for the DEV. Hence snooze state can be used within any super frame
Intention of using Sleep state must be indicated in capability field during association. The sleep state may last for more than one superframe.

## Slide 7: Power Save (2)
Permission to go to sleep must be obtained by the DEV from PNC just before going to sleep state
When the PNC rejects the request, the DEV must remain awake and request again later
When the PNC permits, the DEV can sleep for the time indicated in the sleep-permission command from PNC
When the DEV wakes up from sleep, the DEV must wait for reception of at least one beacon before INITIATING any frame sequence (but it can respond to a frame directed to it).
If the PNC-DEV communication did not happen for longer than the timeout indicated in ASSOC frame, the DEV is considered disconnected.

## Slide 8: Fragmentation and Defragmentation (1)
At the Tx, the start and end of MSDU/MCDU is indicated in separate bits in FC of MAC header
Sequence number is incremented for all fragments in MSDU/MCDU.
NO frag-number. (lesser the better!)
Hence retx request becomes simpler and economical
For practical purposes, a limit f 8Kbytes of max size on MSDU/MCDU is specified

## Slide 9: Fragmentation and Defragmentation (2)
At the rx, whenever Frag-Start is seen, a new MSDU/MCDU buffer is assumed to have started.
Whenever a Frag-end is seen, the current MSDU/MCDU is assumed to have ended.
If one or more frames i missing (after all retx efforts) in an MSDU/MCDU the entire MSDU/MCDU may be dropped.

## Slide 10: Proposal for priority management (1)
Define 8 priorities as in 802.1D. Use priority=0 for all non-data frames and priority=1 being reserved.
In addition, add a bit to indicate stream type (Isoch or async) as part of Stream identification
Add the above 4-bit field in the MAC header for traffic monitoring purpose at PNC: The stream index must be reduced to 12 bits and the remaining 4 bits must be used to indicate the 4-bit priority field
PNC shall allocate channel time for all Isoch first and highest to lowest priority streams in that order.

## Slide 11: Proposal for priority management (2)
PNC shall indicate the Isoch allocation in CTA
DEVs shall transmit Isoch streams at their allocated times only. Non-Isoch streams shall be transmitted in the order of their priority

## Slide 12: Advantage of the Proposed priority management
Makes use of existing 802.1D work on priority management. No re-invention needed.
Hence mapping of priorities at TG3-MAC becomes simple

## Slide 13: Modification to Implied-ack
Responding DEV shall send only one frame for a received frame soliciting implied-ack
Responding DEV can take any length of time within the current GTS without exceeding it
Responding DEV can send imm-ack as response to an implied-ack solicitation
Responding DEV shall send imm-ack if it does not know the end of current GTS
Responding DEV shall make sure there is enough room in the current GTS for the im-ack, if required, for the frame sent as response to implied-ack solicitation.

## Slide 14: Peer discovery
Peer discovery is implied in all the previous versions of the draft, but never explicitly stated\
A clause is added regarding this.
The DEVs use the already defined “Probe information” command to request/provide/obtain the DEV specific information that is required for the stream transactions

## Slide 15: Frame exchange rules
Reference 01/301r0 by Bill
Three important rules are as follows
PNCS/AUTH/ASSOC frame exchanges must be in CAP only
All stream-DATA type frames in CFP only
Command frames can be in CAP if the DEV does not have a non-isoch time slot allocated to it in the current superframe
Detailed list is provided in clause 8.13

## Slide 16: Delayed-ack expedite request
When delayed-ack is used, the source DEV must be able to request the dest-DEV to expedite sending the accumulated delayed-ack
A bit-11 in stream-ID field is used for this purpose in the stream transmission by the source-DEV
Since the frame with this request could be lost in the channel, the bit is interpreted as “Send delayed-ack at your earliest convenience”
If this request is correctly rxd, the dest-DEV attempts sending the delayed-ack before the end of NEXT super frame

## Slide 17: Changes to FC
Frag-start and Frag-End bits added
Del-Ack-request bit in FC
Do we need retry bit? I don’t see the need for it. could save a bit in FC for future use (like the one below)
Pad byte indication for stream-data type frames to allow always word aligned transmissions. Rest of the frames formats are designed to be word aligned.
The source-DEV sets this bit to ‘1’ if the current data body is of odd byte length and pads a byte at the end of the frame body before FCS field. Otherwise this bit is set to ‘0’.

## Slide 18: Changes to channel time request command
Removal of request for all the four priorities. This reduces overhead in most of the simple PAN devices with at most one stream to a destination.
Addition of stream identification in the place of destination address. Dest-address inclusion is already approved. But the stream identification provides stream-type(Isoch/Async), priority and stream index. Using stream index the PNC can find the dest-DEV.
This change keeps the change to stream management command consistent where stream-ID is required along with the channel-time-request block

## Slide 19: Changes to stream management command
Channel time request in stream mgmt command. This allows the PNC to not allow the stream if the requested time can not be provided
Including ACK-policy in stream mgmt command. This was always intended but left out in previous drafts. Without this the parameters like retx-window does not make any sense.

## Slide 20: Moving multi-rate usage table from 7.3.1
Table 56 in 7.3.1 in d4 belongs in clause 8.8 (293r1) where multi-rate support is discussed.

## Slide 21: Braodcasting DEV-Info by PNC
PNC must be specified to broadcast the device-information (table) periodically (aBroadcastDevInfoDuration).
This helps in reducing the delay in PNC-handover by letting all the PNC-capable DEVs to keep their local tables current.