## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [PHY proposal for the 802.15.4 Low Rate WPAN Standard]
Date Submitted: [July 2001]
Source: [Hans van Leeuwen] Company: [STS/Adcon RF Technologies]
Address: [Zekeringstraat 40, 1014 BT Amsterdam, Netherlands]
Voice:[+31 20 420 4200], FAX: [+31 20 420 9652], E-Mail:[HvL@STS.nl]
Re: [PHY layer proposal submission, in response of the Call for Proposals ]
Abstract: [This contribution is a PHY proposal for a Low Rate WPAN intended to be compliant with the P802.15.4 PAR. It is intended to support both star and peer-to-peer communications for low data rate networks, implemented at both 868 MHz-928MHz and at 2.4GHz. It is designed to support ultra low power consumption for battery operated nodes at very low implementation cost.
Purpose: [Unified MAC proposal]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Design Philosophy (1)
We are addressing a community of users who want to design for the unified MAC using a single PHY for 868/-928 ISM bands and another (separate) PHY for the 2.4GHz band.

## Slide 3: Design Philosophy (2)
Who don’t necessarily want to use the 2.4GHz ISM band but DO want a single common PHY for the 868-928MHz bands.
Especially the 868 band, since it’s very well regulated.

## Slide 4: Design Limitations
868MHz in Europe (ERC 70-03)provides 600Khz of bandwidth, a power limit of 25mW and a duty cycle of <1%.
902-928MHz (FCC part 15) PG> 10 dB and a 100% duty cycle .

## Slide 5: Physical layer proposal for low datarate @ 868-928MHz
Conforms to the unified MAC proposal.
Tailored to fit the needs of the lower frequency bands.
Uses DSSS 10kbps 31chips/symbol
Single chip transceiver implementation already available
Provides a single PHY - a virtual world band

## Slide 6: Transceiver characteristics
31 chips spreading enables coexistence with other applications.
Data-shaping lowers used bandwidth (important for 868MHz, only 600kHz available)
10kbps data-rate is sufficient for short or infrequent data exchange (high latency)
High integration eases software development and reduces processor cost

## Slide 7: Transceiver characteristics (2)
Allows seamless integration with micro-controller
Micro-controller can have tight grip on transceiver behaviour (timing)
Single chip solution has very low external part count and parts can be of low spec.
Two dimensional parallel search (in code and frequency) allows for cheap crystals

## Slide 8: Transceiver characteristics (3)
A SAW filter is only required at the receive side and can be of high tolerance (low cost)
Single chip implementation supports low power modes as described in the Unified MAC proposal
Transceiver air-frame easily meets MAC requirements

## Slide 9: Transceiver air-format
The air-frame consists of:
  Preamble (a continuous stream of zeroes)
  Start byte (0x02)
  Payload
  End of frame marker (0x02 0xFF)
  CRC (8-bit)
Data transmission is made transparent by internal byte stuffing

## Slide 10: The air-format applied
The payload of the transceiver can be used to convey higher level framed data i.e.
preamble
sof
start of packet
header
MAC packet data unit
payload
eof
crc

## Slide 11: Performance Sync Algorithm

## Slide 12
An actual implementation

## Slide 13
Low complexity Low cost
front
back

## Slide 14: Manufacturing Costs
Current implementation die size 12,25 mm2 in CMOS 0,35 
Future implementation die size 8 mm2 in CMOS 0,16 
Sub-dollar is a practical possibility

## Slide 15: Power Consumption aspects
Supports all power saving aspects of the unified MAC proposal
Built-in wakeup timer
Idle and sleep mode
Use of optional extra low frequency Xtal further reduces drain

## Slide 16: Link Budget
0 dBM output power
-95 dBM sensitivity
= 95 dB budget
Line of sight range > 1.5 km

## Slide 17: Time to market
Engineering samples July 2001
first production quantities Q4 2001