## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [PHY proposal for the Low Rate 802.15.4 Standard]
Date Submitted: [10 July, 2001]
Source: [Ed Callaway] Company: [Motorola]
Address: [8000 W. Sunrise Blvd., M/S 2141, Plantation, FL 33322]
Voice:[(954) 723-8341], FAX: [(954) 723-3712], E-Mail:[ed.callaway@motorola.com]
Re: [WPAN-802.15.4 Call for Proposals; Doc. IEEE 802.15-01/136r1]
Abstract: [This presentation represents Motorola and Philips’ proposal for the P802.15.4 PHY standard, emphasizing the need for a low cost system having excellent sensitivity and long battery life.]
Purpose: [Response to WPAN-802.15.4 Call for Proposals]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: PHY Proposal for the Low Rate 802.15.4 Standard
Ed Callaway, Member of the Technical Staff
Motorola Labs
Phone: +1-954-723-8341
Fax: +1-954-723-3712
ed.callaway@motorola.com

## Slide 3: Features
Modified from r0 to:
  Enable 250 kb/s operation
  Enable easy conversion to low data rate operation
Low chip rate (1 MHz) for low power operation
O-QPSK, for constant envelope modulation
  Simple, low-cost PA
4- to 6-dB sensitivity advantage over conventional FM-DSSS approaches
  Greater range for a given output power
5 MHz channel separation
  16 channels in the 2.4 GHz band
  Eases channel filter requirements to lower die size & cost
  Can be used for location determination

## Slide 4: Channelization
2.4 GHz band; 16 channels; 5 MHz channel separation
f = 2405 + 5k MHz, k = 0, 1, … 15
Fixed channelization chosen by dedicated device at network initiation
16 channels allow for 16 simultaneous operating WPANs
5 MHz channel spacing sufficient for location determination using DSSS TDOA methods

## Slide 5: Spreading and Modulation
1 Mc/s chip rate, 31.25 kS/s (32-chip pn sequences)
Offset-QPSK, with half-sine shaping
Augmented pn sequences: CP = 45 (I), CP = 75 (Q)
8-symbol preamble used on both I & Q , augmented CP = 67 (scanning node must correlate only one PN sequence)
Differential Code Position Modulation (D-CPM) used on both I & Q.
  The pn sequence on each channel is (independently) cyclically shifted to one of 16 Gray-coded positions.
  Information is transmitted on each channel as the difference in chip 0 positions from one symbol to the next.
Resulting bit rate is 250 kb/s

## Slide 6: Differential Code Position Modulation
I
Q
Symbol 0001
…
cn+1
c31
c0
…
cn-1
Easily converted to low data rate of 31.25 kb/s
  set I = Q, transmit 1 b/S
Symbol 0000
…
ca+1
c31
c0
ca
…
ca-1
Preamble
…
c31
c30
Preamble
…
c31
c30
cn
c0
c0
cb+1
cb
cm
cm+1
Symbol 0011
Symbol 0010
…
…

## Slide 7
BER
BER Curve
4 dB @ 10-3
4.5 dB @ 10-4

## Slide 8: Orthogonal Signaling = Improved Sensitivity
Source: Bernard Sklar, Digital Communications. Englewood Cliffs, New Jersey: Prentice-Hall, 1988, p. 179.
K = 4, 6.5 dB
K = 1, 11 dB
K = 4, 7.5 dB
K = 1, 12.5 dB

## Slide 9: Receiver Implementation Options
Conventional DSSS decoding
  8 dB Eb/N0 (-98 dBm with NF = 15 dB) @ 10-4 BER, 250 kb/s
  ~3 kHz (1.2 ppm) tolerable frequency offset
  Excellent sensitivity; AFC needed
Differential chip decoding
  14 dB Eb/N0 (-92 dBm with NF = 15 dB) @ 10-4 BER, 250 kb/s
  ~100 kHz (>40 ppm) tolerable frequency offset
  Sensitivity similar to conventional DSSS; very inexpensive reference can be used

## Slide 10: 2.4 GHz DSSS Transmitter Size
1 kbit data register
1023 chip SS generator
RF synthesizer & loop
filter
1 mW PA
2.5 x 2.5 mm die
0.18 um standard digital
CMOS
80% empty space

## Slide 11: 2.4 GHz DSSS Receiver Size
Benchmark:
  6 bit x 508 chip complex correlator, plus timing & control circuits, 0.18 um
  Total active area = 4 mm2, at 60% utilization; 80k gates
Our proposal:
  4 bit x 128 chip complex correlator (for preamble)
  2, 4 x 32 chip data correlators
  Timing recovery & control
  Total 26k gates; 1.4 mm2, even at 60% utilization; 1k data register an additional 7k gates (0.35 mm2)
Total Tx/Rx digital:
  40k gates, 2 mm2

## Slide 12: RF Modem
Analog:
  PLL/frequency generation
  Down conversion
  Tx PA
  IF gain
  IF filtering: 2 poles @ 5 MHz
  ADC analog portion
Analog total: 0.6 mm2
Digital
  ADC digital portion
  Filtering
Digital modem total:
20k gates, 1 mm2

## Slide 13
DSSS signal recovery 2.0 mm2
Analog 0.6
ADC & Digital filtering 1.0
Active area total: 3.6 mm2
Size Summary

## Slide 14: Transceiver Specifications
BER ~ 1E-4  PER < 2% (Assuming 12 bytes overhead + 10 bytes payload data = 176 bits/packet)
Sensitivity ~ -92 dBm using differential decoding
(-98 dBm using conventional DSSS decoding)
Selectivity ~ -45 dBm adjacent channel (5 MHz offset)
Signal acquisition using DSSS preamble (8 symbols) with correlator
(4-5 symbols needed to sync using AGC)

## Slide 15: System Considerations
Multipath
  10m range (indoors) implies worst case path length = 2x10m = 60nS. Proposed system can tolerate a delay spread > 100 ns, so there should be no problem in most applications
Interference and Jamming resistance -- Implementation dependent, can be designed to tolerate:
  +20 dBm 802.11b 10m away
  0 dBm 802.15.1 1m away
  Microwave ovens in quiet half-cycle
Intermodulation resistance – -20 dBm IIP3 required
Coexistence and throughput with co-located systems (multiple access)
  Low duty cycle systems, interference should be low

## Slide 16: Power / Range
Power:
Duty cycle = 0.1%
Transceiver active mode = 10 mW
Transceiver sleep mode = 20 uW
Average power drain is
0.001*10 mW + 0.999 *20uW = 30 uW
If this node is supplied by a 750 mAh AAA battery, linearly regulated to 1 V, it has a battery life of 2.8 years (25,000 h).
Range (250 kb/s):
Range outdoors, LOS > 100m
Range indoors = 10m
Also based on –92 dBm Rx sensitivity

## Slide 17: Scalability
Power consumption greatly reduced in sleep mode
(20 uW vs. 10 mW)
Data rate may be adjusted from 1-8 bits/symbol
(31.25 – 250 kb/s); lower with additional coding
Narrowband systems supported: 31.25 kb/s @ 8 bits/symbol = 125 kc/s
Functionality of nodes varies with role, topology
(Distribution and Slave nodes)
Cost per device varies according to functionality of a given node
Network size is scalable due to ad hoc nature of the network and large number of possible clusters

## Slide 18: Bottom Line
Cost estimate is $2 for quantity of 10M
(Includes everything from antenna port to bits)
Implementation size (active area)
  In 0.18 um, it is 3.6 mm2
  (Total active area = RF/analog + Baseband)
Technical feasibility & Manufacturability
  MD demonstration and network simulations available
  Matlab simulations of Code Position Modulation concept
  At present, developing single chip solution
  Samples available Q1 2002

## Slide 19: General Solution Criteria
Criteria | Ref | Value
Unit Manufacturing Cost ($) | 2.1 | $2 for 10M units
Interference and Susceptibility | 2.2.2 | 30-2350 and 2.530-13 GHz, -50 dBm; Adj. Channel (5 MHz), 2400-2483 MHz, -45 dBm
Intermodulation Resistance | 2.2.3 | -20 dBm IIP3
Jamming Resistance | 2.2.4 | Can tolerate – +20 dBm 802.11b 10m away 0 dBm 802.15.1 1m away Microwave ovens in quiet half-cycle
Multiple Access | 2.2.5 | 
Coexistence | 2.2.6 | Low duty cycle systems, interference should be low

## Slide 20: General Solution Criteria
Criteria | Ref | Value
Interoperability | 2.3 | True
Manufacturability | 2.4.1 | Single chip solution in development
Time to Market | 2.4.2 | Samples available Q1 2002
Regulatory Impact | 2.4.3 | True
Maturity of Solution | 2.4.4 | MD demo and network simulations available Matlab simulations of D-CPM
Scalability | 2.5 | 4 of 5 areas listed + network size
Location Awareness | 2.6 | True

## Slide 21: PHY Protocol Criteria
Criteria | Ref | Value
Size and Form Factor | 4.1 | Total active area in 0.18um = 3.6 mm2
Frequency Band | 4.2 | 2.4 GHz
# of Simultaneously Operating Full-Throughput PANs | 4.3 | 16
Signal Acquisition Method | 4.4 | DSSS with correlator
Range | 4.5 | Range outdoors, LOS > 100m Range indoors = 10m
Sensitivity | 4.6 | -92 dBm (differential decoding); -98 dBm (conventional DSSS decoding)
Delay Spread Tolerance | 4.7.2 | 100 ns
Power Consumption | 4.8 | Active mode = 10 mW Sleep mode = 20 uW