## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: IEEE802.15.3: A proposal for improvements to the 802.15.3 MAC to allow static GTS slots and unassigned GTS slots.
Date Submitted: 10 July, 2001
Source: Dr. William Shvodian Company: XtremeSpectrum
Address: 8133 Leesburg Pike, Suite 700, Vienna, Virginia 22182
Voice: +1.703.749-0230 X7129, FAX: +1.703.749.0249, E-Mail: bshvodian@xtremespectrum.com
Re: [ ]
Abstract: This proposal presents some proposed improvements to the 802.15.3 MAC which allow static GTS slots and unassigned GTS slots .
Purpose: To provide an improvement to the current version of the 802.15.2 MAC
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Overview
Static assigned GTS slots would beneficial. This presentation shows how static and pseudo-static GTS slots can be added to the 802.15.3 MAC in a simple, robust and flexible manner.
Unassigned GTS slots can be useful for a number of reasons, including sharing a channel with adjacent piconets and/or daughter piconets as presented by Akahane-san from Sony. This document will show how unassigned GTS slots can be requested and “assigned” with no change to the current baseline.

## Slide 3: Current GTS Slot Assignments
Currently GTS slot assignments are announced in every beacon.
The PNC is free to change the GTS slot assignments in any Beacon.
Devices need to listen to every beacons to determine which slots they will transmit in and which slots they must be listening to.
Since the PNC can change the GTS slot assignments in any beacon. Because of this, if a station receives a Beacon in error, it cannot transmit in that beacon in order to avoid collisions.

## Slide 4: Benefits of Static GTS Slot assignments
Static GTS slot assignments allow low power devices to participate in a WPAN without processing the CTAs in every beacon
Static GTS slots allow stations to transmit in a superframe where they received the Beacon in error.
Allows for the sharing a channel with an adjacent piconet or daughter piconet.
PNC could use directed frames to make static GTS slot assignments.

## Slide 5: Myth: Static GTS slots are Hard to Manage
802.15.3 originally looked at using static GTS slot assignments but decided against them because they were too difficult to manage. The concern is that if you move a static (or pseudo-static) GTS slot, a collision will occur if both transmitting stations don’t receive the change sequence correctly.
In reality Static GTS slots can be managed with a simple and robust scheme

## Slide 6: New Definitions
Static GTS Slot: A GTS Slot that is never moved by the PNC
Pseudo-static GTS Slot: A GTS slot that is only moved by the PNC sending directed Channel Time Grant frames to both the sender and receiver
Some applications may require static GTS slots. Others may be able to use pseudo-static GTS slot assignments.

## Slide 7: Why move a pseudo-Static GTS slot?
If completely static assignments are made, then eventually the channel may become fragmented like a hard drive. There may be ample unassigned channel time in the superframe for additional assignments, but assignments cannot be made because the available slots are too small to be assigned.
The PNC will need to re-locate GTS slots to “de-fragment” the superframe.

## Slide 8: The concern about moving “pseudo-static” GTS slots
If a GTS slot is being taken away from one station and given to another, both stations must receive the change message without error in order to avoid a collision.
Both the transmitter and receiver of a moved GTS slot must be receive the change message without error to ensure that frames are not lost.

## Slide 9: GTS slot “defragmentation”
Contention
Access
Period
Beacon
Contention Free Period
1
2
4
5
3
Contention
Access
Period
Beacon
Contention Free Period
1
2
4
5
3
GTS for Superframe n
GTS for Superframe n+1
Unassigned GTS time

## Slide 10: Potential for GTS slot collision
Contention
Access
Period
Beacon
Contention Free Period
1
2
4
5
3
Contention
Access
Period
Beacon
Contention Free Period
1
2
4
5
3
GTS for Superframe n
GTS for Superframe n+1
If station 3 did not get the change message, station 3 and station 4 will collide. Likewise, station 4 could collide with station 5

## Slide 11: Potential for Receiver Missing a Frame
Contention
Access
Period
Beacon
Contention Free Period
1
2
4
5
3
Contention
Access
Period
Beacon
Contention Free Period
1
2
4
5
3
GTS for Superframe n
GTS for Superframe n+1
If the receiver of slot 4 got the change message, but the transmitter of slot did not, station 4 will listen to a different slot than station 4 is transmitting in.

## Slide 12: Simple, Elegant method for slot assignment changes
Contention Free Period
1
2
4
5
3
Assignment for Receiver of GTS slot 3
Contention Free Period
1
2
4
5
3
3
3
Contention Free Period
4
5
3
3
Contention Free Period
2
4
5
3
3
Assignment for Transmitter of GTS slot 3
Contention Free Period
1
2
4
5
3
3
Contention Free Period
1
2
4
5
3
3
n
n+1
n+3
Contention Free Period
1
2
4
5
3
3
Contention Free Period
1
2
4
5
3
3
n+2

## Slide 13: Pseudo-Static GTS Slot Summary
Pseudo-Static GTS slot changes are made with acknowledged directed Channel Time Grant frames from the PNC to the transmitter and receiver of the GTS slot.
Receiver slot moved and expanded before the transmitter slot change in order to avoid .
One slot moved at a time in order to eliminate the possibility of collisions.
Eliminates to need for a duration field to support low power devices that miss a beacon.

## Slide 14: Changes to the baseline to support Static GTS Slots
Channel Time Requests: Stations must have a way to distinguish between requests for completely static GTS slots, pseudo-static GTS slots or dynamic GTS slots.

## Slide 15: Unassigned GTS Slots
Unassigned GTS slots can be useful for allocating channel time for use by an adjacent piconet using the same channel or by a “daughter piconet.”
Unassigned GTS slots require static GTS slot assignments in order to be used by another piconet.

## Slide 16: How is an “unassigned” GTS slot requested?
A station wishing to request an unassigned GTS slot can send a channel time request with its own assigned address as both the source and destination for the slot.
The owner of the slot would be then be free to establish an adjacent piconet or a daughter pidonet using its slot.