## Slide 1: Bluetooth SIG Coexistence Working Group
Tod Sizer
Chair, Coexistence Working Group
Bluetooth Special Interest Group
Bell Laboratories

## Slide 2: Bluetooth SIG Coexistence Working Group Liason Update
Survey and Testing Finishing
Multiple Interferers
Adaptive Frequency Hopping
Specification Improvements

## Slide 3: Survey and Testing Finishing
Working Group has been performing a survey of Bluetooth Interferers
  Bluetooth
  802.11b
  HomeRF
  Wide Band Frequency Hoppers
  Microwave Ovens
  RFID Devices
  Cordless Phones
Live quantitative testing has been performed.
Simulation tools have been written and employed for studying several of the interferers in depth.
Results from the simulations and testing are being documented presently.

## Slide 4: Multiple Interferers
Starting closer study on the effect of Multiple Interferers on Bluetooth
Traffic models will have a dramatic effect on the magnitude/validity of the results.
Suggestions on likely scenarios of operations we should consider would be welcomed.

## Slide 5: Adaptive Hopping to Avoid Interference
When no interference is detected, hop over the entire frequency band.
When interference is detected at a level which will cause packet errors to Bluetooth, actively avoid these frequency hop locations.
This technique is currently legal for Class 3 Bluetooth units.
The use of intelligence to avoid interference is legal at all powers, however, the required number of hop locations must be maintained.
2.4 GHz ISM Band
Static Interferer
Bluetooth 1.0
Adaptive Hopping

## Slide 6: Adaptive Frequency Hopping
FCC has issued an NPRM which would allow Adaptive Frequency Hopping (among other changes in the band)
We feel that AFH shows the greatest promise in improving coexistence issues with frequency-static devices.
Your company’s support with the FCC on this issue would be appreciated.

## Slide 7: Specification Improvements
The next working group task will be to move to specification improvements to improve coexistence.
  Adaptive frequency hopping algorithms and implementation
  Power control algorithms and implementation.
  ...... (tbd improvements)

## Slide 8: Coordination
Chair of 802.15.2 and Chair of Bluetooth Coexistence Working Group are members of each others’ group.
Managing concerns which have been raised from each of the groups.
Look forward to continued cooperation, particularly in the areas of Adaptive Frequency Hopping and MAC layer simulations.