## Slide 1
NOTE: Update all red fields replacing with your information; they are required. This is a manual update in appropriate
fields. All Blue fields are informational and are to be deleted. Black stays. After updating delete this box/paragraph.
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Low-Band Phy Agere / Honeywell]
Date Submitted: [July 2001 ]
Source: [Carl R. Stevenson / Pat Gonia] Company: [Agere Systems / Honeywell]
Address [555 Union Boulevard, Room 22W214EQ, Allentown, PA 18109]
Voice:[(610) 712-8514], FAX: [(610) 712-4508], E-Mail:[carlstevenson@agere.com, gonia_patrick@htc.honeywell.com]
Re: [revision of IEEE P802.15-01/227TG4r1 after TG4 decision on baseline phy at 2.4GHz DSSS.]
Abstract: [Revision of Agere proposal now focussed on 868-928 band and integrating ZigBee’s narrow band draft proposal.]
Purpose: [to be considered as low-band PHY option]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Agere / Honeywell
Physical Layer Proposal
Overview
for Narrow Band operation in both
902-928 MHz and 868-870 MHz BANDS

## Slide 3: Overview:
A low-cost hardware platform to service both 915 and 868 MHz bands
Merger of Agere NB PHY proposal (IEEE P802.15-01/227TG4r1) and one of the proposed ZigBee PHY options
Compatibility with proposed baseline IEEE 802.15.4 MAC
Operating under FCC Part 15.249 and CEPT/ERC Rec 70-03
Proven, high performance all-digital modem possible
  conventional mod/demodulators could be used

## Slide 4: Frequency Band:
Adaptive channel selection to avoid interference
    Coordinator node “sniffs” band and selects channel(s)
    Slave nodes find coordinator by scanning for beacons
    Network moves to a clear channel in case of interference
Approximately 500 channels proposed for the 902-928 MHz band.
Channel spacing 50 KHz.
Center frequencies F= (915 + 0.05 K) MHz
with K= +/- 0,1……….250

## Slide 5: Frequency Band:
Up to 12 channels can be used in the 868.0 to 868.6 band (1% duty cycle.)
Up to 10 channels can be used in the 868.7 to 869.2 band (0.1% duty cycle.)
Up to 5 channels can be used in the 869.4 to 869.25 band (10% duty cycle)
Up to 6 channels can be used in the 869.7 to 870 band (100% duty cycle)
Duty cycle requirements must be observed.

## Slide 6: Transmitter Characteristics:
Power Output
Power output in the range of 5-10 dBm for 915MHz.
At 915, power level will be selected to control maximum field strength to 50 mv/m at 3 meters per FCC 15.249 regulations while using a very low-cost printed antenna.
More Tx power is allowed in 868 band.

## Slide 7: Transmitter Characteristics:
Modulation
Frequency shift modulation (FSK)
Spurious Emissions
Compliant to FCC 15.249 and ETSI regulations.

## Slide 8: Transmitter Characteristics:
Spectrum Mask
There are no specific rules on spectrum mask in FCC part 15.249 or ETSI.
Out-of-Band Spurious Emissions
Compliant to FCC 15.249 and ETSI regulations.

## Slide 9: Transmitter Characteristics:
Radio Frequency Tolerance
A 35ppm window is proposed ( 50 or 100ppm may be possible).
  A reasonable compromise to accommodate low-cost and acceptable performance

## Slide 10: Receiver Characteristics:
Receiver Reference Sensitivity Level
Better than -100 dBm for a BER of 10-4
Receiver Maximum Input Level
-20 dBm for a BER of 10-4

## Slide 11: Receiver Characteristics:
Spurious Emissions
Compliant to FCC 15.249 and ETSI regulations.
Receive/Transmit Turn-Round Time
Receive/transmit and transmit/receive
turn-round times should be less than 250μsec

## Slide 12: NB v.s. DSSS at 868MHz and 915MHz
More NB channels with dynamic channel selection
  Gives better interference avoidance
  More independent networks supported
NB: Can be lower power consumption than DSSS
Many NB solutions are currently available
  DSSS is not available now in the cost range
NB has better sensitivity
DSSS cost can approach NB but will not be lower
NB can be extremely simple

## Slide 13: Recommendation
Given the newly selected PHY at 2.4 GHz DSSS and the stated need for an alternate at 868-928:
This NB proposal should be more fully developed and optimized for the new (lower band) scoping
- To optimally fit both 915 and 868 requirements
- To eliminate any (now) unnecessary consideration of 2.4GHz
- To optimize for a distinguished market space from 2.4GHz PHY