## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: IEEE802.15.3: Overview of Power Save Proposal.
Date Submitted: 30 July, 2001
Source: Jay Bain Company: Time Domain
Address: 7057 Old Madison Pike
Voice: 256 922 9229 , FAX: 256 922 0853, E-Mail: jay.bain@timedomain.com
Re: [ ]
Abstract: This provides an overview of proposed incorporations in the draft standard relating to power management.
Purpose: To provide information and solicit comments on proposed power management
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15

## Slide 2: Overview of MAC Power Save
Provide the protocol structure that will allow a range of applications the greatest opportunity to save power.

## Slide 3: Changes from R1 to R2
Add shoulds and shalls to text on beacon length, QoS,
Add chart of EPS savings
Add table of comparison of approaches

## Slide 4: Possible operating scenarios
The mode with greatest power saving is OFF!
If off won’t do -- Associate with a network and then:
  Take advantage of characteristics of contention free period – reduce power in slots not assigned to a device. (RPS)
  Take advantage of higher layer inactivity - reduce power by skipping several beacons and superframes. (EPS)

## Slide 5: The enemies of power saving
Constant high throughput requirements.
Time to progress from startup to data movement.
Failure by higher layers to correctly structure requirements for service
Real characteristics of PHY and MAC
Poor environmental conditions resulting in lost packets and use of lower transmission rates

## Slide 6: RPS Operation
PNC may be an RPS device
Stay awake for
  Beacon
  CAP
  Assigned receive slot
  Assigned send slot with activity
Consider receive slot as empty after 25% of duration
Slot location
  Higher layers make realistic RPS QoS requirement known to device
  PNC required to make best effort to locate assigned slot nearest beacon
Contention
Access
Period
Beacon
Contention Free Period
Assigned
Slot
Assigned
Slot
Period of Reduced Power Opportunity
Notes: Slot location is a consideration. It would be an advantage for a RPS device to have a single cycle of activity rather than multiples. Real systems are expected to require time to return from a reduced power state.
A realistic RPS QoS requirement is key to obtaining desired results. Higher layers inform the RPS device of power restrictions and also of a matching scenario of information expected to be exchanged while in an RPS mode of operation.

## Slide 7: Rundown of EPS slides
Skipped superframes
Beacon content for EPS support
Data exchange with a EPS receiving device
Association timeout
Repeater service in EPS

## Slide 8: EPS Operation – skipped superframes
Beacon
Contention Free Period
Assigned
Slot
Beacon
Opportunity to reenter EPS
Beacon
PNC Generated Superframes
Wake to beacon –
no traffic
Indicated
Wake to beacon -
Traffic Indicated
Receive/ack data

## Slide 9: Beacon Content for Support of EPS
EPS information element (new)
  EPS devices each have a block (multiple sources require additional blocks)
  RPS PNC provides all piconet devices a block
Agent between sending and receiving devices (yellow) –
Current (1 bit) – indicates new data
Acked (1 bit) – indicates that an ack on previous data was received
More (1 bit) – indicates that at least one additional packet is queued behind the current packet.
Active (1 bit) – set by sending dev to indicate that it is actively updating the current, acked, and more and fields. If reset the three fields have no meaning and they are no longer valid.
Indicator gauge for association timeout (blue) –see later slide
Current
Seq. No.
Association
Timeout Gauge
Acked
Seq. No.
1 Octet
Active
Update
More
follows
Reserved
Sender controlled
PNC controlled
Destination Device ID
1 Octet

## Slide 10: Sender-PNC-EPS device diagram
Source
PNC
EPS Destination
Traffic Command
Traffic Ack
Beacon is
Second chance
Message in
Assigned slot
(short retry timer)
Receive Beacon
Receive traffic
Ack traffic
Missed Beacon
Missed Beacon
Missed traffic
Missed traffic
Traffic Command
Traffic Ack
Update Beacon
Wake
EPS
EPS
Update Beacon
Message
Repeat
Message
Repeat
B
B
B
B

## Slide 11: Association Timeout Operation
Based on aAssociationTimeoutPeriod parameter (7.3.5 in 0.4 draft). Originated by higher layer
Communicated to PNC by all devices
Related to all devices via gauge in beacon
device responsibility to re-initialized
Applies to active, RPS, and EPS devices
Allows PNC to be an RPS device and not listen to every slot
OK
Retry
Aggressive
retries
00
01
10
11
Gauge
operation
Disassociated

## Slide 12: Repeater Considerations
Use repeater in normal manner as piconet coverage enhancer.
Add use of repeater for EPS sender to EPS receiver operation.
EPS sender to active or RPS destination should not use repeater service (except as coverage enhancer)

## Slide 13: Where is the Beacon?
Consideration of Beacon change (new superframe length) –
  PNC should not change the superframe length if not truly beneficial to traffic requirements
  If it does change, the EPS device shall stay on to find the beacon – if once in a long while event, not a problem.
Clock drift calculation and leading of nominal beacon time is EPS device responsibility. (should)

## Slide 14: QoS Aspects for RPS/EPS
Higher layers shall determine the latency of the EPS device waking for a beacon
Higher layers should not ask for more than needed
Option is to divide into multiple streams for persistant low rate control and non-persistent QoS data

## Slide 15: MAC to PHY communications
Taking James Gilb suggestion
Table of power save options in PHY sent to MAC. Content is time to return to normal operation.
MAC chooses the appropriate table index for each power down command to PHY.
MAC sends power on command to return the PHY to normal mode.

## Slide 16: No Op Wake Cycle Amp Hr Chart
Notes: This chart is described as follows: It uses an active power value suggested by Mark Schrader, James Gilb's 1 mS wakeup time (using Mark’s active power value), and Ed Callaway's TG4 sleep power of 20 uA. There are 5 series depicted. The chart shows AHrs as y-axis (log) and wake-to-wake cycle time (seconds) as x-axis. Bounded between always active and always asleep are three plots.The one with the greatest power saving is a baseline of having no power up requirement (for all of these is the 65uS beacon length based on calculations including preamble, 16 slot CTA, and 22Mb/s). The next up is with 1 mS power up and depicts the approach proposed for EPS. The next up is the best I can figure for adding the necessary messaging to support Raju's protocol. There are three parts: message exchange indicating return to wake state; followed by the exchange requesting sleep state; and then the sleep state permit exchange. I fudged a bit and concluded that another 3 mS (a CAP of 1 mS, return of 1 mS, and another CAP of 1mS(second beacon of 65uS not in calculation)) would cover the exchanges that would take place over 2 or 3 superframes (I just lumped it into a return time of 4mS for the chart). A lot of this depends on the architectural divisions of implementations (would all three exchanges occur in a single CAP or would 2 or three be likely?).
If my analysis is correct and Excel didn't confound me, there is a substantial power consumption hit for the three exchanges of Raju's proposal.

## Slide 17: Tri-shake approach
Beacon
Opportunity to
reenter EPS
CAP
EPS Ret
Beacon
CFP
Opportunity to
reenter EPS
CAP
EPS Ret
Beacon
CFP
Opportunity to
reenter EPS
CAP
EPS Ret
CFP
Active State Indication
ACK at end of SIFS
Sleep State Request
ACK at end of SIFS
Sleep State Permit
ACK at end of SIFS
Assume 1 mS EPS Return required
Assume CAP of 1 mS
Notes: This diagram is for the case of a “no op” wake cycle.
There are three message exchanges as defined in doc 01/293r1 table 51
The first is sent by the EPS device after it has received it’s first beacon upon waking from sleep.
There is the expectation by the EPS dev that data might be queued so the EPS must be awake to receive it.
The second and third message exchange is to go back to sleep again.
Different implementations of the standard will result in fewer superframe requirements. The wake cycle Amp hour chart assumes two superframes (and CAPs) required.

## Slide 18: EPS approaches - Comparison
Emphasis on lowest power use for “no op” wake cycles.
Beacon provides
  Association timeout gauge
  Ack + indications
PNC does not responsible for ack/indications during active mode
Dev-to-dev and repeater service available
PNC not required to support repeater service for basic EPS
PNC provides repeater service for EPS-EPS devs (if PNC supports repeater service). Ceases when devs go active.