## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Unified MAC proposal for the 802.15.4 Low Rate WPAN Standard]
Date Submitted: [June 2001]
Source: [Phil Jamieson] Company: [Philips Semiconductors]
Address: [Cross Oak Lane, Redhill, Surrey, RH1 5HA, United Kingdom]
Voice:[+44 1293 815 265], FAX: [+44 1293 815 050], E-Mail:[phil.jamieson@philips.com]
Re: [ MAC layer proposal submission, in response of the Call for Proposals ]
Abstract: [This contribution is a highly flexible MAC proposal for a Low Rate WPAN intended to be compliant with the P802.15.4 PAR. It is intended to support both star and peer-to-peer communications for low data rate networks. It is designed to support ultra low power consumption for battery operated nodes at very low implementation cost. This document forms a unified MAC proposal with contributions from Agere, Invensys, Motorola and Philips Semiconductors.]
Purpose: [Unified MAC proposal]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Unified MAC proposal for the 802.15.4 Low Rate WPAN Standard
Phil Jamieson
Principal Engineer, Philips Semiconductors
Phone: +44 1293 815265
Email: phil.jamieson@philips.com

## Slide 3: Contents
Introduction
MAC Features
Topologies
System Considerations
Upper Layer Scenarios
Evaluation Matrix

## Slide 4: Introduction

## Slide 5: Target Markets
Low Data Rate Radio Devices

TV

VCR

DVD

CD

Remote

Mouse

Keyboard

Joystick

Gamepad

Security

HVAC

Lighting

Closures

PETs

Gameboys

Educational

Monitors

Diagnostics

Sensors
Industrial & Commercial
Consumer Electronics
Personal Healthcare

Monitors

Sensors

Automation

Control
Toys & Games
Home Automation
PC Peripherals

## Slide 6: TG4 Drivers
Extremely low cost
Ease of installation
Reliable data transfer
Short range operation
Reasonable battery life
Simple but flexible protocol

## Slide 7: MAC Features

## Slide 8: Key Features
Star & peer-peer topologies
  Supports: master/slave, point to any point, cluster tree, etc.
Access is p-persistent slotted CSMA-CA
Data rates of 28k & 250kbps but scalable
Optional use of network beacons
Optional time slots for low latency transfer
Super-frame is contention based
Support for 7+ co-located networks
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 9: Node Types
Distribution node
  Controls the network topology at that node
  Master/co-ordinator or mediation device
  Talks to other distribution and slave nodes
Slave node
  Cannot control the network
  Very simple implementation
  Talks only to a distribution node

## Slide 10: Addressing Modes
Star
  Network identifier (16) + short allocated address (8)
  Network identifier (16) + unique (IEEE) address (64)
  Cluster tree address (24) + short allocated address (8)
  Cluster tree address (24) + unique (IEEE) address (64)
Peer-peer
  2x Unique (IEEE) address (64)
  2x (Cluster tree address (24) + short allocated address (8))
  2x (Cluster tree address (24) + unique (IEEE) address (64))
All nodes have a 64-bit IEEE but this can be withheld

## Slide 11: Composite Addressing
IEEE address:
  Vendor identifier (24 bits)
  Device identifier (40 bits)
Cluster tree address:
  Network identifier (12 bits)
  Collapse value (4 bits)
  Cluster identifier (8 bits)

## Slide 12: Traffic Types
Periodic data
  Application defined rate
Intermittent data
  Application/external stimulus defined rate
Repetitive low latency data
  Allocation of time slots

## Slide 13: Data Packet Structure
PRE
SFD
LEN
MFL
CRC
Link Layer PDU
ADDRESSING
Preamble sequence
SFD, one for each packet type
Length for decoding simplicity
Flags specify addressing mode
Addresses according to specified mode
CRC-8/16, depending on the LPDU size

## Slide 14: Network Beacon
Optional for the network
Period determined by collapse value (= 15 ms * 2CV)
Identifies the network (during connection)
Describes the super frame structure
Provides data presence indications
Only present during network activity

## Slide 15
t
15 ms
Collapse 0
30 ms
Collapse 1
60 ms
Collapse 2
.
.
.
Collapse 15
8.192 minutes
Collapse Value Concept
In collapse n+1 mode, a beacon is sent half as often as in collapse n mode
Assigned slots continue at 15 ms period
Higher collapse values offer alternatives for high latency devices and low duty cycle devices (collapse 15 alternatively may be defined as “no beacon”)

## Slide 16: Time Slots
Optional for the network
Requested by individual nodes
Allocated by the network co-ordinator
Variable size for flexibility
Supports low latency devices
  For example, joysticks, mouse and keyboard

## Slide 17: Optional Super Frame Structure
15ms
Network
beacon
Contention
period
Beacon
extension
period
Slot 3
Slot 2
Slot 1
Allocated
slot
Transmitted by distribution nodes. Contains network information,
super frame structure and notification of pending node messages.
Space reserved for beacon growth due to pending node messages
Access by any node using CSMA-CA
Reserved for nodes requiring guaranteed bandwidth.

## Slide 18: Power Management
Protocol designed for low power devices
Slave nodes initiate all transfers (where used)
Sleep periods are application defined
Nodes wake on
  external interrupt from some user stimulus
  application defined interval
  health check cycle

## Slide 19: Use of Channels
Dependent on choice of PHY layer
Application defined classes
PHY defined (low data rates/high data rate)
Frequency agility for interference robustness
High density transfer between two nodes

## Slide 20: Exported Data Primitives
DATA_REQ(
SourceAddress,
DestinationAddress,
PDULength,
PDU,
Options
)
SourceAddress DestinationAddress Implied Topology
NULL NULL Other
NULL Defined Star
Defined NULL Star
Defined Defined Peer-Peer
DATA_IND(
SourceAddress,
DestinationAddress,
PDULength,
PDU,
Options
)

## Slide 21: Topologies

## Slide 22: Star Topology
Distribution node
Slave node
Communications flow
Master/slave

## Slide 23: Peer-Peer Topology
Distribution node
Communications flow
Point to any point
Cluster tree

## Slide 24: Combined Topology
Distribution node
Slave node
Communications flow
Clustered stars - for example,
cluster nodes exist between rooms
of a hotel and each room has a
star network for control.

## Slide 25: “Connect & Go” Topology
Distribution node
Connecting
Walk by - for example, a retail
shop advertises offers. As users
walk by the nodes connect, exchange
data and leave.
Watch & Learn - for example, a
node can connect to a picture in a
gallery and exchange information.
The user will then leave.
Communications flow

## Slide 26: System Considerations

## Slide 27
IEEE 802.15.4 MAC
NWK A
IEEE 802.15.4 LLC
IEEE 802.2
LLC, Type I
IEEE 802.15.4
915/2400 MHz
PHY
IEEE 802.15.4
868/915 MHz
PHY
NWK B
NWK C
Application Convergence Layer (ACL)
Maintained by
IEEE 802.15.4
Maintained by
ZigBee
Working Group
Low Rate Stack Architecture
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 28: Stack Components
Multiple IEEE 802.15.4 PHY layers
  868/915 MHz and 915/2400 MHz
IEEE 802.15.4 MAC
Link layers
  IEEE 802.15.4, IEEE 802.2 (Type I)
Network layers implement topology commands
  Star (PURL), Cluster Tree, etc.
Application convergence layer
  Application can interface to all NWK layers
  Common application functions

## Slide 29: Upper Layer Functionality
Transfer reliability (LLC)
Packet segmentation/sequencing (LLC)
Topology management (NWK)
Node connection procedures (NWK)
Security & authentication (ACL)
Application convergence protocol (ACL)
Device/service discovery (ACL)

## Slide 30: Total System Requirements
8-bit C, e.g. 80c51
Distribution node protocol stack <32k - <64k
  Depends on upper layer configurations
Slave node stack ~4k
Distribution nodes require extra RAM
  Device database
  Routing table
  Message storage for subsequent transfer

## Slide 31: Upper Layer Scenarios

## Slide 32: Cluster Tree: Mediation
Source
Node
MD
Destination
Node
RTS
RTS Reply
Query
Query Response
CTS
DATA
ACK
Timing
adjustment
Rx slot
Tx slot
Star
comms.
Peer-peer
comms.

## Slide 33: Master/Slave: Network Connection
CONNECT
CONNECT
ACK
CONNECT-CONF
ACK
BEACON
PERMIT-CONNECTION
CONNECT-CONF
NEW-DEVICE
Slave
Master
Rx
Tx

## Slide 34: Master/Slave: Pairing Links
Slaves do not store network information
  “phone book” requires storage space
  must be continuously updated
Slaves are able to request a connection
  intuitive user operation: 1st slave, 2nd slave
  master creates and manages link
Routing performed at the master device
Links can be broken in the same way

## Slide 35: Connect & Go
ID-INFO
DATA-PDU
ID-INFO
Service
Requester
Service
Provider
DATA-PDU
ID-INFO
Tx
Rx
User
activation
Data
transfer

## Slide 36: Evaluation Matrix

## Slide 37: MAC Evaluation Matrix

## Slide 38: MAC Evaluation Matrix, cont….

## Slide 39: MAC Evaluation Matrix, cont….