## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: IEEE802.15.3: Proposed changes to the TG3 MAC amendments listed in 221r0.
Date Submitted: 4th June, 2001
Source: Dr. Rajugopal Gubbi Company: Broadcom, corp
Address: 400, E-Caribbean Drive, Sunnyvale, CA 95084
Voice: +1.408-543-3470, FAX: +1.408-543-3470, E-Mail: rgubbi@Broadcom.com
Re: [ ]
Abstract: This presents concerns regarding the MAC amendments in 01221r0. And proposes changes to the amendments listed in 221r0
Purpose: To provide an improvement to the current version of the 802.15.3 MAC
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that these viewgraphs becomes the property of IEEE and may be made publicly available by P802.15, however, the substance of the subject matter contained in the viewgraphs remains the property of Broadcom, Corp

## Slide 2: Disclaimer
This document is submitted as author’s individual contribution and NOT submitted as sub-editor’s contribution

## Slide 3: Overview
Changes to Frame types and formats
Addition of Piggybacked ACK
Removal of Duration field in MAC header
Addition of Repeater service by member DEVs
Removal of Reserved field in Association frame
Removal of max-dur of time slot in CTA element
Addition of Max GTS

## Slide 4: Frame formats
Instead of adding clarification that was lacking, a totally new frame format is employed.
The concept of commands was accepted in both Tampa and HH
“No coherent policy” cited in doc#250 is not a good enough reason to simply change the formats. We should have added the clarifying text.
The idea behind the command frame was to allow devices to transact multiple command information with overhead of one frame on the channel

## Slide 5: Frame format
In the command frame based format, all the information that HAS to be sent as stand-alone takes the form of a unique frame while the rest of the “control” information can be bunched into one command frame, and hence resulting in low overhead.
Example: a DEV sending two Repeater requests and a stream management request and two retx requests to the coordinator. Instead of combining all these into one frame and sending in one shot, under the new frame formats, the device is incurring the overhead of four SIFS+preamble+PLCP_Header+MAC_Header+HEC+FCS overhead which is very expensive to be incurring on just the non-data (control) information

## Slide 6: Frame format
As the control information increase, the command format results in nearly flat, low overhead while the new frame format results in linearly increasing overhead.
In implementations, all the command frame must be processed by a command analyzer entity (CAE) which is same as information-element processor. CAE must feed all the “management” commands required by SME to SME and the rest to be processed within MAC.
New format needs two more bits in FC field. The bits in FC field are precious and hence we must use them diligently. The old format uses only 4 bits in FC field but provides plenty of room for future extension!!

## Slide 7: Proposal for frame types and formats
Introduce CAE in architectural description in clause-5
To enable processing of management v/s control commands at different entities and easy sorting while keeping the advantage of command frame format, the commands can be grouped into management and control commands.
Bit-7 of command type can be used to distinguish between the management and control commands
If it helps implementation, it must be mandated that DEVs place all control commands first in a command frame followed by the management frames, although I am not sure whether this restriction is required.

## Slide 8: Piggyback ACK Policy
This is a useful modification to have. But there must be a way for the owner of the time-slot to know exactly how much channel time the responding device is going to take.
Without this the implementations are not going to support as the responding station could choose the lowest rate and longest frame to transmit and hence taking the all of the or most of the remaining time slot
This problem gets worse when the responding has not received the Beacon correctly and hence do not know the limit of current time slot

## Slide 9: Removal of Duration field
Duration field in MAC header helps in DEVs to know the end of time slot when they did not receive the Beacon correctly or when they wakeup from deep sleep.
If the DEVs know the end of current Time slot, they can go snooze till the end, if the first frame in that time slot is not for them and wake up to rx again at the beginning of the next time slot.
The above helps minimize the adverse effect on power saving when a DEV did not rx the Beacon correctly. Removal of Duration field forces the DEVs to be awake for the entire Beacon interval.

## Slide 10: Repeater service by member DEVs
Repeater service by member DEVs is more complicated than it seems as it has a number of corner cases that need complicated support from the MAC protocol
Assumption of PNC being able to see all the DEVs in the piconet at all times is a valid one. How does the requesting DEV know that the provider is able to see its dest-DEV currently. This calls for specification for a DEV to either conduct a trail and error request/rejectORaccept sequence or somehow obtain a list of DEVs that are currently in the range of a potential repeater. In practice implementations would simply choose to request PNC as it is a sure hit.

## Slide 11: Repeater service by member DEVs
If the current repeater does not see the dest-DEV anymore the requestor has to go through another trial to re-establish the link and hence potentially interrupting the flow of the stream
This also complicates the channel time allocation
The repeating-DEV must be able to request channel time for repeated traffic which is not currently supported. At PNC this is very simple as this is a local process. But with non-PNC repeater, the PNC must be aware that the allocation is for a stream that does not originate at the repeater and hence complicates the CTA req/grant and any traffic monitor process at PNC
Hence I recommend that repeater service be provided only by PNC and not by member services

## Slide 12: Reserved field in ASSOC frame
“Reserved” field is present for word alignment
All frame format, information elements etc are carefully adjusted for word alignment for ease of implementation
I strongly recommend retaining the word alignment in these formats as the cost of byte aligned implementations are far exceeding an additional byte in a frame
This calls for two more amendments: (a) possibility of padding a byte in non-word aligned data frames and the indication of the same in MAC header (b) making sure all the SEC related fields and challenge text etc. are also word aligned.

## Slide 13: Eliminating Slot-Dur from CTA
In any Beacon interval there may be one or more devices in the piconet that receive the beacon in error
If a device did not receive the CTA information, it can not access the channel during CFP
The CTA-Grant command gives the flexibility to the PNC to announce the CTA information during the super frame in addition to the broadcast in Beacon and hence increasing the robustness in communicating that information. This also provides flexibility to PNC to help preserve Qos at a DEV that is experiencing more than usual channel errors.

## Slide 14: Eliminating Slot-Dur from CTA
All times in CTA are relative to Beacon tx-start time
If a DEV receives Beacon in error but receives a directed CTA-Grant command from PNC, the DEV has no way of using the CTA unless CTA contains both the start-time and duration of the time slot allocated.
Hence I recommend retaining the slot-dur field along with the slot-start field in the CTA element

## Slide 15: Max GTS field
This is another useful modification to have.
One suggestion is that, this one may be better of as an information element than as a field in capability field
In any case the PNC has to probe the DEV and obtain supported rate, sec, power save parameters, etc. the same probe can be made to provide the Max-GTS element
This information is needed during the channel time allocation and not necessarily during the association

## Slide 16: Max GTS field
Adding another information element has two advantages. Provides the Max GTS field as many bits as it needs and leaves enough bits in capability field for future extensions
Hence I recommend Max-GTS to be an information element rather than a field within Capability information

## Slide 17: An eye on the time
As it is we do not have enough time to fill the known holes in the draft and make it to LB in the next plenary meeting.
It is lot of work to make the changes, make sure they don’t break anything else or become inefficient and reverse them when they do.
Ask for clarification by email or in teleconference or through Al’s list of issues.
Hence I suggest we work on the known holes in the draft and inconsistencies, provide clarification to the existing mechanisms to get the draft to LB.