## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: IEEE802.15.3: A proposal to add geographical coverage based criteria to Coordinator selection as well as to clarify the usage of “Des-mode” and Coordinator handover.
Date Submitted: July 03, 2001
Source: Shig Sugaya, Kaz Takamura, Masa Akahane Company: Sony Corporation
Address: 6-7-35 Kitashinagawa Shinagawa-ku, Tokyo Japan 141-0001
Voice: +81.3.5782.5067, FAX: +81.3.5782.6880
E-Mail: sugaya@wcs.sony.co.jp, takamura@wcs.sony.co.jp, akahane@wcs.sony.co.jp
Re: [ P802.15.3/D0.4, P802.15-01/259r0]
Abstract: This proposal presents modified comparison order of fields and Coordinator selection frame body that provide an accessible Device count for geographical coverage based Coordinator selection.
Purpose: To provide an improvement to the current version of the 802.15.3 MAC
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that these viewgraphs becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Outline
“Des-mode” concept and utilization
Geographical coverage based Coordinator selection scheme

## Slide 3: “Des-mode”
To set “Des-mode” means to entitle the highest priority to be a Coordinator
  This priority is effective when Coordinator selection process is started for:
    Piconet initialization YES
    Handover ???

## Slide 4: Concerns on Coordinator Handover
Expected handover opportunities
  At the time user sets “Des-mode”
  When Coordinator disappears
Problems on handover
  No guarantee to keep the same coverage before handover
  Need extra computation and status management
    Select alternate candidates every time the topology of piconet is changed
      When a Device joins/leaves the piconet
  Coordinator handover makes life complicated

## Slide 5: Basic Concept on Piconet
Simplicity is the goal of Wireless PAN
  Piconet is defined by the coverage of Coordinator
  When Coordinator leaves, the piconet should be “adjourn”
    If Coordinator need to be changed,
      1) Set “Des-mode” to the new Device
      2) Reset the piconet
    No need to define “handover” anymore
  We propose
  “Des-mode” is effective only when initialization

## Slide 6: Geographical coverage based selection
Issue
  A Device located at the fringe area of the piconet may become the Coordinator if the Device has the highest capability
Demand
  Geographical coverage should also be one of the selection criteria
Decision Criteria
  A Device which has the largest number of accessible Devices becomes Coordinator
Good Selection
Bad Selection
Ideal Piconet
Unexpected Piconet
Devices out of reach
Ideal Coordinator
Inappropriate Coordinator

## Slide 7: Inquiry Command
Inquiry Command consists of Inquiry Request and Inquiry Response
Alternate Coordinators send Inquiry Request to all Devices
All Devices that could receive Inquiry Request send Inquiry Response to the Alternate Coordinator
Alternate Coordinator sums up the total number of Inquiry Responses
Inquiry Res
Inquiry Res
Inquiry Request
Inquiry Res
Inquiry Res
Accessible Device Count = 4
CS Frame Broadcast
Device A
Device B
Device D
Device E
Device C
Alternate
Coordinator

## Slide 8: Recommended Comparison Order
Order | Information | Notes
1 | Designated mode bit in capability field | Coordinator designation is preferred
2 | SEC bit | SEC=1 is preferred
3 | Battery/AC Power | AC Power preferred
4 | PS bit | PS=1 is preferred
5 | Accessible Device Count | High value is preferred
6 | MAX GTS Slots | High value is preferred
7 | Repeater Memory | High value is preferred
8 | Device ID | High value is preferred
Draft 0.4, Table 59 Comparison order of fields in AC-announcement command
Based on 01/259r0

## Slide 9: Inquiry Frame
Type Value | Frame type description
0000 | Beacon
0001 | Coordinator Selection (CS)
0010 | Association request
0011 | Association response
0100 | Disassociation request
0101 | Immediate Acknowledgement (ACK)
0110 | Command
0111 | Stream-Data
1000 | Inquiry
1001-1111 | Reserved
Octets | Field
1 | Action Type -- 0:Alternate coordinator announcement -- 1:Alternate coordinator pull out -- 2:New coordinator announcement -- 3:Inquiry -- 4-255:Reserved
1 | Reserved
2 | Capability
1 | Total External Connections
1 | Active External Connections
1 | Total System Memory
1 | Avail System Memory
1 | Maximum PHY Transmit Power
1 | Max PHY Rate
6 | Device ID
2 | CS Timeout
Figure 6 -- Coordinator selection frame body
Table 55 -- Valid Frame type values
Based on P802.15.3/D0.4
or

## Slide 10: Coordinator Selection Frame Body
Octets | Field
1 | Action Type
1 | Reserved
2 | Capability
1 | Accessible Device Count
1 | Total External Connections
1 | Active External Connections
1 | Total System Memory
1 | Avail System Memory
1 | Maximum PHY Transmit Power
1 | Max PHY Rate
6 | Device ID
2 | CS Timeout
Figure 6 -- Coordinator selection frame body

## Slide 11: Coordinator Selection Process
Geographical coverage based selection starts if the higher comparison criteria could not reach the decision
Every Alternate Coordinator sends Inquiry Request and counts the total number of Inquiry Responses and stores it in Coordinator Selection Frame respectively
Alternate Coordinators exchange Coordinator Selection Frame and pull out if self-number is smaller
Parameter
Comparison
(Order 1-4)
The First AC
Broadcasts
CS-frame
Other AC
Broadcasting CS-frame
Inquiry
Process
Winning AC
Broadcasts
CS-frame
Other AC
Broadcasting
CS-frame
Parameter
Comparison
(Order 5-8)
Winning AC
Broadcasts
Coordinator
Announcement
First Beacon
Transmission
Time
Coordinator selection process outline

## Slide 12: Required Modification
Add “Accessible Devices Count” to the comparison order of fields
Add “Accessible Devices Count Field” to Coordinator selection frame body
Define “Inquiry Command”

## Slide 13: Conclusions
When Coordinator need to be changed, reset the piconet and start Coordinator selection process
  “Des-mode” becomes enable when piconet is initialized
Geographical coverage is added in the criteria of Coordinator selection mechanism
  The number of accessible Devices is counted by Alternate Coordinators in order to decide the best location among them

## Slide 14: By the way…
When is the opportunities of Coordinator selection process?
  What happens if a designated Coordinator just starts sending Beacon after a carrier sense without Coordinator selection process?
  Do we need to mandate Coordinator selection process?
    Nice to have if the most efficient Device is automatically selected using this process
    Can you tell any other specific scene to use Coordinator selection process?