## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: IEEE802.15.3: A proposal to acquire the topology and efficient management of the network by having “Heart Beat” mechanism.
Date Submitted: July 09, 2001
Source: Shig Sugaya, Kaz Takamura, Masa Akahane Company: Sony Corporation
Address: 6-7-35 Kitashinagawa Shinagawa-ku, Tokyo Japan 141-0001
Voice: +81.3.5782.5067, FAX: +81.3.5782.6880
E-Mail: sugaya@wcs.sony.co.jp, takamura@wcs.sony.co.jp, akahane@wcs.sony.co.jp
Re: [ P802.15.3/D0.4 ]
Abstract: This proposal presents added signal called “Heart Beat” so that provide an efficient node management.
Purpose: To provide an improvement to the current version of the 802.15.3 MAC
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that these viewgraphs becomes the property of IEEE and may be made publicly available by P802.15, however, the substance of the subject matter contained in the viewgraphs remains the property of Sony Corporation.

## Slide 2: Heart Beat Mechanism for Monitoring
Current issues and motivation
  Coordinator cannot recognize such a situation as a Station is shut down all of sudden or disappear from the coverage of the PSS
  Coordinator need to know all the Stations that are alive within the coverage as well as to reduce redundant management
Solution
  Implement “Heart Beat” mechanism to update the network
    Each Station periodically sends a command to Coordinator
    Coordinator discards the entry of the Station if Coordinator does not receive a command tbd times

## Slide 3: Command and Mechanism
Connection Update Command
  A Command sent from a Station to Coordinator so that a Station reports the existence to Coordinator
  Each Station should Periodically send this command to Coordinator
    eg) Every second that does not make small impact for the power consumption
  Regular message exchanges also work as a “Heart Beat” even if it is not received by Coordinator
    Figure 1 -- Connection Update Command
Command Type
Octets : 2
1
Link Connection
Length
(n+1)
･･
2
Received Other Link Connection - 1
1
1
Received Other Link Connection - n
･･

## Slide 4: Disassociation Mechanism
Coordinator disassociates a Station that has not sent the command for more than N x Heart_Beat_Period
  Moratorium is required for mis-disassociation
    Figure 2 -- Coordinator Connection Update Sequence
Station #1
Station #2
Station #3
Heart_Beat_Period
Disassociation
Connection Update Command
Connection Update Command
Other Commands
Time
> N x Heart_Beat_Period