## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [TG3-PHY-Changes-from-Orlando]
Date Submitted: [9 July 2001]
Source: [James P. K. Gilb] Company [Mobilian]
Address [11031 Via Frontera, Suite C, San Diego, CA 92127]
Voice:[1-858-217-2201], FAX: [1-858-217-2301], E-Mail:[gilb@ieee.org]
Re: []
Abstract: [This document lists the proposed changes to the 2.4 GHz PHY for the draft standard. The changes are the consensus of the PHY subcommittee.]
Purpose: [To present the changes to the PHY agreed to by the PHY subcommittee for approval by TG3.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: CCA Definition
11.6.5 Receiver CCA performance
A compliant receiver provides CCA capability by performing energy detection in the received signal bandwidth. The receiver CCA shall report a busy medium upon detecting energy above the energy detect (ED) threshold in a 16 symbol window in the current receive channel, 11.2.3. The 16 symbol interval corresponds to the length of a single CAZAC sequence, 11.4.6, and is approximately 1.45 us based on the 11 Msymbol/s symbol rate. The ED threshold shall be equal to -7 dBm integrated over a 16 symbol interval.

## Slide 3: SIFS and Slot
11.2.6.1 Interframe spacing
A conformant implementation shall support the interframe spacing parameters given in Table 101.
Table 101 —Interframe spacing parameters
802.15.3 MAC parameter | Corresponding PHY parameter
SIFS | aRXTXTurnaround
Slot | aCCADetectTime

## Slide 4: RSSI
11.6.6 Receiver RSSI
RSSI is defined as the power relative to the maximum receiver input power level, 11.6.3, in 8 steps of 8 dB with +/-4 dB accuracy for each step. The range covered shall be a minimum of 40 dB. The steps shall be monotonic. This number shall be reported to the SME and MLME via the PHY-RXSTART.indication, 6.8.4.13.

## Slide 5: LQI – Link Quality Indication
11.6.7 Link quality indication
The link quality indication (LQI)shall be reported for the TCM coded QAM modes using an SNR estimation. The SNR shall be measured at the decision point in the receiver. The receiver shall report the SNR as a 5 bit number that covers a range of 12 dB to 27.5 dB of SNR. The value x00000 shall correspond to less than or equal to 12 dB SNR and 0x11111 shall correspond to more than or equal to 27.5 dB SNR with equal steps in between. This number shall be reported to the SME and MLME via the PHY-RXSTART.indication, 6.8.4.13.

## Slide 6: Header Coding
Goal is to have probability of header error << probability of frame error
11.4.2 Header modulation
The PHY service field, MAC header and HCS shall be modulated using QPSK modulation. Since the header is usually much shorter than the frame body, it is more probable to correctly receive the header than the frame body, even without FEC for the header. This is true as well for a BPSK frame body that is longer than ?? bytes.

## Slide 7: QPSK vs. OQPSK
Criteria | QPSK | OQPSK
PA Backoff | Worse | Better (0.5 dB)
Filter linearity | More stringent | Less stringent
Band limiting in receiver | Less tolerant | More tolerant
Progression to QAM | Easy | More difficult, requires additional gates.

## Slide 8: QPSK vs. OQPSK (cont.)
Criteria | QPSK | OQPSK
Supports CAZAC | Yes | No, require different synchronization
Equalization | OK | Offset of I and Q makes it very different from QAM and therefore more complex
Ease of implementation | Same for digital implementation | Same for digital implementation, has some advantage in non-coherent implementations.
PHY committee recommends changing to QPSK

## Slide 9: Symbol Clock Synchronization
11.5.6 Clock synchronization
The transmit center frequency and the symbol rate shall be derived from the same reference oscillator.

## Slide 10: Jamming Margin
Desired signal to 5 dB above reference sensitivity
Data Rate (Mbit/s)
Minimum sensitivity
Adjacent channel rejection (dB)
Alternate channel rejection (dB)
22
-75 dBm
7 dB
23 dB
33
-74 dBm
6 dB
22 dB
44
-71 dBm
3 dB
19 dB
55
-68 dBm
0 dB
16 dB
11
-78 dBm
10 dB
26 dB
Changed or new numbers

## Slide 11: Data Whitener Seed Initialization
The initialization vector is determined from the seed identifier contained in the PHY header of the received packet.
The 15 bit seed value chosen shall correspond to the seed identifier,11.4.4,as shown in Table 105. The seed identifier value is set to when the PHY is initialized and is incremented in a 2-bit rollover counter for each packet that is sent by the PHY. The value of the seed identifier that is used for the packet is sent in the PHY header, 11.4.4.
Seed identifier | Seed value
00 | 0011 1111 1111 111
01 | 0111 1111 1111 111
10 | 1011 1111 1111 111
11 | 1111 1111 1111 111

## Slide 12: EVM modifications
Relaxed 64-QAM to 2.6% EVM for cost considerations
11.5.2 EVM Calculated Values
A compliant transmitter shall have EVM values of less than those given in Table 11 for all of the modulation levels supported by the PHY when measured for 1000 symbols. The error vector measurement shall be made on baseband I and Q data after recovery through a reference receiver system. The reference receiver shall perform carrier lock,symbol timing recovery and amplitude adjustment while making the measurements.
Changed text

## Slide 13: PLME/PHY PIB
Suggestions, need to work with System committee
Modify PHY PIB for RSSI and LQI definitions
Add TX max power and TX power step size from TPC
Change PHY-CCA,
  PHY-CCA.start, PHY-CCA.end., P.request and .confirm commands
Change PHY-RXNAP
  PHY-RXEND.request and PHY-RXEND.confirm
Add PHY-PWRMGT.request, PHY-PWRMGT.confirm
  1 byte parameter to 1 of available levels.

## Slide 14: PHY Header/Service Field
PHY header is 2 bytes with three fields
  2 bit seed indicator, b0-b1 (see scrambler for mapping)
  3 bit rate indicator, b2-b4 (mapping below)
  11 bit frame length in bytes
    b5 is MSB, b15 is LSB
    e.g. 4 byte FCS only frame is 0x0000 0000 100
Modulation | Data rate | b2-b4
BPSK | 11 Mb/s | 000
QPSK | 22 Mb/s | 001
16-QAM, TCM | 33 Mb/s | 010
32-QAM, TCM | 44 Mb/s | 011
64-QAM, TCM | 55 Mb/s | 100

## Slide 15: Possible lower rate mode
Proposal
  11 Mbaud uncoded BPSK for 11 Mb/s
  PHY preamble, PHY header and MAC header stay the same.
The goal is
  larger range
  fall back mode for better link quality

## Slide 16: 15.247+NPRM vs. 15.249
Criteria | 15.247+NPRM | 15.249
Availability | Real Soon NowTM | now
Minimum channel separation (with 15 MHz BW) | 3 MHz | 1 MHz
Transmit power | 125 mW (+21 dBm, ~ 2 W DC power) | ~ +8 dBm
World wide TX power limit | +10 dBm | ~ +8 dBm
Implementation ease/cost | Easier TX filter, 8 MHz 30 dB point, 16 MHz 40 dBm, less gates, cheaper | baseline
Adjacent channel interference | Better, depending on PSD | baseline
Risk if NPRM not approved | Need to change channel programming only | baseline
Recommend 15.247 with NPRM

## Slide 17: Transmit power control
11.5.9 Transmit power
...
A compliant transmitter that is capable of transmitting more than 4 dBm shall be capable of reducing its power to less than 4 dBm in monotonic steps no smaller than 3 dB and no larger than 5 dB. The steps shall form a monotonically decreasing sequence of transmit power levels. A compliant device shall have its maximum transmit power level and nominal power level step size indicated in its PHY PIB.

## Slide 18: Base rate and differential encoding
Base rate
  11.3.1 Base rate
  The base rate of the 802.15.3 2.4 GHz PHY shall be the 22 Mb/s,uncoded QPSK mode.
Differential encoding
  Draft d0.4 had differential encoding
  Provides marginal advantage for non-coherent receivers
  Has small SNR impact on coherent designs
  Recommend keeping differential for QPSK, add for BPSK but not for TCM QAM mode

## Slide 19: Maximum Receiver Input Level
11.6.3 Receiver maximum input level
The receiver maximum input level is the maximum power level of the incoming signal,in dBm,present at the input of the receiver for which the error rate criterion in 11.6.1 is met. A compliant receiver shall have a receiver maximum input level of at least -10 dBm for un-coded QPSK modulation. The receiver maximum input level is not defined for the other modulation formats.