## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: IEEE802.15.3: Overview of Power Save Proposal.
Date Submitted: 19 June, 2001
Source: Jay Bain Company: Time Domain
Address: 7057 Old Madison Pike
Voice: 256 922 9229 , FAX: 256 922 0853, E-Mail: jay.bain@timedomain.com
Re: [ ]
Abstract: This provides an overview of proposed incorporations in the draft standard relating to power management.
Purpose: To provide information and solicit comments on proposed power management
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15

## Slide 2: Overview of MAC Power Save

## Slide 3: Outline
RPS (reduced power save)
EPS (extended power save)
Startup considerations
Wakeup – remote as in new 802.3 capability. TBD but is this capability implied already?

## Slide 4: RPS
Recommend that RPS devices stay awake for all beacons, all CAPs, and all slots where it is a destination. Sending slots only when information to send.
Recommend to require PNC to locate RPS’s slot near CAP so a device can stay awake rather than have two cycles of powering up per superframe.
Consideration of slot assignments that are set artificially long with no expectation that presented information will use any part of them. This gets into duration of data. Can a RPS DEV go away if no data in slot ¼ of the way through slot?
Consideration of QoS mechanism to use one slot per superframe if stream request allows (latency)
  Recommended text is that associated equipment desiring RPS not over state request QoS.
Consideration – Can the PNC be an RPS device? If it has the responsibility to look at all slots for “keep alive” then can’t do RPS.

## Slide 5: EPS (1)
Recommend consideration of beacon based information for EPS device
  One bit in frame header indicates that one or more EPS devices in the piconet have traffic. If not set, device may go away before beacon body completed (unless watchdog reset is desired)
  Device receives information in new information element (2 octet per EPS device)
  Device uses CAP for watchdog reset – doesn’t have to be for every wake period
  Sending device repeats frame until receiving station acks
  EPS sender uses repeater service
  Recommend that non-EPS sender goes direct rather than using repeater service
    sender must tell coordinator about information to send as well as ack state

## Slide 6: EPS (2)
Where is the Beacon?
  Consideration of Beacon change (new superframe length) –
    Don’t change the superframe length if not truly beneficial to traffic requirements
    If it does change, the EPS device stays on to find the beacon – if once in a long while event, not a problem.
  Clock drift calculation and leading of nominal beacon time is EPS device responsibility – idea is to make acceptable for largest range of applications
Consideration on stream management – TBD

## Slide 7: EPS beacon body element content
Device ID (1 octet)
Watchdog gauge ( 2 bits) –
  11 – disassociated
  10 – watchdog still not received (stay awake and get through to coordinator)
  01 – watchdog reset not received (hope it happens this time)
  00 – watchdog reset received
Stay awake (1 bit) –
Acked (1 bit) – indicates that an ack on previous data was received
Current (1 bit) – indicates new data
Available (3 bits)

## Slide 8: Sender-PNC-EPS device diagram
Source
PNC
EPS Destination
Traffic Command
Traffic Ack
Beacon is
Second chance
Message in
Assigned slot
(short retry timer)
Receive Beacon
Receive traffic
Ack traffic
Missed Beacon
Missed Beacon
Missed traffic
Missed traffic
Traffic Command
Traffic Ack
Update Beacon
Wake
EPS
EPS
Update Beacon
Message
Repeat
Message
Repeat
B
B
B
B

## Slide 9: Sender-PNC-EPS destination text description
Sending device with traffic to EPS device sends message to PNC to set beacon content (this is a new message type)
PNC acks the message
Sending device inserts traffic in previously assigned slot – repeats for each superframe
PNC sets PS bit in header and builds information element for next beacon.
EPS device on sniffing, receives and acks traffic to sender
Sending device sends traffic clear or next traffic to PNC.
Sending device stops sending repeated information or inserts new traffic for repeating (depends on desired effect of first message)
PNC clears bit and info element or sets new info element in the case of new info for next beacon.

## Slide 10: Startup considerations for Power Save Devices
Presume a power saving device that is not a PNC
First time (out of box) start – scanning channels is heavy burden
Additional cold starts – use last channel used as first try. For many applications this will be effective towards power savings.
Once locked to superframe, can use RPS and reduce power after CAP.
Still need to calculate how many superframes are required before an EPS may be entered – to do