## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Nokia MAC Proposal for IEEE802.15 TG4]
Date Submitted: [2.7.2001]
Source: [Juha Salokannel] Company [Nokia]
Address [Visiokatu 1, FIN-33720, Tampere, Finland]
Voice:[+358 3 272 5494], FAX: [+358 3 2727 5935], E-Mail:[juha.salokannel@nokia.com]
Re: [Revision]
Abstract: [Submission to Task Group 4 for consideration as the Low Rate MAC for 802.15.4 with MAC merger proposal considerations]
Purpose: [Overview of MAC proposal for evaluation]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Nokia MAC Submission to IEEE 802.15 Task Group 4
Presented by
Heikki Huomo and Juha Salokannel
Nokia
Note: See notes below some pages in Notes Page View
Notes: Here are the notes!

## Slide 3: CONTENTS
Nokia Key Points in MAC Merger
Nokia Application View
MAC Self Evaluation Criteria
Background Slides (the Detailed MAC proposal)

## Slide 4: Nokia Key Points in MAC Merger

## Slide 5
IEEE 802.15.4 MAC
PURL NWK
(ZigBee)
IEEE 802.15.4 LLC
IEEE 802.2
LLC, Type I
IEEE 802.15.4
915/2400 MHz
PHY
IEEE 802.15.4
868/915 MHz
PHY
Mesh NWK
(Motorola)
Other NWK
Application Convergence Layer (ACL)
(ZigBee)
Specified & Maintained
by IEEE 802(.15.4)
Maintained by ZigBee Working Group
Low Rate Stack Architecture
Open
Other ACL
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 6
IEEE 802.15.4 MAC
Basic Requirements for TG4 MAC
Mandatory: Initialization interoperability with
all (P-aP, Mesh and Star) devices
Mandatory: Interoperability with PHY and upper layers
Mandatory: Very low cost (minimal complexity)
Mandatory: Very low power consumption

## Slide 7
Above the IEEE 802.15.4 MAC
Mesh routing tables, mesh algorithms e.g. are above .15.4 MAC layer
PURL NWK
(ZigBee)
PURL DLC
(ZigBee)
Mesh DLC
(Motorola)
IEEE 802.2
LLC, Type I
Mesh NWK
(Motorola)
Other NWK
Application Convergence Layer
(ACL) (ZigBee)
Other ACL

## Slide 8
IEEE 802.15.4 MAC
IEEE 802.15.4 MAC Block Tasks
Device discovery in
Initialization Channel
Delivery of upper
layer packets
Mandatory features
Optional features
CRC (16/32)
CSMA/CA
Interface to PHY
Interface to DLC/LLC
Stop-and-Wait ARQ
MAC packet
decoding/encoding
MAC Addressing?
Superframe handling
(TDMA)

## Slide 9
Device discovery in
Initialization channel
Multiple Access
The TDMA superframe structure increases complexity and is needed only for real time applications in star topology.
  >Superframe optional
  >Initialization frequency needed
TDMA alone provides poor interoperability between networks.
  > TDMA (star networks) connections should be separated from CSMA/CA and other TDMA networks in frequency.
  > Narrowband PHY
Superframe handling
(TDMA)
CSMA/CA

## Slide 10: Example of Frequency Allocation
Initialization frequency (for all devices), no superframe
CSMA Frequencies for ad hoc data transfer frequencies
(when free from superframes)
TDMA Frequencies for superframe structure
Frequency channels
The specification defines only the initialization frequencies,
the other frequencies are freely available for TDMA
(superframe) and CSMA operation

## Slide 11: Example of Connect&Go "Tell Me More About This Offer"
Service Provider - a simple device having strict power consumption and cost requirements.
Many users (e.g. PDAs) may use the service
virtually at the same time. These devices don't have very stringent power consumption requirements (batteries loaded regularly).
N.Y. $199
Book Now!

## Slide 12
The ID_info (inquiry based on device advertising), CSMA/CA and initialization frequency results in:
  > low power consumption
  > fast service response times
  > low complexity
Due to contention period the starting time of beacons will vary
  >Very bad for powersaving
  > Separate channels for superframes and others
  > Narrowband PHY
Multiple Access & Powersaving
Device discovery in
Initialization channel
Superframe handling
(TDMA)
CSMA/CA

## Slide 13: Key Points in MAC Merger
Fully Optional Superframe
  also the slave functionality for superframe optional
Separate initialization frequencies (without superframes)
  fast device discovery for mobile ad hoc devices
  superframe structure may also contain random access channel
  narrowband PHY layer in globally available band
Addressing Mode: possibility to operate only with IEEE addresses (other addresses optional)
Simple "bit-pipe" MAC
  routing, security etc. implemented in upper layers

## Slide 14: Nokia Application View

## Slide 15: The Web of Trillion Devices
2...3G Wireless
Bluetooth
IrDA
WPAN
RFID
1K Operators -- 1M E-businesses -- 1B People -- 1000B Devices
Zero-Conf
Service (XML, RDF)
Discovery
IPv6 Addressing
& Framing
TCP
UDP
HTTP
WLAN
106
109
1012
103
Personal Trusted Device

## Slide 16: The lock of my door
The lock @ your front door
LOCKED since 2.5 hours. Last user: Pertti. See use history.
Brought to you by
www.securihome.com
at 10:23 27-Feb 2000.
The lock @ your front door
LOCKED since 2.5 hours. Last user: Pertti. See use history.
Brought to you by www.securihome.com
at 10:23 27-Feb 2000.
Not just a lock, but part of an e-business (huge value/bit)

## Slide 17: Tell me more about this painting
The museum installs radio tags to paintings. Users receive the tag IDs in the terminals, which then translate the ID into local/global web pages.
The tag may be a beacon that announces the id periodically, or a passive device that wakes up on terminal’s demand. Very low power demands (parasitic?) would allow permanent embedding.
The ID could be an URL, HP Cooltown-style.

## Slide 18: My Universal Privilege Device
Announces my access privileges to things & services. Maybe identity & authentication as well.
At home, I am the superuser. At office, a humble worker :-)
Only works on me. Talks to the various login controls and hooks me up with minimum hassle.

## Slide 19: Lego-like stuff with embedded electronics
This kid here hacked a motion capture and automated navigation system into his PAN enabled PowerTransformer hero. Basic stuff that any 8-year kid can do with a PC and Lego blocks.
Price is not a constraint since Santa Claus is paying :-)
Neither are batteries, they will only last a day.
But the action must happen by the millisecond to sustain his fast reactions!

## Slide 20: Mobile Commerce
stores can install radio tags to items, smart shelves, scales
detect when items are taken from shelf to shopping cart. Store can do dynamic inventory.
shelf scanners have radio tags and can communicate wirelessly with an access point providing personalized sales items.

## Slide 21: MAC Self Evaluation Criteria

## Slide 22: MAC Criteria Self Evaluation
Transparent to Upper Layer Protocols (TCP/IP) - TRUE
Unique 48-bit Address -TRUE (64-bit)
Simple Network Join/UnJoin Procedures for RF enabled devices - TRUE
Device Registration TRUE
Delivered data throughput (Mini-Mini: 183kbits/s, Pico-Pico/Mini:20.48kbits/s)
Traffic Types - all types supported (Mini-Mini)
Topology - see previous slides
Ad-Hoc Network - TRUE
Access to a Gateway - TRUE (Service field indicates the devices providing access service)

## Slide 23: MAC Criteria Self Evaluation (cont'd)
Max. # of devices
  Address Space: 40 bits (lower part of IEEE address)
The proposal is fully load and RF interference limited P-aP system
Master Redundancy (in P-aP not applicable, in star TRUE)
Loss of Connection - TRUE (device continues ID_info transm.)
MAC Power Management Types - OFF/SLEEP/ON modes
Power Consumption of MAC controller - Low
Authentication and Privacy - FALSE an application layer specific issues (some need some not), reuse of existing work e.g. AAA in IETF.

## Slide 24: Background Slides (The detailed MAC proposal)

## Slide 25: Point-to-anyPoint (P-aP)
Pico device
Beacon device
Mini device
the lock of
our door
my
PDA
her PDA
the lamp
in the room
my PC with
internet access
her watch
a painting
in a museum
a commerce
on the store

## Slide 26: Star Topology Option -an optional MAC feature
Controller
Controller
Sensor with
fixed power supply
Sensor without
fixed power supply
A Mini device becomes
a master of some Pico, Beacon and Mini
devices in the range by making a master-
slave request (one by one). The relation is
maintained by sending beacon messages.
Pico device
Mini device

## Slide 27: The P-aP does not prevent to build a Mesh on the top
Controller
Controller
Sensor
Sensor
Sensor
Sensor
Sensor
Sensor
Pico device
Mini device
MAC only provides a multiple
access. Routing and forwarding
strictly in layer 3.

## Slide 28: Building a Mesh on the top of the MAC
The Point-to-anyPoint MAC topology is the ideal foundation for upper layer routing
Minimal mandatory MAC feature implementation
Avoids layering violations
  routing and forwarding is strictly kept in L3 (IETF)
The proposal allows the usage of existing work e.g. MANET/IETF
  AODV and TORA algorithms
The proposal is future proof and allows scenario based optimizing
  routing algorithms for the mesh topology are improving rapidly at the moment.
  different applications scenarios may require different IP-routing algorithms.

## Slide 29: Foundation for three different Topologies provided
Pico device
Beacon device
Mini device

## Slide 30: Network Definition
Point to anyPoint (P-aP):
  Devices belonging to a network of device A are all those devices who are bidirectionally within the A's radio range. Thus, every device has its own network.
Star (P-mP):
  For a central device, the network is the all the devices it has a master relation and all the other unassociated devices within the radio range.
  For slave devices, the network consists only of the master and itself.

## Slide 31: Network Definition
For every device
in P-aP or a Master
in Star topology:
For a slave device
in Star topology
A
Network of device A
Network of device B
B

## Slide 32: Device classes
Maximal scalability for devices of different size, applications and power consumption requirements
Notes: Mini devices can operate with all device classes
Pico and Beacon devices can not communicate with each other since they are operating in different frequency channels

## Slide 33: Usage Targets for different device classes

## Slide 34: LLC interface
The proposal supports standard IEEE 802.2 LLC interface
  enables incorporation into higher level TCP/IP stacks.
  the proposal does not require TCP/IP nor 802.2 functionalities
Notes:   MAC has a single default upper layer, which then discards unknown packets to another upper layer

## Slide 35: MAC Services
Device Discovery with Device Service Classification
FDMA/CSMA multiple access
Delivery of upper layer packets
Association and Disassociation (optional for Star topology)

## Slide 36: Device Discovery and Service Classification
Each device broadcasts periodically information about its availability for the others by sending id_info PDU
With this PDU the broadcasting device informs that it can be contacted during the next e.g. 1ms
  The PDU contains IEEE address and 8-bit device service field
  Mini devices also include the used unicast channel index into id_info PDU
  Beacon and Pico devices use their own frequency channels all the time
Notes: The broadcasting nature (comparing to alternative listening nature) of all devices is chosen based on some expectations:
  - The TX and RX power consumption are close to each other, thus it does not make much difference.
  - The long TX period in device discovery is avoided (replaced with long listening period)
  - By listening channels the device can find out what kind of devices are available

## Slide 37: Device Discovery and Data Transfer
Notes: Both devices inform periodically about themselves by sending id_info PDU in SAC (Service Advertisement Channel). The left device is activated (from periodic advertisementing) by user and it starts to listen to SAC0 to find out if the needed device is in range. The listening in SAC0 lasts max. 1 second. In the example the left device can hear the second id_info PDU. In the PDU the used data channel (X) of the right device is told. The right device tunes immediately after sending the id_info to the channel X to listen. The left device sends a data PDU to right device and vice versa. Afterwards, both devices come back to the basic cycle (sleep-send id_info-listenonChX-sleep...).

## Slide 38: Basic Packet Structures

## Slide 39: Data Delivery
Acknowledgement
  Stop-and-Wait ARQ
Error Detection
  32 bit CRC check (16 bits in ID-info)
Segmentation and Reassembly of upper layer packets
  IEEE 802.15.1 alike reassembly info in a MAC header
MAC address
  Direct usage of lower part of the IEEE address
  enables flexible topology alternatives

## Slide 40: Data delivery - Bit Rates
Data rate between a Pico and a Mini/Pico device:
  max payload 512 bits
  max. TX duty cycle 25ms
  Max data rate 2 x 20.48 kbits/s
Bit rate between two Mini devices:
  max payload 2048 bits
  carrier sensing 25us, Rx/Tx turnaround 30us
  1 x 169 kbits/s or 2 x 91.6 (=183) kbits

## Slide 41: Star Topology Option
Motivation:
  Tighter Master-Slave relation
  Increased reliability and controlled polling interval (e.g. keyboard)
  On Pico channel, the beacon interval should be max. 1s
  Low latency connections made with mini devices
  Normal service discovery, request, terminate (or expiring)

## Slide 42: Star Topology Messaging

## Slide 43: Design Objectives
Very low power consumption
Easy implementation
MAC is only to provide a generic multiple access, device discovery and data transfer services for upper layers
Scalability
(M)Any device can contact any device in range
Optimized for low bit rates and low duty cycles

## Slide 44: Key Points
Three device classes
  Scalable for different type of devices
CSMA/FDMA Multiple Access schemes
  CSMA/CA for ad hoc operation
  FDMA; special initialization frequencies for fast service setup
Device discovery based on device advertising
  Each device broadcasts its availability for the others
Point to anyPoint topology
Security issues not covered
  Left for upper layer

## Slide 45: Medium Access Scheme FDMA part
Predefined separate frequency channels for Pico and Beacon devices
  device discovery and data transfer in these channels if one of the devices is a Pico or Beacon device
Predefined device discovery channels (SAC)
  device discovery and inquiry between Mini devices
The other frequency channels are allocated for unicast data transmission between mini devices (Data Channels)

## Slide 46: Medium Access Scheme FDMA part
Example of Frequency Channel allocation for device classes
2400
2401
2402
2403
2481
2482
2483
2480
Bluetooth cannels
IEEE 802.11b channel
in North America and Europe
IEEE 802.11b channel
in Europe
Pico
SAC1
SAC2
DataCh#76
SAC0
Beacon

## Slide 47: Medium Access Scheme CSMA/CA part
Air interface transmission (excluding Identification Information PDU in the beacon channel) is preceded by carrier sensing and collision avoidance protocol.
The used parameters vary in the different channels
The parameter values are for further study

## Slide 48: Device Discovery and Data Transfer
Notes: From mini point of view, communication with Beacon device is similar to communication with another mini device, but the whole communication happens on one (Beacon) channel.
The operation with Pico devices is similar, but takes place on Pico channel and Pico is expected to have long sleep periods like the Mini has.

## Slide 49: Device Service Field
Device uses the 8-bit Service Field to advertise the generic services it provides
  An example:
  0000 0000 = default
  0000 0001 = access to gateway
  0000 0010 = a tag proving URL
  0000 0100 = neighborhood device information available
  etc..

## Slide 50: Duty Cycle
An example of duty cycle for mini device
Notes: With the short activity during longer time period, the power consumption is kept low.