## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: IEEE802.15.3: A proposal to reserve multiply fixed time slot for isochronous streaming transmission.
Date Submitted: July 09, 2001
Source: Shig Sugaya, Kaz Takamura, Masa Akahane Company: Sony Corporation
Address: 6-7-35 Kitashinagawa Shinagawa-ku, Tokyo Japan 141-0001
Voice: +81.3.5782.5067, FAX: +81.3.5782.6880
E-Mail: sugaya@wcs.sony.co.jp, takamura@wcs.sony.co.jp, akahane@wcs.sony.co.jp
Re: [ 802.15-01/292r0, P802.15.3/D0.4 ]
Abstract: This proposal presents modified frame type definitions that provide an efficient and a smooth isochronous transmission.
Purpose: To provide an improvement to the current version of the 802.15.3 MAC
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that these viewgraphs becomes the property of IEEE and may be made publicly available by P802.15, however, the substance of the subject matter contained in the viewgraphs remains the property of Sony Corporation.

## Slide 2: One Time Reservation for Multiple Slot
Issues and motivation
  Channel Time Request for isochronous transmission is required every frame
  Streaming contents could be torn by the error of Channel Time Request to a Coordinator
  Transmission could be kept even when the Beacon could not spontaneously be reached
Multiple Fixed Time Slot Allocation
  Reserve multiple super frame allocation with one time Channel Time Request
  Notify the number of super frames that can be allocated by the request

## Slide 3: Request Mechanism
P802.15.3/01292r0 -- Page70
Figure 22 - Channel time request block for a particular stream
Request from Station to Coordinator
  In order to reserve multiple fixed time slot from a Station to a Coordinator, allocate an Octet in Request Type in Channel Time Request
    Multiple Reservation Identifier Octet
      N frames will multiply reserved by one Channel Time Request
        Single fixed time slot request if N=0
        Infinite fixed time slot request if N=255 as far as the network exists
      Another multiple reservation request will be issued before above N is expired if needed
Octets: 2
2
Stream Index
Requested
Channel time
Multiple Fixed Time Slot Requests
1
1
Latency
(in Kμs)

## Slide 4: Assignment Mechanism
Broadcast Information from Coordinator to Stations
  In order to provide multiple fixed time slot from Coordinator to Stations, use 1 CTA(Channel Time Allocation) element
    0 means single fixed time slot allocation (as it is)
    1 - 254 mean multiple fixed time slot allocation
      The number corresponds the number of slots (Time Slot Count)
      The number is decreased every super frame so that the other Stations even can monitor the current status
    255 means infinite fixed time allocation
P802.15.3/01292r0 -- Page68
Figure 20 - Channel time allocation block
Octets: 1
2
Source DEV Address
Slot Start Time
(in 8 μsec Resolution)
Multiple Fixed Time Slot Counts
1
1
Destination DEV Address
2
Time Slot Duration
(in 8 μsec Resolution)

## Slide 5: Continuous Reservation
Time Slot Counter (TSC) is decreased every super frame after Multiple Fixed Time Slot Request (MFTS Req.) is received
Another MFTS Req. is issued before TSC is expired so that continuously reserve Multiple Fixed Time Slot if needed
Beacon
MFTS Req.
Beacon
Beacon
Beacon
Beacon
Beacon
Fixed Time Slot
Fixed Time Slot
Fixed Time Slot
Fixed Time Slot
Beacon
Beacon
Fixed Time Slot
Fixed Time Slot
MFTS Req.
Time
Super Frame
Beacon
Fixed Time Slot
CTA (TSC=4)
CTA (TSC=3)
CTA (TSC=2)
CTA (TSC=4)
CTA (TSC=3)
CTA (TSC=2)
CTA (TSC=1)
MFTS Req.: Multiple Fixed Time Slot Request
CTA: Channel Time Allocation (Multiple Fixed Time Slot Counts = n)

## Slide 6: Cancellation
Infinite reservation is done by sending Infinite Fixed Time Slot Request (IFTS Req.) and Coordinator sets Time Slot Counter (TSC)=0xFF, which is not decremented
If the Station need to cancel the reservation, the Station sends another IFTS Req. and Coordinator resets TSC=0, which could be sent Multiple Fixed Time Slot mode.
Beacon
IFTS Req.
Beacon
Beacon
Beacon
Fixed Time Slot
Fixed Time Slot
Fixed Time Slot
Beacon
Beacon
Fixed Time Slot
IFTS Req.
Time
Super Frame
Beacon
Fixed Time Slot
IFTS Req.: Infinite Fixed Time Slot Request
CTA: Channel Time Allocation (Infinite Fixed Time Slot Count is set by 0xFF not decremented)
CTA (TSC=FF)
CTA (TSC=FF)
CTA (TSC=FF)
CTA (TSC=FF)
CTA (TSC=FF)