## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Physical Layer proposal for the 802.15.4 Low Rate WPAN Standard]
Date Submitted: [July 2001]
Source: [Said Moridi] Company: [Philips Semiconductors]
Address: [Cross Lake Lane, , Redhill, Surrey RH1 5HA, United Kingdom],Voice:[+44 1293 815 428], FAX: [+44 1293 815 050], E-Mail:[said.moridi@philips.com]
Re: [ PHY layer proposal submission, in response of the Call for Proposals ]
Abstract: [This contribution is a PHY proposal for a Low Rate WPAN intended to be compliant with the P802.115.4 PAR. The PHY is designed for ultra low cost and low power consumption networks which are battery powered. The option to implement different output power levels allows to cover a single family dwelling with a robust communication link.]
Purpose: [Response to IEEE 802.15.4 TG Call for Proposals]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: PHY Proposal for Low Data Rate Application
Said Moridi
Philips Semiconductors

## Slide 3: Air Interface Physical Layer
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 4: Frequency Bands
2.4GHz ISM band
  Channel spacing: 4MHz
  F = 2404 + 4k MHz with k = 0, 1, …, 19
  Common band: USA & Europe
915 MHz band can be supported (US)
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 5: Direct Sequence
Spread spectrum regulations allow higher transmit power
  Longer range
  Nominal transmit power: 0dBm
  Up to 30 dBm (USA) using external PA
  Europe: maximum of 35mW eirp (10mW/MHz occupied for data rates>250Kbps)
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 6: Direct Sequence
Direct sequence
  Faster acquisition than frequency hopping
  Complexity in digital domain (cheaper)
  Wide band allows easier integration (channel filters, oscillator)
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 7: Modulation
GFSK/GMSK
  Constant envelope  (cheap) non-linear PA
  Spectrally efficient
  Modulation index; h = 0.5  10%
  Pre-modulation filter; BT = 0.5
  Simple pulse shaping
  Length 11 Barker spreading sequence
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 8: Modulation
Transmitted spectrum:

## Slide 9: Data rates
High bit rate: 250 Kbps
  For low latency short range devices (gaming applications, etc.)
Low bit rate : 27.35 Kbps
  For applications needing longer range and non time critical, like home automation.
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 10: Low Bit Rate
27.35Kbps :
  Trade data rate for extra range via error correction coding
  Hadamard Error Correction Coding (64,7)
    achieves reliable link at low SNR
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 11: Demodulation
Possible to use a frequency discriminator
No equalizer, no Rake receiver
Fast synchronization using Barker sequence matched filtering
Low complexity Hadamard decoder for the low data rate

## Slide 12: Physical Layer Characteristics
Rx | 
Sensitivity Level@ 250Kbps | -91dBm @ BER = 10-4 PER = 1.5 %
Adjacent channel interference | -20dB
Radio freq. Tolerance |  100KHz (40ppm)
Clock tolerance | 40ppm
Rx/Tx switching time | <250μs
Tx | 
Output Power (nominal) | 0dBm
Spectral mask @2MHz offset | 20dBc
Spectral mask @2.5MHz offset | 28dBc
Spurious emission | Compliant to ETSI 300 328 spec.

## Slide 13: Jamming performance
Signal @ -88dBm (sensitivity point + 3dB)
Bluetooth: SIR = 8dB (worst case at 1MHz from carrier)
Microwave oven: SIR = 8dB (always in-band)
80211.b : SIR = -4dB (seen as white noise)

## Slide 14: Performance at 250kbps
Delay spread tolerance: TRMS ~ 50ns (1% PER, 63-byte packet)
Co-channel interference: -97dBm (BER=10-4 )
Adjacent channel interference: -70dBm

## Slide 15: Complexity and Power Consumption
RF part : 5mm2 in .25μm
1 bit A/D converters @ 10Mhz
Baseband: 5mm2 in .25μm
  4K gates (Rx and Tx)
  4K gates (Walsh Hadamard decoder for the low data rate)
  7K gates MAC
  15K gates Micro-controller and Interfaces

## Slide 16: Power Consumption
Two chips solution at present
Baseband: 35mW (0.25μm )
RF:
  120mW for a 0.5μm technology
  55mW for a 0.25μm technology

## Slide 17: Air Interface Summary
Direct Sequence
2.4GHz band (and 915 MHz in USA)
250kbps and 27.35kbps supported
0dBm nominal output power
Allows higher Tx power
GFSK, h = 0.5, BT = 0.5
Simple modulator/demodulator
Good resistance to multipath
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 18: General Solution Criteria

## Slide 19: General Solution Criteria, cont….

## Slide 20: PHY Evaluation Matrix