## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Common reference oscillator for carrier frequency and symbol rate timing]
Date Submitted: [27 June 2001]
Source: [Keith Holt] Company [Intel Corporation]
Address [9750 Goethe Road, M/S LOC 3/8, Sacramento, CA 95827]
Voice:[(916) 855-5177], FAX: [(916) 854-2809], E-Mail:[keith.holt@intel]
Re: []
Abstract: [This contribution presents a proposal for requiring the transmitter to derive the carrier frequency and the symbol clock from a common reference oscillator.]
Purpose: [For information only.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Proposed Change
Propose to change spec to read:
  11.5.4 Transmit center frequency tolerance
    “The transmitted center frequency tolerance shall be ±25 ppm maximum. The transmit center frequency and the symbol rate shall be derived from the same reference oscillator.”
  11.5.5 Symbol rate
    “The PHY shall be capable of transmitting at a symbol rate of 11 Mbaud ±25 ppm. The transmit center frequency and the symbol rate shall be derived from the same reference oscillator.”
Rationale
  Expect that all designs would comply anyway since they would most likely only have one crystal.
  Enforcing this practice might make receiver designs simpler since only one parameter needs to be estimated in the receiver instead of two.

## Slide 3: Symbol Clock Recovery
 N1
 N2
FREF(ACTUAL) = FREF(NOMINAL) (1 + )
FSYM(ACTUAL)
= N1  FREF (ACTUAL)
= N1  FREF (NOMINAL)  (1 + )
FLO(ACTUAL)
= N2  FREF (ACTUAL)
= N2  FREF (NOMINAL)  (1 + )
If we know FLO(ACTUAL) (and of course FSYM(NOMINAL FSYM(NOMINAL)), we can solve for FSYM(ACTUAL) (or equivelantly )
FSYM(ACTUAL) = FSYM(NOMINAL)  (FLO(ACTUAL) / FLO(NOMINAL) )
By deriving both the symbol clock and the transmit frequency from a common reference it is only necessary to measure one to know the other
If we can estimate then we know both symbol clock and transmit frequency
Multiplicative error term is common to all derived frequencies

## Slide 4: Symbol Clock Rate Estimation “Low Side” Frequency Conversion
FIF
FRF
FLO = FRF – FIF = M  FREF
Transmitter
FLO = FRF – FIF = M  FREF
FRF
FIF = FRF – FLO
Receiver
Actual Transmit LO
F’LO = M  F’REF
Actual Transmit Spectrum
F’RF = F’LO + FIF
Actual IF Spectrum
F’IF = F’RF – FLO = (F’LO – FLO) + FIF
Freq
Freq
Error in the transmitter reference relative to the receiver
F’REF – FREF =   FREF
causes an error in the relative symbol rate
F’SYM – FSYM =   FSYM
and an offset in the received IF of
F’IF – FIF =   FLO
By measuring F’IF – FIF, we can obtain
F’SYM – FSYM = F’IF – FIF   FSYM FLO
|S(f)|2
|S(f)|2

## Slide 5: Symbol Clock Rate Estimation “High Side” Frequency Conversion
Transmitter
FIF
FLO = FRF + FIF = N  FREF
FRF
Receiver
F’IF = FLO - FRF
FLO = FRF + FIF = N  FREF
FRF
Freq
Freq
Actual Transmit Spectrum
F’RF = F’LO - FIF
Actual IF Spectrum
F’IF = FLO - F’RF
= -(F’LO – FLO) + FIF
Actual Transmit LO
F’LO = N  F’REF
|S(f)|2
|S(f)|2
Error in the transmitter reference relative to the receiver
F’REF – FREf =   FREf
causes an error in the relative symbol rate
F’SYM – FSYM =   FSYM
and an offset in the received IF of
F’IF – FIF = -  FLO
By measuring F’IF – FIF, we can obtain
F’SYM – FSYM = -F’IF – FIF   FSYM FLO
Note this has opposite sign than for the case of “low side” conversion. However, the received IF spectrum is inverted. If we “flip” the spectrum about FIF, to make it upright then the equation is the same (although the value of FLO is different).
Pre-inverted Spectrum

## Slide 6: Symbol Clock Rate Estimation “High Side” TX, “Low Side” RX
Transmitter
FIF
FLO(TX) = FRF + FIF = N  FREF
FRF
Pre-inverted Spectrum
FLO(RX) = M  FREF
FRF
FIF = FRF – FLO(RX)
Receiver
Actual Transmit Spectrum
F’RF = F’LO(TX) - FIF
Actual IF Spectrum
F’IF = F’RF – FLO(RX)
= F’LO(TX) – FLO(RX) – FIF
= N  F’REF – M  FREF - FIF
Actual Transmit LO
F’LO(TX) = N  F’REF
= (1 + )  N  FREF
Freq
Freq
|S(f)|2
|S(f)|2
Error in the transmitter reference relative to the receiver
F’REF - FREf =   FREf
causes an error in the relative symbol rate
F’SYM - FSYM =   FSYM
and an offset in the received IF of
F’IF – FIF =   FLO(TX)
By measuring F’IF – FIF, we can obtain
F’SYM - FSYM = F’IF – FIF  FSYM FLO(TX)
The problem here is the receiver must know FLO(TX) in order to compute F’SYM - FSYM

## Slide 7: Conclusion
The problem in the final case was that computation of
F’SYM - FSYM = F’IF – FIF  FSYM FLO(TX)
Required the receiver to know FLO(TX).
If we assume zero-IF single-stage direct conversion in both transmitter and receiver, then
FLO(TX) = FLO(RX),, FIF = 0
and the original equation holds
F’SYM - FSYM = F’IF  FSYM FLO(RX).
What about other cases?
Assertion: If we begin and end at baseband with upright spectra then the original equation for the offset in the symbol rate still holds in all cases. Corollary: It doesn’t matter how many stages are used to get from baseband to RF – the net result is equivalent to a single conversion stage. This is still true even if we switch from digital to analog – as long as the sample clock is derived from the same reference.

## Slide 8: Multi-Stage Frequency Conversion
Fin
F’LO(1)
F’LO(2)
F’LO(3)
F’out
F’LO(1) = (1 + )  N1  FREF
F’LO(2) = (1 + )  N2  FREF
F’LO(3) = (1 + )  N3  FREF
F’1
F’2
F’1 = F’LO(1) ± Fin
F’2 = F’LO(2) ± F’1 = F’LO(2) ± (F’LO(1) ± Fin)
F’out = F’LO(3) ± F’2 = F’LO(3) ± F’LO(2) ± (F’LO(1) ± Fin)
= (1 + )  FREF  (N3 ± N2 ± N1) ± Fin
F’out – Fout is only a function of the net frequency shift and is independent of the number of conversion stages
F’REF = (1 + )  FREF