## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [TG3-PHY-and-Draft-report]
Date Submitted: [9 July 2001]
Source: [James P. K. Gilb] Company [Mobilian]
Address [11031 Via Frontera, Suite C, San Diego, CA 92127]
Voice:[1-858-217-2201], FAX: [1-858-217-2301], E-Mail:[gilb@ieee.org]
Re: []
Abstract: [The opening and closing reports for the PHY committee and draft standard for the July meeting in Portland. This summarizes the work accomplished on the conference calls and interim meeting from Orlando through the end of the Portland meeting.]
Purpose: [Document the work accomplished by the PHY committee and for the Draft standard.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: PHY Decisions Reached
CCA defintion
  ED > -70 dBm for 16 symbols)
Sync wording for SIFS and slots
  SIFS = aRXTXTurnAround, slot = aCCADetectTime
Define RSSI and LQI
  RSSI: 8 steps of nominally 8 dB from max. signal
  LQI: SNR measured at demodulator
Header coding
  none, reduce overhead, shorter length improves PER

## Slide 3: PHY Decisions Reached (cont.)
QPSK vs. OQPSK
  To preserve CAZAC, suggest QPSK
Symbol clock synchronization
  Frequency and timing derived from the same crystal
Reviewed jamming margin numbers
  +5 dB above, correct for QPSK number
Data whitener added, seed in PHY header
  in D0.5, 4 rotating seeds, x^15+x^14+1
  Have reference, calculated to verify maximal length

## Slide 4: PHY Decisions Reached (cont. 2)
EVM measurement clarified
  Use reference receiver with carrier lock, timing recovery and amplitude adjustment
Review PLME/PIB, suggestions for modifications
  Modify PHY CCA for start, end, request and confirm
  Change RXNAP to be RXEND
  Add LQI, RSSI, TX power step/max power to PIB
  PWRMGT request and confirm
PHY service field defined (called PHY header)
  2 bytes, 2 bit scrambler seed, 3 bit frame rate, 11 bit frame length

## Slide 5: PHY Decisions Reached (cont. 3)
Lower data rate mode
  Allow 11 Mb/s BPSK for payload
  Longer range for some cases
  Preamble and header are still QPSK
Suggest change to new 15.247 rules
  Allows better channel spacing.
  Easier out of band requirements
  Only drawback is that is not yet at R&O
TPC – as 4 dB steps to less than +4 dBm
Base rate clarified – 22 Mb/s un-coded QPSK

## Slide 6: PHY Decisions Reached (cont. 4)
Differential encoding of QPSK
  Allows non-coherent receivers
  Need to define for BPSK mode
  Not applied to TCM QAM modes
Maximum RX input level: -10 dBm

## Slide 7: Draft Progress
D0.5 released 6 July, 2001
  154 pages
  Only partially review, not ready for voting
Missing pieces
  QoS policies
  Security and privacy
  PICS
  PIB definitions
  Overview