## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Overview of the 802.15.4 PHY Baseline]
Date Submitted: [11 July, 2001]
Source: [Ed Callaway] Company: [Motorola]
Address: [8000 W. Sunrise Blvd., M/S 2141, Plantation, FL 33322]
Voice:[(954) 723-8341], FAX: [(954) 723-3712], E-Mail:[ed.callaway@motorola.com]
Re: [WPAN-802.15.4 Call for Proposals; Doc. IEEE 802.15-01/136r1]
Abstract: [This presentation is an overview of the P802.15.4 PHY baseline.]
Purpose: [Response to WPAN-802.15.4 Call for Proposals]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Overview of the 802.15.4 PHY Baseline
Ed Callaway, Member of the Technical Staff
Motorola Labs
Phone: +1-954-723-8341
Fax: +1-954-723-3712
ed.callaway@motorola.com

## Slide 3: Features
250 and 31.25 kb/s operation
Low chip rate (1 MHz) for low power operation
O-QPSK, for constant envelope modulation
  Simple, low-cost PA
Orthogonal coding provides 4- to 6-dB sensitivity advantage over FM-DSSS approaches
  Greater range for a given output power
5 MHz channel separation
  16 channels in the 2.4 GHz band
  Eases channel filter requirements to lower die size & cost
  Can be used for location determination

## Slide 4: Channelization
2.4 GHz band; 16 channels; 5 MHz channel separation
f = 2405 + 5k MHz, k = 0, 1, … 15
Fixed channelization chosen by dedicated device at network initiation
16 channels allow for 16 simultaneous operating WPANs
5 MHz channel spacing sufficient for location determination using DSSS TDOA methods

## Slide 5: Spreading and Modulation
1 Mc/s chip rate, 31.25 kS/s (32-chip pn sequences)
Offset-QPSK, with half-sine shaping
Augmented pn sequences: CP = 45 (I), CP = 75 (Q)
8-symbol preamble used on both I & Q , augmented CP = 67 (scanning node must correlate only one PN sequence)
Differential Code Position Modulation (D-CPM) used on both I & Q.
  The pn sequence on each channel is (independently) cyclically shifted to one of 16 Gray-coded positions.
  Information is transmitted on each channel as the difference in chip 0 positions from one symbol to the next.
Resulting bit rate is 250 kb/s

## Slide 6: Differential Code Position Modulation
I
Q
Symbol 0001
…
cn+1
c31
c0
…
cn-1
Easily converted to low data rate of 31.25 kb/s
  set I = Q, transmit 1 b/S
Symbol 0000
…
ca+1
c31
c0
ca
…
ca-1
Preamble
…
c31
c30
Preamble
…
c31
c30
cn
c0
c0
cb+1
cb
cm
cm+1
Symbol 0011
Symbol 0010
…
…

## Slide 7: Bottom Line
Cost estimate is < $2 for quantity of 10M
(Includes everything from antenna port to bits)
Implementation size (active area)
  In 0.18 um, it is 3.6 mm2
  (Total active area = RF/analog + Baseband)
Technical feasibility & Manufacturability
  Matlab simulations of Code Position Modulation concept
  At present, developing single chip solution
  Samples available Q1 2002