## Slide 1
Slide <number>
<footer>
<date/time>
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: TG4 RFWaves PHY Proposal
Date Submitted: 2 July, 2001
Source: David Ben-Bassat, RFWaves, LTD.
Address Yoni Netanyahu 5 Or-Yehuda 60376, Israel
Voice: +972-3-6344131 , FAX: +972-3-6344130, E-Mail:DavidB@RFWaves.com
Re:0
Abstract: RFWaves proposal of a PHY layer for TG4.
Purpose: Presentation at the Portland meeting, July-2001.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: RFWaves Proposal
DSSS radio
3 Spreading codes – 13 bits BPSK, 13 bits BFSK, Linear FM
3 Channels per code (BW of 20MHz each)
OOK modulation
1Mbps raw bit rate per channel
Simplicity, Low Cost, Low Power
Suggested implementation using a SAW correlator

## Slide 3: RFWaves – PHY Concepts

## Slide 4: The SAW Correlator

## Slide 5: The RFWaves Radio - Transmitter

## Slide 6: The RFWaves Radio - Receiver

## Slide 7: The RFWaves Radio – Full Module

## Slide 8: Reply to Criteria Document

## Slide 9: Unit Manufacturing Cost (UMC)
SAW Technology, being a 1-layer process, is 10-20 times cheaper than ‘standard’ Silicon technologies.
Additional 6 inductors and 4 capacitors are required for impedance matching and external time constants.
Result to 2.1.2
Device | Technology | Die size
Correlator | SAW | 5X1mm
Resonator | SAW | 1.5X1mm
RFIC | BiCMOS / CMOS | 1.3X1mm

## Slide 10: Unit Manufacturing Cost (UMC)
 | 2002 – 10M units ($) | 2003 – 20M units ($) | Flip Chip packaging($)
RFIC 1.3mm^2 | .63 | .5 | .35
SAW correlator | .55 | .4 | .4
SAW resonator | .43 | .25 | .2
Passives | .1 | .1 | .1
PCB (10X10mm) | .05 | .05 | .05
Assembly & testing | .15 | .1 | .1
Yield | .9 | .96 | .96
Total | 2.1 | 1.35 | 1.25
Result to 2.1.2
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 11: Unit Manufacturing Cost (UMC)
A 50cents, 8-bit micro controller / logic is enough to support a simple MAC layer
Flip Chip packaging technology is under development now for SAW devices, which will enable a single chip solution
We can give up the SAW resonator and exchange it with a reference frequency from the MAC and on-chip PLL
Result to 2.1.2
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 12: Signal Robustness – Interference and Susceptibility
P interferer=P signal - 6dB
Result to 2.2.2.2
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 13: Signal Robustness – Interference and Susceptibility
IIP1 = -18dBm
Input filter Q=5
30 MHz – 1GHz: acceptable interferer power level < -10dBm
1GHz-2GHz : acceptable interferer power level < -20dBm
3GHz-13GHz : acceptable interferer power level < -20dBm
Result to 2.2.2.2
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 14: Signal Robustness - Intermodulation Resistance
Result to 2.2.3.2: (+)
IIP3=-10dBm (simulated)
Notes: Page <number>
        <footer>
<header>
<date/time>
Refers to Jamming as well

## Slide 15: Signal Robustness – Jamming
Result to 2.2.4.2
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 16: Interoperability
Result to 2.3.2
FALSE
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 17: Technical Feasibility - Manufacturability
Manufacturability of SAW Devices:
A well known & tested technology in the past 40 years
Based on piezo-electric qualities of crystals
Penetrated consumer applications in the past decade, as cellular markets evolved rapidly
A one-mask process – only one aluminum layer
SAW correlators have been used in military & radar applications for over 30 years
Result to 2.4.1.2
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 18: Technical Feasibility - Manufacturability
Spreading function & pulse shaping – simulated
Result to 2.4.1.2
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 19: Technical Feasibility - Manufacturability
Spreading function & pulse shaping – measured
Result to 2.4.1.2
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 20: Technical Feasibility - Manufacturability
Autocorrelation function – simulated
Result to 2.4.1.2
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 21: Technical Feasibility - Manufacturability
Autocorrelation function – measured
Result to 2.4.1.2
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 22: Technical Feasibility - Time to Market
RFWaves Schedule
  SAW components have been manufactured and tested
  Functioning RFIC in Q3 2001
  Engineering samples available Q4 2001
  Mass production by RFWaves end of Q1 2002
Result to 2.4.2.2

## Slide 23: Technical Feasibility – Regulatory Impact
Complies with FCC part 15.247
Complies with ETSI ETS 300 328
Result to 2.4.3.2
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 24: Technical Feasibility – Maturity of Solution
The SAW Correlator is functioning, and is very close to the simulated results
The SAW Resonator is functioning, and is very close to the simulated results
A functioning RFIC will be available by Q3 2001
A discrete prototype (based on the real SAW correlator) was built & tested for performance.
Result to 2.4.4.2
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 25: Scalability
Power consumption
  Latency/Bit-rate can be linearly exchanged for power consumption
Coding can be used in the MAC layer to increase range, in exchange for bit-rate/power
Frequency bands
  The system can work in 5GHz and 915MHz ISM bands
Cost
  By supplying reference frequency from the MAC layer, the SAW resonator can be saved, and replaced by an on-chip PLL
Result to 2.5

## Slide 26: Location Awareness
No location awareness capability
The system supports RSSI (as part of the OOK receiver) – which allows distance estimation
Result to 2.6
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 27: Size and Form Factor
 | Length | Width | Height
SAW resonator | 3.8 | 3.8 | 1
SAW correlator | 7 | 5 | 1.3
RFIC | 5 | 5 | 0.5
Passives (10X0402) | 2 | 4 | 0.5
Total size: 10X10mm
Result to 4.1.2
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 28: Size and Form Factor - flip chip option
 | Length | Width | Height
SAW resonator | 1.5 | 2 | 0.8
SAW correlator | 5 | 1 | 0.8
RFIC - BiPOLAR | 5 | 5 | 0.5
Passives (10X0402) | 2 | 4 | 0.5
Total size: 7X7mm
Result to 4.1.2
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 29: Frequency Band
Band width : 20MHz @ -20dBc
Result to 4.2.2
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 30: Number of Simultaneously Operating Full Throughput PAN’s
FDMA:
3 frequency channels are offered: 2.4-2.44, 2.42-2.46, 2.44-2.48
Result to 4.3.2
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 31: Number of Simultaneously Operating Full Throughput PAN’s
Blue – 13bit BPSK Green – Linear FM Red – 13 bit BFSK
Result to 4.3.2
CDMA:
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 32: Number of Simultaneously Operating Full Throughput PAN’s
CDMA: 3 codes
FDMA: 3 frequencies
Total: 9 independent channels are possible
Result to 4.3.2
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 33
9 independent 1Mbps throughput PANs are available
Each frequency/code combination can support:
  9 PANs of 100Kbps using TDMA
  3 PANs of 100Kbps using CSMA
  Many PANs of very low bit-rate/high latency
Number of Simultaneously Operating PAN’s
Result to 4.3.2

## Slide 34: Signal Acquisition Method
A SAW correlator is a matched filter – hence locks on the 1st bit it detects. A preamble of 4-5 bits is enough to set up the link (one bit) and allow the MAC to synchronize (3-4 bits)
Greatly effects power consumption
Result to 4.4.2
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 35: Signal Acquisition Method – 4 consecutive pulses
Result to 4.4.2
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 36: 4 Consecutive Auto-Correlations
Result to 4.4.2
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 37: Range
Output power = 10dBm
Sensitivity = -90dBm
Antenna gain = -5 dBi (Rx & Tx)
Path Loss = 10-(-90)+(-5)+(-5)=90dB
Range:
D=10^[(L-40)/33]=30meter
Result to 4.5.2
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 38: Sensitivity
Result to 4.6.2
Modulation: On Off Keying
BER < 10^-4
(1+2): Eb/N0=11dB
Receiver data:
  Noise Figure = 10dB
  Thermal Noise: Pn=-114+10*log(20)=-101
  (4.1+4.2): N0=-101+10=-91dBm
(3+4): Sense=Ebmin=Eb/NO+NO-PG=-90dBm
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 39: Power Consumption
Power supply: 2-5Vdc
Sleep / Deep Sleep: 1uAmp.
Idle: 20mAmp – Not useful in proposed architecture
Device Registration : 20mAmp
Network infrastructure management: 20mAmp
Result to 2.7.2

## Slide 40: Power Consumption
Result to 2.7.2
 | % sleep | % active | Average current consumption | Battery life for 3V 500mAH
Periodic | 99.999997 | 0.000003 | <1.1uAmp | >>10Years
Intermittent | 99.999994 | .000006 | <1.1uAmp | >>10Years
Repetitive low latency | 97.5 | 2.5 | 0.5mAmp | 1000 hours
* In all 3 scenarios we assumed 500 bits Tx/Rx per transmission
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 41: Power consumption
True measurement of power efficiency should be in Joule/bit – 60nJoule/bit
In low bit-rate - with small packets, the following become critical to total power consumption:
  Standby (sleep) power consumption - 1A
  Wake up time (and related power consumption) - 10Sec
  Acquisition time - 1Sec (1Bit)
Result to 4.8.2

## Slide 42: Power Consumption
Peak current consumption (Vcc=3V)
  Tx=20mA
  Rx=20mA
  STDBY=1A
Result to 4.8.2
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 43: Thank You