## Slide 1: FCC Regulations for Spread Spectrum Devices
Presentation to IEEE 802.11
March 13, 2001
Julius P. Knapp
Chief, Policy & Rules Division
Office of Engineering and Technology
Federal Communications Commission
The views expressed in this presentation are those of the author and may not necessarily represent the views of the FCC or the Commissioners

## Slide 2: Overview
The Basics of Part 15
Spread Spectrum Rules
Recent Developments
A Possible Way Forward
Other Items of Interest

## Slide 3: Part 15: Unlicensed Devices
Provides for Low Power Transmitters
Subpart C: Intentional Radiators
Subpart D: Unlicensed Personal Communications Service Devices (U-PCS)
Subpart E: Unlicensed National Information Infrastructure (U-NII)

## Slide 4: Part 15 Operating Conditions
No Vested Rights to Continued Operation
May Not Cause Harmful Interference
Must Accept Any Interference Received
Operation Must Cease if Notified by FCC that Device is Causing Harmful Interference

## Slide 5: Spread Spectrum Rules Roadmap
Part 2
  Section 2.1 - Spread Spectrum Definition
  Subpart J - Equipment Authorization Procedures
  Subpart I - Marketing Rules
  Subpart K - Importation Rules
Part 15:
  Section 15.31 - Measurement Requirements
  Section 15.201 - Equipment Authorization
  Section 15.203 - Antenna Requirement
  Section 15.207 - Conducted Emissions
  Section 15.209 - Restricted Bands
  Section 15.247 -Technical Rules

## Slide 6: Spread Spectrum Definition
Section 2.1 - Spread Spectrum Systems: A spread
spectrum system is an information bearing
communications system in which: (1) Information
is conveyed by modulation of a carrier by some
conventional means, (2) the bandwidth is deliberately
widened by means of a spreading function over that
which would be needed to transmit the information
alone. (In some spread spectrum systems, a portion
of the information being conveyed by the system
may be contained in the spreading function.)

## Slide 7: Technical Rules
Section 15.247
Frequency Bands
  902-928 MHz
  2400-2483.5 MHz
  5725-5850 MHz
  Presentation will focus on 2400-2483.5 MHz
Separate Provisions for:
  Frequency hopping systems
  Direct sequence systems

## Slide 8: Frequency Hopping Systems (2400 -2483.5 MHz)
Power Output Power: 1 Watt
Must Use At Least 75 Hopping Frequencies
Max. 20 dB Bandwidth: 1 MHz
Avg. Occupancy Time on Any Frequency no Greater Than 0.4 secs. in 30 sec. Period
Power Reduction Required for Antenna Gains Above 6 dBi
RF Exposure Requirements

## Slide 9: Direct Sequence Systems (2400-2483.5 MHz)
Power Output: 1 Watt
Minimum 6 dB Bandwidth: 500 kHz
Peak Power Spectral Density: No Greater Than 8 dBm in any 3 kHz Band
Processing Gain of At Least 10 dB
Power Reduction Required for Antenna Gains Above 6 dBi
RF Exposure Requirements

## Slide 10: Recent Rule Changes (2400-2483.5 MHz)
Home RF Proceeding: Report and Order in ET Docket 99-231 adopted August 22, 2000
Allows Bandwidths up to 5 MHz
Minimum Hopping Channels: 15
Power Reduction for Bandwidths Above 1 MHz: 125 mW
Decision Balanced A Variety of Factors
Did Not Address Processing Gain Msmts.

## Slide 11: Reconsideration Request
Petition for Clarification or Reconsideration Filed on October 25, 2000
Requests That Frequency Hopping Systems With 1 MHz of Less BW Use 15 Hops
Oppositions Filed by Proxim & Mobilian

## Slide 12: Wi-LAN Petition
Wi-LAN, Inc. Filed for Certification of a Device Using Wide-Band Orthogonal Frequency Division Multiplexing (WOFDM) under SS Rules
FCC Staff Denied Application: Fails to Meet Spread Spectrum Definition
Wi-LAN Has Appealed to Commissioners: Argues Its System Meets All FCC Rules

## Slide 13: Assessing the Situation
Outstanding Issues:
  Direct Sequence processing gain measurement
  Home RF Reconsideration
  Wi-LAN Application for Review
Other Technology Issues Anticipated
IEEE 802.11 Standards Activities
Rules May Restrict Technologies Unnecessarily
Frequent Rule Makings Are Undesirable

## Slide 14: A Possible Way Ahead
Initiate a Notice of Proposed Rule Making In the Near Future
Areas for Consideration - Whether to:
  Retain Processing Gain Requirement
  Reduce Number of Hops
  Liberalize Spread Spectrum Definition
  Craft Rules Similar to U-NII Rules?
  Also Consider 915 MHz & 5.8 GHz bands?
Have Received Informal Suggestions
May Conduct Forum After NPRM Released

## Slide 15: Understanding the Rule Making Process
Administrative Procedures Act
Rule Making Process:
  Notice of Proposed Rule Making
  Opportunity for Comments & Replies
  Ex-Parte Contacts
  Report & Order - Adopts Rules
  Reconsideration
  The Electronic Comment Filing System (ECFS)
Role of FCC Staff: Analysis & Recommendations
Decision-Makers: Chairman and Commissioners

## Slide 16: FCC Organization Chart

## Slide 17: A Word About Industry Standards
Industry Has Developed Standards Under Part 15: IEEE 802.11; Bluetooth; Home RF.
FCC Has Sought to Provide A Flexible Framework for Standards to Develop
Consistency of Standards & FCC Rules:
  Products must comply with the rules
  FCC will consider rule changes to accommodate advances in technologies & standards
  Final determination will be based on the record
  Everyone will have the opportunity to comment

## Slide 18: Other Developments: Equipment Certification
Equipment Certification Required
Certification Can be Performed by:
  FCC
  Telecommunications Certification Body (TCB)
Mutual Recognition Agreements (MRAs):
  MRA implemented with European Union
  MRA with APEC agreed & progressing
  MRA with CITEL moving less quickly

## Slide 20: Other Developments: RF Exposure
TCBs Are Currently Not Permitted to Certify Devices Subject to RF Exposure Testing
Reason: No Measurement Procedure
IEEE is Developing Measurement Procedure
FCC Considering Update to OET Bulletin 65 Supplement C

## Slide 21: Modular Devices
FCC Public Notice: June 26, 2000: Part 15 Unlicensed Modular Transmitter Approval
Intended to Reduce the Burden of Filing for Certification of Every Device
Issue: How to Deal With RF Exposure

## Slide 22: Other Developments: General Issues
Recent Enforcement Bureau Letter: Interference to Amateurs in 2.4 GHz Band
Technological Advisory Committee
  Examining unlicensed devices
  Concern about “Tragedy of the Commons”
  Noise study planned
Unlicensed PCS (1910-1930 MHz, 2390-2400 MHz)
  Winforum petition
  UT Starcomm Petition

## Slide 23: Conclusion
Thank You For This Opportunity To Address IEEE 802.11
We Anticipate An FCC Rule Making
We Welcome Any Ideas You May Have
For Further Information:
  www.fcc.gov
  jknapp@fcc.gov