## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: P802-15_TG3-Draft-Standard-d05-MAC-Amendments
Date Submitted: 11 July, 2001
Source: Allen Heberling Company XtremeSpectrum
Address 8133 Leesburg Pike, Vienna, Va. 22182
Voice: 703-269-3022, FAX: [], E-Mail: adheberling@ieee.org
Re: [00000d05P802-15-3_Draft-Standard.pdf]
Abstract: [Amendments to the MAC clauses of 00000d05P802.15.3__Draft-Standard.pdf]
Purpose: To record MAC layer amendments identified as being required modifications for draft standard d05.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: TG3 MAC Committee P802-15_TG3-Draft-Standard-d05-MAC-Amendments Recommendations

## Slide 3: Issue Resolution Recommendations
R. Gubbi Frame type and Command Types vs B. Shvodian Frame type table organization ( 221r2 items:. 42,43,63,187,188,189 ,190 ,191,193) and (114r6 item: 186)
  R. Gubbi & B. Shvodian agreed to this recommendation: Move these currently defined frame types into the command frame type structure:
    PNC Selection Frame
      Alternate PNC Announcement Command
      Alternate PNC Pullout Command
      New PNC Announcement Command

## Slide 4: Frame types becoming Command Types continued…
    Association Request Frame Becomes Association Request Command
    Association Response Frame Becomes Association Response Command
    Disassociation Request Frame becomes Disassociation Request Command
  Frame type bits used in Frame Control Field will now be 3 instead of 4.

## Slide 5: Frame types becoming Command Type continued…
Frame Types remaining
  Beacon
  Immediate ACK
  Command frame
  Data Frame

## Slide 6: Command Types 114r6 item 192:
Split Probe Information command into Probe Request and Probe Response Commands.
Split Device Information command into Device Information Request and Response

## Slide 7: Coordinator Challenge Frame (114r6 items 68,205, 206, 230)
R. Gubbi & B. Shvodian agreed to this recommendation: Add the following text to d05 Clause 8.1.8,
  “When a station joins a piconet, the coordinator shall compare the capabilities field of the new station to its own. If the PNC-Des-Mode bit is set in the new station and not in the current PNC, the old PNC shall perform coordinator handover if allowed by the TBD security policy. …

## Slide 8: Coordinator Challenge Frame (114r6 items 68,205, 206, 230,231)continued…
  …If the new station is more qualified to be the coordinator, the coordinator may perform coordinator handover if allowed by the TBD security policy. Handover shall happen within a TBD parameter duration.”
  Add MACPIBPNCDesMode to the MAC PIB.

## Slide 9: Coordinator Selection (114r6 Item 68)

## Slide 10: Issue Resolution Recommendations continued…
Retain Frag/Defrag text in D05/Clause 8.5.
Peer discovery added to d05/Clause 8.7. Supporting reasons listed in 271r1.
Moved multi-rate usage table from 7.3.1 in d04 to clause 8.8 in d05. (per 271r1)

## Slide 11: Issue Resolution Recommendations continued…
Delayed ACK expedite request added to d05 with additional supplemental text provided in 271r1.
Recommend Pad byte indication bit in Frame Control. Supporting text in 271r1.

## Slide 12: Priorities 114r6 items 170, 215
are addressed by text in 271r1 and 802.1D. Consequently, the MAC Data Service and Priority Management clauses need to be updated with text from the aforementioned sources.

## Slide 13: PNID 114r6 item 48
Add this text to 8.1.2 :
  “The seed for generating a randomized PNID shall be the 48 bit PNC device ID.”

## Slide 14: Implied Ack 114r6 item 194
114r6 Implied Ack item 194 is addressed by d05 with additional text below.
  “Responding DEV shall send only one frame for a received frame soliciting implied-ack.”
  “Responding DEV can take any length of time within the current GTS without exceeding it.”
  “Responding DEV can send imm-ack as response to an implied-ack solicitation.”

## Slide 15: Implied Ack 114r6 item 194 continued…
  “Responding DEV shall send imm-ack if it does not know the end of current GTS.”
  “Responding DEV shall make sure there is enough room in the current GTS for the im-ack, if required, for the frame sent as response to implied-ack solicitation.”

## Slide 16: Assoc/Disassoc 114r6 items (211,212).
  Add Broadcasting DevInfo concepts to d05 as captured in 271r1 and 259r2.
  Also, in Figure 33, Clause 7.5.10.1/d05 remove Requester Dev. ID field

## Slide 17: StreamMgt 114r6 item 216
Add this text:
  “Reduce the stream index to 8 bits with the remaining 3 bits reserved. This results in simpler implementation based on global stream index that is allocated by PNC. An implementation based stream index that is unique for SA/DA pair results in more complex implementation.
  Add a Stream-index to ChnlTimeReq by replacing the reserved field in Fig.22, Clause 7.5.1.1; Add Stream-index to ChnlTimeAllocationBlock along with one reserved byte in figure 20 clause 7.4.9;

## Slide 18: StreamMgt 114r6 item 216 continued…
  Remove time slot duration from CTA block in Fig. 20, clause 7.4.9;
  Add ChnlTimeReq Block to Stream QoS parms in Stream Mgt . Cmnd in figure 42 Clause 7.5.12;
  Retain StreamID in Stream QoS parms.; Add descriptions for each of the "new" fields.

## Slide 19: CoordHandOvr (114r6 item 128)
Add these variables: minHandOvrTO(.25sec) and maxHandOvrTO(1.sec). Also change the CoordHandOvr timer resolution to 1Kus

## Slide 20: MaxGTS Info Element (114r6 item 213)
Doc: 259r2 item #6 suggests replacing the reserved byte of the Max GTS info element with MaxProcessedCTAs. Also add indicated PIB values.
Managed Object
Data Type
MACPIBMaxAssignedCTAs
Integer
MACPIBMaxProcessedCTAs
Integer

## Slide 21: Channel Time Request good until changed.(221r2 Item 117 and 114r6 Item 217)
Add the text below to clause 8.2.4/d04
  “Channel time requests that are ACKed are valid until the next channel time request is made.”
Add text to d05/8.2.3.2 to address What happens if the PNC allocates less channel time than was requested? Does it allocate more if it becomes available? Yes.
  MAC committee consensus recommendation.

## Slide 22: TSF Elimination and Duration increment change (114r6 items: 166, 208, 209, 210)
Add or delete text to the d04 clauses referenced in doc 259r2

## Slide 23: CAP Back-Off Resolution (114r6 Items 146, 219)
Add the following sentence to section d04/8.2.3.1:
  “The resolution of the backoff value shall be aBackoffSlot μs, where aBackOffSlot is a PHY dependant parameter. “
  MAC committee consensus recommendation.

## Slide 24
Add aMaxFrameSize parameter to d04/clauses 7.1.12 and 11.2.7. Indicate this parm is a Phy dependant parameter.
FrameBody 114r6 item 228:

## Slide 25: Repeater 114r6 item 224
Add clarifying text to the Repeater Service MAC Functional Description Subclause describing the ACK policy required to support the repeater service.

## Slide 26: Device Registration 114r6 item 225
Add this text to the Device Registration MAC Functional Description subclause
  PNID should always have the PNID value that appears in the Beacon.
  Open registration should be accomplished through a new open registration command (if needed) and not via a null PNID.