## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [PHY proposal for the 802.15.4 Low Rate WPAN Standard]
Date Submitted: [July 2001]
Source: [Hans van Leeuwen, David Archer] Company: [STS/Adcon RF Technologies]
Address: [Zekeringstraat 40, 1014 BT Amsterdam, Netherlands]
Voice:[+31 20 420 4200], FAX: [+31 20 420 9652], E-Mail:[HvL@STS.nl]
Re: [PHY adoption for 868MHz ]
Abstract: [This contribution explains the PHY specifications for 868 -928 MHz bands]
Purpose: [A unified PHY proposal for the 868-928 MHz bands Motorola, Philips, STS/Adcon]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Starting point
Original proposal had 1 or 2 radio channels in the 868MHz band, using 31 chips, and a data rate of 10 kbps
We have looked at ways to increase the number of channels, and the data rate

## Slide 3: Adding More Channels
2 scaleable solutions:
5 or 10 radio channels
  2 or 4 in 1% Duty cycle band
  2 or 4 in 0,1% DC
  1 or 2 in 100% DC
Data rate higher with complex modulation
  QPSK 2bits/S

## Slide 4
Receiver adjacent channel rejection requirements are contained
in ETSI 220 section 9.1.3
This stipulates :
70 dB for the adjacent channel in the band selected ( specified by the manufacturer)
Problems we encounter

## Slide 5: Channels
Implementing multiple channels in the 868MHz band
is going to prove very, very expensive.:

## Slide 6
CONCLUSION: Channels:
DSSS gives the possibility of 15 dB spreading plus the 10 dB less stringent selectivity requirement
Even so, implementing filter circuitry would be so
costly that we decided to stay with the 2 channel
solution.
NB would have to provide 25 dB more filtering

## Slide 7: Data rate
We propose 32 chip DSSS with dual data rates:
1 bit/symbol 10 kbps
8 bit/symbol 80 kbps
Ultimately other data rates are possible. These are achievable with the current implementation.