## Slide 1: IEEE P802.15 Working Group for Wireless Personal Area NetworksTM
IEEE 802.15.2 Coexistence Task Group
Presentation to the Bluetooth SIG
Program Managers

## Slide 2: IEEE 802.15.2 Deliverables
Coexistence Model
  Quantify the effect of the mutual interference of WLAN (e.g. 802.11) and WPAN (e.g. Bluetooth) upon one another.
Coexistence Mechanisms
  Mechanisms or techniques to facilitate coexistence of WLAN and WPAN devices.
Both to be documented in an IEEE Recommended Practice

## Slide 3: Coexistence Model
The purpose of this Coexistence Model is:
  To quantify the effect of the mutual interference under various scenarios.
    WLAN in Laptop and Bluetooth in nearby PDA
    WLAN and Bluetooth in the same Laptop
  To demonstrate the effectiveness of the adopted Coexistence Mechanism.

## Slide 4: Coexistence Model
The Coexistence Model consist of four sections,
  Physical Layer Models of the 802.11 and Bluetooth Radios
  MAC Layer Models of both 802.11 and Bluetooth
  RF Channel Model of the Radio Channel
  Data Traffic Models of the traffic over both 802.11 and Bluetooth networks.

## Slide 5: Coexistence Mechanisms
Submissions were given at,
  November 2000 meeting
  January 2001 meeting
Voted on Selection of Coexistence Mechanisms
  March 2001 meeting
  May 2001 meeting

## Slide 6: Coexistence Mechanisms
Collaborative Mechanisms
  Some form of communication exists between the WLAN and WPAN.
  Use this link to provide fair sharing of medium (i.e. air waves)
Non-Collaborative Mechanisms
  No communication between WLAN and WPAN exists.
  Techniques to minimize the effects of the mutual interference

## Slide 7: Coexistence Mechanisms
Collaborative Mechanism (Only one)
  Selected a joint proposal from Mobilian, Symbol Technologies, and NIST.
  Primarily a Coordinated Scheduling Mechanism.
  To be used when IEEE 802.11b and Bluetooth are to be co-located in the same unit (e.g. laptop computer)

## Slide 8: Coexistence Mechanisms
Non-Collaborative (Multiple)
  Bluetooth Packet Selection and Scheduling
  Bluetooth Adaptive Frequency Hopping
  IEEE 802.11b Data Rate Scaling

## Slide 9: Current Relationship between IEEE and Bluetooth SIG
IEEE 802.15.1 is converting the Bluetooth specification into an IEEE standard.
Steve Shellhammer, Chair of IEEE 802.15.2, is a member of the Bluetooth SIG Coexistence Working Group.
Tod Sizer, Chair of the Bluetooth SIG Coexistence Working Group, gives a liaison report at IEEE 802.15.2 meetings

## Slide 10: Proposal from IEEE 802.15.2 to the Bluetooth SIG
IEEE 802.15.2 is developing an Adaptive Frequency Hopping technique to allow Bluetooth to hop around frequency-static systems, like IEEE 802.11b WLAN.
The Bluetooth SIG is interested in Adaptive Frequency Hopping.

## Slide 11: Proposal from IEEE 802.15.2 to the Bluetooth SIG
The IEEE would like to avoid having two incompatible Adaptive Frequency Hopping techniques, one defined by the IEEE and one defined by the Bluetooth SIG.
The IEEE would like to work with the Bluetooth SIG to agree on a common Adaptive Frequency Hopping technique.

## Slide 12: Proposal from IEEE 802.15.2 to the Bluetooth SIG
Once the common technique is agreed upon it would be,
  Standardized in IEEE 802.15.2
  Possibly included in a future revision of the Bluetooth specification.
We could also look into working together on other topics
  Collaborative Coexistence Mechanisms
  Coexistence Modeling