## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [TG3-Channel-Placement]
Date Submitted: [2 July 2001]
Source: [Chandra Vaidyanathan] Company [Aryya Communications]
Address [444 N Frederick Av., Suite 309 Gaithersburg, MD 20877]
Voice:[240-683-8802], FAX: [301-947-8964], E-Mail:[chandrav@ieee.org]
Re: []
Abstract: [This contribution proposes a channel plan for 802.15.3 WPAN.]
Purpose: [To propose a channel plan for 802.15.3 high-rate PHY.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Overview
2 Channel placement plans presented based on regulatory requirements
  FCC 15.249, ETS 300 328 and ARIB STD-T66
  FCC 15.247 (new), ETS 300 328 and ARIB STD-T66
Channel plan includes
  High-density user plan
  802.11b co-existence plan

## Slide 3: Channel Placement Plan - 1
Current draft based on regulatory emission requirements
  FCC 15.249 (US), ETS 300 328 (Europe) and ARIB STD T66 (Japan)
Channel placement strategy
  Find the minimum and maximum center frequencies that meet the emission requirements based on the transmit spectral mask
  The middle channels are selected by maximizing inter-channel spacing

## Slide 4: Summary of Regulatory Body Requirements
Max power in US and Japan: -1.25 dBm/MHz
Higher power levels permitted in Europe
Emissions: FCC requirements most restrictive at –41.25 dBm/MHz
Transmit power
Emission requirements

## Slide 5: Selecting Center Frequencies
Min center freq: 2.415 GHz (2.4 + 0.015)
Max center freq: 2.468 GHz (2.4835-0.015)
0 dBr = -1.25 dBm/MHz

## Slide 6: Channel Plan: High-user Density
Channel ID
Center Frequency
(MHz)
1
2415
2
2433
4
2450
5
2468

## Slide 7: Channel Plan: 802.11b Co-existence
Channel ID
Center Frequency
(MHz)
802.11b Center Frequency (MHz)
1
2415
2412
3
2441
2437
5
2468
2462

## Slide 8: Channel Placement Plan - 2
Under the NPRM issued on May 11, 2001 digital modulation schemes can use FCC 15.247
Use same strategy as before
  Find max and min center frequencies
  Maximize inter-channel spacing

## Slide 9: Summary of Regulatory Requirements
Higher transmit powers possible in the US
Transmit power
Emission requirements

## Slide 10: Channel Placement
Min center frequency: 2.412 GHz (2.39 + 22)
Max center frequency: 2.461 GHz (2.4835 – 22)
US and Europe:
0 dBr = 8.75 dBm/MHz
Japan:
0 dBr = -1.25 dBm/MHz

## Slide 11: Channel Plan: High-user Density
Channel ID
Center Frequency
(MHz)
1
2412
2
2428
4
2445
5
2461

## Slide 12: Channel Plan: 802.11b Co-existence
Channel ID
Center Frequency
(MHz)
802.11b Center Frequency (MHz)
1
2412
2412
3
2437
2437
5
2461
2462

## Slide 13: Conclusions
Two channel plans presented
  The inter-channel spacing is 16-17 MHz which prevents adjacent channels from overlapping
  Both plans have a high-user density and 802.11b co-existence mode
  Since the second plan based on FCC 15.247 permits higher transmit powers in the US it is recommended that this plan be adopted in the standard

## Slide 14: Backup

## Slide 15: Summary of Regulatory Requirements
ETS 300 328
  Radiated power <= 20 dBm, and peak power density <= 10 dBm/MHz
  Out-of-band emissions < –20 dBm/MHz and –30 dBm
ARIB STD-T66
  Radiated power (non spread spectrum systems) <= 10 dBm
  Emissions should be less than
    –16 dBm (~ –27.3 dBm/MHz) in frequency bands [2.387 - 2.4 GHz] & [2.483 – 2.4965 GHz]
    –26 dBm for frequencies < 2.387 GHz and frequencies > 2.4965 GHz

## Slide 16: Summary of Regulatory Requirements
FCC 15.249
  The maximum transmit power is limited to –1.25 dBm/MHz
  Emissions
    Less than –41.25 dBm/MHz in freq bands [2.310-2.390 GHz] and [2.4835-2.500 GHz] (FCC 15.205)
    Freq < 2.31 GHz and freq > 2.5 GHz should be either
      Less than –41.25 dBm/MHz (FCC 15.209), or
      Less than 50 dBc (FCC 15.249)

## Slide 17: Summary of Regulatory Requirements
FCC 15.247 and FCC 15.205
  Maximum transmit power can be up to either 0.125 watt or 8 dBm in a 3 kHz bandwidth, whichever is lower
  Emissions in frequency bands 2.310-2.390 GHz and 2.4835-2.500 GHz must be less than –41.25 dBm/MHz (FCC 15.205)
  Emissions in frequency bands outside the 2.4 – 2.4835 GHz band, with the exception of the bands listed in item 1, should be 20 dB below the transmit power in the desired channel (FCC 15.247)