## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Proposed technique for transmitter EVM measurement]
Date Submitted: [27 June 2001]
Source: [Keith Holt] Company [Intel Corporation]
Address [9750 Goethe Road, M/S LOC 3/8, Sacramento, CA 95827]
Voice:[(916) 855-5177], FAX: [(916) 854-2809], E-Mail:[keith.holt@intel]
Re: []
Abstract: [This contribution presents a proposed measurement technique for verifying compliance to the transmitter EVM specification.]
Purpose: [For information only.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Problem
Purpose of EVM is to measure the modulation accuracy of the transmitter
EVM Measurement is ambiguous unless the precise conditions are specified under which it is to be measured
Some transmitter impairments are mitigated by the receiver
Current wording implies a transmitter design which is more difficult than necessary

## Slide 3: Definitions
Definition #1
  Measurement of the deviation of the actual transmitter from an ideal transmitter
  Includes effects of all impairments
Definition #2
  Measurement of the uncorrectable deviation of the actual transmitter from an ideal transmitter as determined using an “ideal” reference receiver
  Impairments mitigated by reference receiver don’t count

## Slide 4: Transmitter Impairments
I/Q gain imbalance
I/Q phase error
Carrier leakage (I/Q offset)
Intermodulation distortion
Amplitude/group delay distortion vs. frequency
Phase noise
Noise
I/Q delay mismatch
Which of these impairments should be included as part of the EVM measurement?

## Slide 5: Reference Receiver
Propose that reference receiver estimates/corrects
  Carrier frequency/phase
  Symbol timing
  Gain
And does not estimate/correct
  I/Q offset
  I/Q gain imbalance
  I/Q phase error
  Phase noise
  Intermodulation distortion
  I/Q delay mismatch
  Amplitude/phase distortion vs. frequency (I.e., no equalizer)
Even those impairments which are not explicitly corrected will be partially mitigated by compromise solution to optimal gain, carrier phase, etc.

## Slide 6: Conclusions
Should not unnecessarily complicate the transmitter design with performance metrics than don’t matter (because the receiver partly corrects them).
Definition of EVM should be more specific about measurement technique to include reference receiver detail.