## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Unified MAC proposal for the 802.15.4 Low Rate WPAN Standard]
Date Submitted: [June 2001]
Source: [Phil Jamieson] Company: [Philips Semiconductors]
Address: [Cross Lake Lane, , Redhill, Surrey RH1 5HA, United Kingdom]
Voice:[+44 1293 815 265], FAX: [+44 1293 815 050], E-Mail:[phil.jamieson@philips.com]
Re: [ MAC layer proposal submission, in response of the Call for Proposals ]
Abstract: [This contribution is a highly flexible MAC proposal for a Low Rate WPAN intended to be compliant with the P802.15.4 PAR. It is intended to support both master-slave and peer-to-peer communications for low data rate networks. It is designed to support ultra low power consumption for battery operated nodes at very low implementation cost. This proposal is an attempt to bring together features from all the presented MAC proposals into a unified approach.]
Purpose: [Combined MAC proposal following Orlando meeting]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Unified MAC proposal for the 802.15.4 Low Rate WPAN Standard
Phil Jamieson
Principal Engineer, Philips Semiconductors
Phone: +44 1293 815265
Email: phil.jamieson@philips.com

## Slide 3
IEEE 802.15.4 MAC
PURL NWK
(ZigBee)
PURL DLC
(ZigBee)
Mesh DLC
(Motorola)
IEEE 802.2
LLC, Type I
IEEE 802.15.4
915/2400 MHz
PHY
IEEE 802.15.4
868/915 MHz
PHY
Mesh NWK
(Motorola)
Other NWK
Application Convergence Layer (ACL)
(ZigBee)
Maintained by
IEEE 802.15.4
Maintained by
ZigBee
Working Group
Low Rate Stack Architecture
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 4: Stack Components
Multiple IEEE 802.15.4 PHY layers
  868/915 MHz and 915/2400 MHz
IEEE 802.15.4 MAC
Multiple link layers
  PURL, Mesh, IEEE 802.2 (Type I)
Network layers implement topology
  Star (PURL), Mesh (Cluster Tree), etc.
Application convergence layer
  Application can interface to all NWK layers

## Slide 5: IEEE 802.15.4 MAC
Master/slave & peer-peer topologies
  Supports: star, point to any point, mesh
Access is CSMA-CA
Data rates of 28k & 250kbps but scalable
Optional use of network beacons
Time slots for low latency transfer
Super-frame is contention based
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 6: Node Types
Distribution node
  Controls the network topology at that node
  Master/co-ordinator or mediation device
  Talks to other distribution and slave nodes
Slave node
  Cannot control the network
  Very simple implementation
  Talks only to a distribution node

## Slide 7: Addressing Modes
Master/slave
  Network identifier
  Short network or unique (IEEE) addresses
Peer-peer
  Unique (IEEE) addresses
All nodes have 64-bit IEEE address
  Can be withheld

## Slide 8: Network Capacity
One distribution node per master/slave n/w
Up to 254 allocated nodes per master/slave n/w
Slave/distribution nodes (only memory limited)
4 low latency devices
7+ co-located networks
  Dependent on the PHY layer capabilities

## Slide 9: Master/Slave Topology
Distribution node
Slave node
Communications flow
Star

## Slide 10: Peer-Peer Topology
Distribution node
Communications flow
Point to any point
Cluster tree/mesh

## Slide 11: Combined Topology
Distribution node
Slave node
Communications flow
Clustered stars - for example,
cluster nodes exist between rooms
of a hotel and each room has a
star network for control.

## Slide 12: “Connect & Go” Topology
Distribution node
Connecting
Walk by - for example, a retail
shop advertises offers. As users
walk by the nodes connect, exchange
data and leave.
Watch & Learn - for example, a
node can connect to a picture in a
gallery and exchange information.
The user will then leave.
Communications flow

## Slide 13: Traffic Types
Periodic data
  Application defined rate
Intermittent
  Application/external stimulus defined rate
Repetitive low latency data
  Allocation of time slots

## Slide 14: Network Beacon
Identifies the network
Describes the super frame structure
Provides data presence indications
Only present during network activity
Network can choose not to use it

## Slide 15: Super Frame Structure
15ms
Network
beacon
Contention
period
Beacon
extension
period
Slot 3
Slot 2
Slot 1
Allocated
slot
Transmitted by distribution nodes. Contains network information,
super frame structure and notification of pending node messages.
Space reserved for beacon growth due to pending node messages
Access by any node using CSMA-CA
Reserved for nodes requiring guaranteed bandwidth.

## Slide 16: Power Management
Protocol designed for low power devices
Slave nodes initiate all transfers (where used)
Sleep periods are application defined
Nodes wake on
  external interrupt from some user stimulus
  application defined interval
  health check cycle

## Slide 17: Use of Channels
Dependent on choice of PHY layer
Application defined classes
PHY defined (data rates?)
Frequency agility for interference robustness
High density transfer between two nodes

## Slide 18: Higher Layer Functionality
Transfer reliability (DLC/LLC)
Packet segmentation/sequencing (DLC/LLC)
Topology management (NWK)
Node connection procedures (NWK)
Security & authentication (ACL)
Application convergence protocol (ACL)
Device/service discovery (ACL)

## Slide 19: Total System Requirements
8-bit C, e.g. 80c51
Distribution node protocol stack <32k - <64k
  Depends on higher layer configurations
Slave node stack ~4k
Distribution nodes require extra RAM
  Device database
  Routing table
  Message storage for subsequent transfer

## Slide 20: Analysis of the Cluster Tree Requirements

## Slide 21: Current MSC
Source
Node
MD
Destination
Node
RTS
RTS Reply
Query
Query Response
CTS
DATA
ACK

## Slide 22: MSC Using PURL
Source
Node
MD
Destination
Node
RTS
ACK/NAK
Query
Query Response
CTS
DATA
ACK
ACK
ACK
ACK

## Slide 23: Cluster Tree Snapshots
N1
N2
MD
Mediation Phase:
Transfer Phase:
N2
N1
Topology: Star
Topology: Peer-peer
RTS/ACK
Query/Query Response/ACK
CTS/ACK/DATA
PURL supports both topologies

## Slide 24: Data Primitives
DATA_REQ(
SourceAddress,
DestinationAddress,
PDULength,
PDU,
Options
)
SourceAddress DestinationAddress Topology
NULL NULL Other
NULL Defined Star
Defined NULL Star
Defined Defined Peer-Peer
DATA_IND(
SourceAddress,
DestinationAddress,
PDULength,
PDU,
Options
)

## Slide 25: Packet Structure
PRE
SOP
LEN
MFL
CRC
DSP
DSN
PURL DATA Packet
ADDRESSING & NWK PDU Contents:
SNeID
SCID
SNoID
CV
SH
SNC
DNoID
SCID
SNoID
NM
RCID
RNoID
DNeID
DCID
RCV
RT
DNoID
SCID
SNoID
NP
CV
DNeID
DCID
SNeID
SCID
SNoID
DCID
DNoID
Query
Query Response
RTS
CTS
NWK PDU
ADDRESSING

## Slide 26: Address Normalization
Address has four (five?) components:
  Network identifier (12 bits)
  Cluster identifier (8 bits)
  Node identifier (8 bits)
  Collapsed value (4 bits)
  Timing information?
All transfers send all this information
MAC flag indicates cluster tree addressing

## Slide 27: Primitives Addressing
DATA_REQ(
SourceAddress,
DestinationAddress,
PDULength,
PDU,
Options
)
SourceAddress/DestinationAddress is a logical concatenation of:
Network Identifier +
Cluster Identifier +
Node Identifier +
Collapsed Value +
Timing Information?

## Slide 28: Proposed Packet Structures
SA
CV
SH
SNC
SCID
SNoID
NM
RCID
RNoID
DA
RCV
RT
DNoID
SA
NP
CV
DNeID
DCID
SA
DA
Query
Query Response
RTS
CTS
Packets sent using the STAR topology:
Packets sent using the PEER-PEER topology:
SA
DA
DATA
DATA
DSP
DSN
DSP
DSN
DSP
DSN
DSP
DSN
DSP
DSN

## Slide 29: Minimal Changes to PURL
Add option in DLC data primitives
Add option in MAC data primitives
Add new flag to MAC flags field
MAC must handle new address information
Everything else is transparent

## Slide 30
IEEE 802.15.4 MAC
PURL NWK
(ZigBee)
PURL DLC
(ZigBee)
IEEE 802.2
LLC, Type I
IEEE 802.15.4
915/2400 MHz
PHY
IEEE 802.15.4
868/915 MHz
PHY
Mesh NWK
(Motorola)
Other NWK
Application Convergence Layer (ACL)
(ZigBee)
Maintained by
IEEE 802.15.4
Maintained by
ZigBee
Working Group
Low Rate Stack Architecture
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 31: Conclusions
Cluster tree uses both star & peer-peer
Do not use BEACON packet
Minimal changes to MAC
DLC layer is the same
Use DLC layer handshake mechanism
Implement commands in the NWK layer