## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Physical Layer proposal for the 802.15.4 Low Rate WPAN Standard]
Date Submitted: [July 2001]
Source: [Carl R. Stevenson] Company: [Agere Systems]
Address: [555 Union Boulevard, Room 22W214EQ, Allentown, PA 18109]
Voice:[(610) 712-8514], FAX: [(610) 712-4508], E-Mail:[carlstevenson@agere.com]
Re: [ PHY layer proposal submission, in response of the Call for Proposals ]
Abstract: [This contribution is a PHY proposal for a Low Rate WPAN intended to be compliant with the P802.115.4 PAR. It is based on proven, low risk technology, which can be implemented at low cost and can provide scaleable data rates with robust performance and low power consumption for low data rate, battery-powered devices intended to communicate within the 10m “bubble” which defines the PAN operating space. NOTE: Total area and power estimates are based on Agere’s previous MAC proposal and will be substantially less when this PHY is combined with the “unitfied MAC” proposal.)]
Purpose: [Response to IEEE 802.15.4 TG Call for Proposals]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
PHY Layer Proposal Submission to the IEEE P802.15.4 Low Rate WPAN Task Group

## Slide 3: Who is ?
Formerly Lucent Technologies Microelectronics Group
In the process of spinning off as an independent semiconductor company
Extensive experience in communications IC design, DSPs, and wireless systems design

## Slide 4: Description of Physical Layer Proposal
System Operation
  Orthogonal BFSK modulation (modulation index = 1)
    Robust operation with low complexity (good Eb/No performance possible)
    Proven, high performance all-digital modem possible (though conventional modulators/demodulators could be used)
  Operating frequencies
    2400-2483.5 MHz (unlicensed operation)
      ~244 channels, 320 kHz spacing @ 160 kbps
      Low IF architecture with upper/lower sideband select keeps LO and image in-band - fewer out of band spurious issues
      Other bands possible with minor changes (where is the ?)
  Operates under FCC Part 15.249 rules
    Not SS - uses DCS “Dynamic Channel Selection”
      Coordinator node “sniffs” band and selects channel(s)
      Slave nodes find coordinator by scanning for beacons
      Network moves to a clear channel in case of interference

## Slide 5: Description of Physical Layer Proposal
System Operation (cont.)
  Image-reject up/down conversion between low IF and RF
    Proven techniques provide good performance
      Avoids 1/f noise problems in CMOS
      Avoids DC offset and linearity problems of direct conversion (RX IF can be AC-coupled and hard limited)
    Minimizes amount of high frequency circuitry, allowing majority of signal processing to take place at very low frequencies in simple digital circuitry
      Reduces total power consumption
        Low frequency digital CMOS is power efficient
      Reduces chip area
        Small geometry digital CMOS is compact
      Reduces total solution size
        Integration of filters, etc. allows single chip solution with only minimal external passives (bypass caps, etc.)
      Significant portions of system synthesizable from VHDL

## Slide 6: Description of Physical Layer Proposal
System Operation (cont.)
  All system timing and frequency generation are based on a single master oscillator in each node
  Slaves track frequency of coordinator
    Proven techniques provide good performance
      Allows use of low cost, low precision crystals
      Slaves adjust their master oscillator (or synthesizer reference frequency) such that received signal is centered in their receive IF and recovered symbol timing is correct
      Alignment takes place as “slaves” join network
      Once initial acquisition is complete, tracking is based on fine corrections in recovered symbol clock
      Typical tracking in a real, commercially-produced system is equal to or better than 1 ppm with 50 ppm crystals
        This equates to about 2.5 kHz worst-case offset at Fo of 2.5 GHz, which results in negligible performance loss
  Range/margin stated in this proposal are based on -2 dBm nominal TX power output (with duty cycle averaging allowance ~ + 18 dBm is possible)

## Slide 7: Simplified Transceiver Block Diagram (does not show all control and power management signal details)

## Slide 8: Spectrum of All-digital Modulated TX Signal at 1.360 MHz Low IF (unfiltered)

## Slide 9: Response of 5 pole Butterworth Filter with 280 kHz BW at 1.360 MHZ

## Slide 10: Spectrum of Modulated TX Signal at 1.360 MHz Low IF (filtered)

## Slide 11: Spectrum of Modulated TX Signal at 1.360 MHz Low IF

## Slide 12: Spectrum of Modulated Signal Image-reject Upconverted to 71.36 MHz (to demonstrate image rejection - lower Fo used to reduce simulation time)

## Slide 13: Spectrum of Modulated Signal Image-reject Upconverted to 71.36 MHz (less resolution than low IF simulation due to FFT size at higher Fo)

## Slide 14: SimplifiedTransceiver Block Diagram (does not show all control and power management signal details)

## Slide 15: Measured Receiver Performance of a Similar System Using Agere’s All-Digital FSK Demodulator

## Slide 16: 5-th Order Complex Filter: Block Diagram and Pole Location
C_Z(s)
pole 1
+
_
+
_
C_Z(s)
pole 2
+
_
+
_
C_Z(s)
pole 5
Current input
(directly from
the mixers)
X
X
X
X
X
X
X
X
X
X
o
o
o
o
o
1.360
MHz
1
2
3
4
5
complex filters can also provide channel selectivity i.e.
suppress adjacent channels (similar to a regular BP filter)
NOTE: The actual design is fully-differential

## Slide 17: Measured Image Rejection in Actual Implementation Exceeds 40dB
signal
image
These two tones at the input
of the filter have the same
magnitude

## Slide 18: Die Size Estimate - Total Solution (PHY + MAC + Misc)
NOTE: Area estimates for MAC and total die size are based on the previous Agere Systems MAC proposal and will be reduced substantially when the Agere Systems PHY is combinted with the “unified MAC” proposal.

## Slide 19: Power Consumption Estimate - Total Solution (PHY + MAC + Misc)
NOTE: Total Power estimates are based on the previous Agere Systems MAC proposal and will be reduced according to MAC behavior if the Agere Systems PHY is combinted with the “unified MAC” proposal. The PHY proposed can make use of a number of power manaaagement modes, depended on support from the MAC and application layers.

## Slide 20: Link Budget, Receiver Performance, and Link Margin – LP IFE

## Slide 21: Link Budget, Receiver Performance, and Link Margin – LP DFE

## Slide 22: Link Budget, Receiver Performance, and Link Margin – HP DFE

## Slide 23: General Solution Criteria
CRITERIA
REF.
VALUE
Unit Manufacturing Cost ($)
2.1
Based on area estimates + SOC mplementation, total system cost, including PHY, MAC, LLC & simple application est. to be ~ $1.00-$1.50
Interference and Susceptibility
2.2.2
Intermodulation Resistance
2.2.3
Jamming Resistance
2.2.4
Source 1: ~ -30 dBm (DCS avoids microwave)
Source 2: ~ -30 dBm (future BT AH assumed)
Source 3: ~ -30 dBm (DCS avoids 802.11b)
Source 4: ~ -30 dBm (DCS avoids 802.15.3)
Interoperability
2.3
FALSE – does not interoperate with other systems over the air, but can connect to other systems via a gateway provided by a node.
Time to Market
2.4.2
Depends on finalization of the 802.15.4 spec.
PHY solution proposed is based on proven technology which has been used in existing products which have been shipping for 2-3 years.
In-band (see Jamming Resistance)
Out of band ~ -30 dBm (P1dB - 10 db - FE filter)
IIP3 ~ -10 dBm (higher level posible with some increase in current consumption)

## Slide 24: General Solution Criteria (cont.)
CRITERIA
REF.
VALUE
Regulatory Impact
2.4.3
FALSE – proposed PHY solution complies with existing rules for low power unlicensed devices
Maturity of Solution
2.4.4
Proposed system is based on substantial reuse of existing, proven technology which has been in high volume production for several years
Scalability
2.5
Basic concept can be scaled to other data rates, frequency bands, number of channels, etc.
Location Awareness
2.6
Not supported in terms of measuring relative locations in cm … RSSI and time of arrival techniques can only provide limited information
Application Dependent Power Consumption
2.7
MAC Behavior Dependent – see preceeding tables on power consumption vs. duty cycle

## Slide 25: PHY Protocol Criteria
CRITERIA
REF.
VALUE
Size and Form Factor
4.1
Frequency Band
4.2
Number of Simultaneously Operating Full-Throughput PANs
4.3
Signal Acquisition Method
4.4
Range
4.5
Sensitivity
4.6
Power level: -96 dBm
PER: dependent on packet size
BER: 10e-4
Delay Spread Tolerance
4.7.2
TRUE
FALSE
Power Consumption
4.8
CMOS SOC flip-chip approx. <<9mm^2, plus a few passives (bypass caps, etc.) << compact flash
2.4 GHz ISM band for global availability, variants could be designed for other bands (e.g. 900 MHz)
At least 15, assuming 16 channel spacing and no interference from other systems – perhaps more, depending on RX dynamic range/power tradeoffs
Nodes track to frequency of coordinator’s beacon, adjusting their local references to achieve and maintain frequency and timing sync
>= 10m with >= 28 dB fade margin to 10e-4 BER
TX & RX Peak: ~ 68.75 mW (100% duty cycle)
Average power duty cycle dependent – see table