## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: PHY Proposal for the 802.15.4 Low Rate Standard
Date Submitted: 12 March, 2001
Source: Pat Kinney Company: Invensys
Address: Forrest Hills, PA
Voice 412-225-8242, E-Mail:pat.kinney@ieee.org
Re: Call for Proposals for Low Rate PHYs
Abstract: Proposal for a Low Cost, Low Rate PHY
Purpose: For consideration as the PHYof the 802.15.4 standard.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: 802.15.4 Low Rate PHY Proposal Overview
Pat Kinney
Invensys Metering Systems
pat.kinney@ieee.org

## Slide 3: Changes Since Last Presentation
This proposal has been modified since the prior presentation to enhance its performance and to provide a more “consolidatable” proposal.

## Slide 4: Objectives
Very Low Cost
  Minimal complexity of implementation
  Minimal filters, tolerant of VCO noise
  Good candidate for SOC
Performance
  Robustness to interference, multipath,
Low current drain
  Very fast acquisition times (5-10 chips)
  minimal correlator decorrelator

## Slide 5: Features of this Proposal
Ability to alter data rate for range
Very low complexity for modulator and demodulator
Exceptionally fast acquisition times
Spread spectrum allows possibility of higher transmit powers

## Slide 6: Implementation Overview
Spread Spectrum
Frequency Range: 2.4 GHz
  other bands are possible
Modulation method: QPSK
Data Rate: 10.47, 115.2 kb/s
  other data rates are possible
Transmit Power Level: 1 mW
  higher is possible, but as per 15.247

## Slide 7: Implementation Overview
Spread Spectrum
  Direct Sequence, Transmitted Reference
    Two orthogonal channels, I&Q
    I channel carries spread data
    Q channel carries only the spreading function
    Delay in the Q channel allows for O-QPSK
    Receiver merely multiplies the I against the Q to recover the data
  Direct Sequence, Optional Low Rate
    use of 8bit Hadamard/Walsh or 11 bit orthogonal code to reduce 115.2 kb/s to 12.6 or 10.47 kb/s with enhanced range

## Slide 8: Implementation Overview
Benefits
  Doesn’t require the receiver to “know” the PN sequence of the transmitted signal
  Doesn’t require the receiver to synchronize timing between the received signal and its internal clock
  Reduces
    acquisition time,
    correlator complexity
    current drain of the correlator
    demodulator complexity

## Slide 9: Architecture
Rcvr FE
Xmit BE
Spreader
MAC
Host
Interface
Despreader
Frequency
Generators
PN
Generator
PMD
PLCP
Demodulator
Antenna
Modulator
MAC

## Slide 10
PN Generator
Programmable feedback
Programmable restart interval
Programmable restart vector
~2% of ASIC area
Feedback select
Restart control
PN Code
Control
8-bit shift register

## Slide 11
Modulator/Spreader
Manchester
Encoder
0
1
TX Data
PN Code
Delay
TXI
TXQ
Programmable delay (½ to 7½ chips)
Optional Manchester encoder
~4% of ASIC area
Control

## Slide 12
Despreader
RXI
RXQ
A
B
Programmable delay (½ to 7½ chips)
~23% of ASIC area
Control
Delay
Delay

## Slide 13
Demodulator


A
B

Clock
Recovery
RX Data
RXDCLK
Optional Manchester decode
~40% of ASIC area
Control

## Slide 14
Low Rate Demodulator
11 bit shift register
Rx Data
Rx Data Clock
Compare
Compare
Code for logic one
Code for logic zero
Data Correlator
Timing Recovery
Code for logic one
Code for logic zero
Low Rate Data
Low Rate Data Clock

## Slide 15: PHY Parameters

## Slide 16: PHY Parameters

## Slide 17: Summary
Very Minimal Complexity
Ability to trade off range for data rate
Very short acquisition times