## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Security proposal for the High Rate 802.15.3 Standard]
Date Submitted: [10 Jul, 2001]
Source: [Gregg Rasor] Company [Motorola, Inc.]
Address [1500 Gateway Blvd., MS100, Boynton Beach, Florida 33426, USA]
Voice:[(561)739-2952], FAX: [(561) 739-3517], E-Mail:[gregg.rasor@motorola.com]
Re: [Doc. IEEE 802.15-01/054r0, Doc. IEEE 802.11/00-362, Draft P802.15.3/D0.5]
Abstract: [This presentation represents Motorola’s proposal for the P802.15.3 Security standard, describing the components of a secure low cost high rate WPAN system.]
Purpose: [To provide a baseline proposal for 802.15.3 MAC Security clause]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Security Proposal for the High Rate 802.15.3 Standard
Gregg Rasor, Member of the Technical Staff
Motorola Personal Communications Sector
Phone: +1-561-739-2952
Fax: +1-561-739-3715
gregg.rasor@motorola.com

## Slide 3: Security Options for 802.15.3
Introduction and Goals
Information Security Basics
A Simple, Extensible Security Protocol
Security Related Clauses in Draft P802.15.3/D0.5

## Slide 4: Introduction
802.11 wireless “security flaws” exposed:
  In February 2001, Borisov et. al. (UC Berkeley) published the paper titled Intercepting Mobile Communications: The Insecurity of 802.11. Several attacks on WEP were discussed.
  Jesse Walker presented in doc. IEEE 802.15/01-154 evidence that 802.11 TGe knew about most of the published attacks (see doc. IEEE 802.11/00-362).
  What followed were attacks from industry publications on the existing WEP standard.

## Slide 5: Goals
Review historical approaches for the secure exchange of information.
Define the scope of our task by analyzing at least the trade-offs between system cost, complexity, and power use versus the risk of implementing a security protocol that is either too strong (that can never happen) or too weak.
Finally, establish a baseline approach for an effective overall network security model.

## Slide 6: Security Options for 802.15.3
Introduction and Goals
Information Security Basics
A Simple, Extensible Security Protocol
Security Related Clauses in Draft P802.15.3/D0.5

## Slide 7: Information Security Basics
If you are curious about cryptography, buy the book “Applied Cryptography.” It is an excellent reference and reads like a novel.
Cryptographic protocols: these are basically agreements between parties that want to securely exchange information. Such protocols make use of ciphers, keys, and other cryptographic mechanisms to insure data integrity and provide authentication.

## Slide 8: Information Security Basics 802.11 Security Today
Goals of existing 802.11 security
  Create the privacy achieved by a wired network.
  Prevent casual eavesdroppers from intercepting and interpreting the “protected” information.
  Simulate physical access control by denying access to unauthenticated stations.
Existing security consists of two subsystems
  A data encapsulation technique called Wired Equivalent Privacy (WEP).
  An authentication algorithm called Shared Key Authentication.

## Slide 9: Information Security Basics 802.11 Security Today
Status of existing 802.11 security
  Data encryption by itself offers no protection from attack
    there is no meaningful privacy if the data authenticity problem is not solved (you don’t know who sent the data!)
    “It’s [supposed to be] access control [but is isn’t], stupid”
  It is profoundly easy to mis-use a cipher
    “don’t try this at home”
    Any good cryptographic scheme must be peer reviewed by professional cryptographers.
Excerpted from IEEE 802.15/01-154, presented by Jesse Walker in February, 2001

## Slide 10: Information Security Basics Symmetric Key Cryptosystem
Plaintext
011001010
Ciphertext
?????????
Plaintext
011001010
Locking Key
(Encryption)
Unlocking Key
(Decryption)

## Slide 11: Information Security Basics Public Key Cryptosystem
Plaintext
011001010
Ciphertext
?????????
Plaintext
011001010
Public Key
(Encryption)
Private Key
(Decryption)
One Way

## Slide 12: Information Security Basics Public Key Cryptography
  Encryption and decryption allow two communicating parties to disguise information they send to each other. The sender encrypts, or scrambles, information before sending it. The receiver decrypts, or unscrambles, the information after receiving it. While in transit, the encrypted information is unintelligible to an intruder.
  Tamper detection allows the recipient of information to verify that it has not been modified in transit. Any attempt to modify data or substitute a false message for a legitimate one will be detected.
  Authentication allows the recipient of information to determine its origin--that is, to confirm the sender's identity.
  Nonrepudiation prevents the sender of information from claiming at a later date that the information was never sent.

## Slide 13: Public-Key Cryptographic Schemes
There are 3 major families of public-key schemes:
  Discrete logarithm schemes (e.g. Diffie-Hellman, DSA)
  RSA
  Elliptic curve cryptosystems (ECC)
The security of each of these 3 families lies on the difficulty of some mathematical problem. The problem underlying the security of ECC is much harder than the problem for RSA. Thus ECC offers the same security as RSA but with significantly smaller key sizes.
Example: 163-bit ECC is equivalent to 1024-bit RSA.
Example: 256-bit ECC is equivalent to 3078-bit RSA.

## Slide 14: ECC Standardization
ECC has been widely standardized by accredited standards organizations including:
  IEEE (1363-2000)
  ANSI (X9.62, X9.63)
  ISO/IEC (14888-3, 15496,…)
  NIST (FIPS 186-2)
In particular, FIPS 186-2 specifies the elliptic curve digital signature algorithm (ECDSA). This specification is compliant with all the other ECC standards, and is recommended for US federal government use.

## Slide 15: Advantages of ECC
The smaller key sizes for ECC results in:
  Faster computations
  Bandwidth savings (smaller keys, certificates and signatures)
  Lower power consumption
These advantages can be especially advantageous in environments where any of the following are constrained;
  Processing power
  Bandwidth
  Power source
The advantages become even more pronounced as we move to stronger security levels for long-term security.

## Slide 16: Other Advantages of ECC
In RSA, the key generation process is quite cumbersome since each party has to generate two large random prime numbers.
In ECC, all parties in a network share the same set of domain parameters (an elliptic curve and a generating point G on the curve). Key pair generation simply involves selection of a random integer k and then computation of the point Q=kG.

## Slide 17: Long-Term Security
Flexible hardware can be build to allow for different key sizes for long-term security. This is especially important as security standards are starting to move towards AES key sizes.

## Slide 18: Comparative Timings on a Palm Pilot

## Slide 19: Security Options for 802.15.3
Introduction and Goals
Information Security Basics
A Simple, Extensible Security Protocol
Security Related Clauses in Draft P802.15.3/D0.5

## Slide 20: A Simple Security Protocol
Our first task is to define a set of rules for the exchange of information required to communicate information in either plaintext or encrypted form. The following example illustrates a simple, extensible cryptographic protocol.

## Slide 21: A Simple Security Protocol
Rule 1 – negotiate a connection between devices and identify the “data stream” properties, e.g., plaintext or encrypted.

## Slide 22: A Simple Security Protocol
Rule 2 – if the data stream is encrypted, exchange cryptographic set-up information.

## Slide 23: A Simple Security Protocol
  Risk – if cryptographic set-up information is exchanged in the clear (as plaintext), an eavesdropper can easily determine the parameters necessary to decrypt your “secure” information. Typically, cryptographic set-up information conveys parameters that are used to generate a “session key” which is applied, through a cryptographic algorithm, to encrypt and decrypt information. In a perfect world, once a session key is established, secure communication can take place indefinitely. However, given enough time and processing horsepower, most cryptographers consider breaking the system described above akin to child’s play!

## Slide 24: A Simple Security Protocol
  Solution – (one of many) public key cryptosystems mitigate this risk by encrypting the session key based on a user’s public key. This avoids requiring apriori knowledge of a shared secret key that may be compromised or deduced. However, each user must generate a private - public key pair, distribute that public key to all users (or a public key server) and each user must have apriori knowledge of any other possible user(s) public key in order to establish secure communication between users.

## Slide 25: A Simple Security Protocol
  This solution avoids the requirement for a master authentication server such as used with many enterprise systems (e.g., RADIUS). However, when implemented in conjunction with a combined public key server / certificate authority, it is possible to certify each possible member of a network (establish who they are) and establish trust relationships between both inter- and intra- network devices and networks, just like an enterprise system. Note that a masquerade attack by cloning is still possible.

## Slide 26: A Simple Security Protocol
  Accordingly, careful selection of the parameters on which the private and public keys are based is important! Parameters used to generate a private and public key pair are (in RSA) two “large” relatively prime pseudorandom numbers. In ECC, key pair generation simply involves selection of a random integer k and then computation of the point Q=kG. A passcode is used in conjunction with the private key to decrypt messages encrypted using a user’s public key and their passcode.

## Slide 27: A Simple Security Protocol
  The passcode should be based in part on the foundry assigned MAC address associated with each 802.15.3 device. In that way, just knowing the MAC address will not be enough information to clone a device and breach a secure network.

## Slide 28: A Simple Security Protocol
  The harder question is which other piece of unique information is combined with the MAC address to produce the passcode. Selection of this parameter will set the security level of this system.
  To further insure constant security, the session key must be periodically (or preferably aperiodically) changed. Session keys must have a finite, short lifetime.

## Slide 29: A Simple Security Protocol
  Rule 3 – once cryptographic set-up information is exchanged, determine network membership status based on an authentication algorithm controlled by the master.

## Slide 30: A Simple Security Protocol
  There must be a way to operate the system in a “wildcard” mode (all devices are investigated and admitted if allowed) for network initialization and establishment, as well as in cases where brute force re-initialization is required.
  The problem with operating in a wildcard mode is how do we determine (at a piconet coordinator [PNC]) which devices to permit as a network member, without over complicating the task.

## Slide 31: A Simple Security Protocol
  Shared secrets such as used in 802.11 (network name and cryptographic key) are not secure in most cases. Thus, they should be avoided.
  Public key systems allow a WPAN device to generate a public key that can be shared without significant risk.

## Slide 32: A Simple Security Protocol
  To prevent a breach of security based on a playback attack, each device that configures a secure data stream must be required to authenticate when joining a network, and at aperiodic intervals thereafter.
  A self synchronizing stream cipher (risk: vulnerable to playback attacks) should be used rather than a block cipher (AES). This allows devices that miss a portion of a broadcast message to recover without having to request retransmission of a complete encrypted data block.

## Slide 33: Security Options for 802.15.3
Introduction and Goals
Information Security Basics
A Simple, Extensible Security Protocol
Security Related Clauses in Draft P802.15.3/D0.5

## Slide 34: Security Related Clauses in Draft P802.15.3/D0.5
5.6.2 Joining
A station desiring to join an 8 2.15.3 WPAN will set its receiver to periodically listen on the various PHY channels for a beacon. If the beacon indicates a network of interest to the station,it will attempt to authenticate with the coordinator. Upon success,it is considered to be in the WPAN.The station may receive a secret key during authentication which can be used to encrypt data. It will also exchange capability information with the coordinator. This capability information includes all the PHY data rates supported by the station, its power management status (whether it needs to power management or not) whether the station can be a coordinator,buffer space,etc. As a result of this exchange,a coordinator handover may occur.

## Slide 35: Security Related Clauses in Draft P802.15.3/D0.5
6.7.1.3 Security Services
NOTE: This clause needs definition.
6.7.2.2.1 When generated
The MA-UNITDATA.indication primitive is passed from the MAC sublayer entity to the LLC sublayer entity or entities to indicate the arrival of a frame at the local MAC sublayer entity. Frames are reported only if they are validly formatted at the MAC sublayer,received without error, received with valid security properties according to the security policy at the local MAC sublayer entity, and their destination address designates the local MAC sublayer entity.

## Slide 36: Security Related Clauses in Draft P802.15.3/D0.5
7.2.1.1 Frame control field
The Frame Control field consists of the following sub-fields: Protocol Version,ACK policy, Frame Type, Frame Position, Frag-start, Frag-end, retry, Del-Ack request, SECurity and Repeater. The format of the frame control field is illustrated in Figure 4.
7.2.1.8 Frame body field
The frame body is a variable length field and contains information specific to individual frame types. The minimum frame body is zero octets. The maximum length frame body is 2 3 octets,including the security information,if any.
7.4 Information elements

## Slide 37: Security Related Clauses in Draft P802.15.3/D0.5
7.4.7 Security parameters element
<TBD>
7.5.12 Stream Management
…
The security is a 3-bit field <TBD>
8.1.4 Authentication
Authentication is described in clause 10.
10. Privacy and Security