## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: IEEE802.15.3: Overview of Power Save Proposal.
Date Submitted: 09 July, 2001
Source: Jay Bain Company: Time Domain
Address: 7057 Old Madison Pike
Voice: 256 922 9229 , FAX: 256 922 0853, E-Mail: jay.bain@timedomain.com
Re: [ ]
Abstract: This provides an overview of proposed incorporations in the draft standard relating to power management.
Purpose: To provide information and solicit comments on proposed power management
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15

## Slide 2: Overview of MAC Power Save
Provide the protocol structure that will allow a range of applications the greatest opportunity to save power.

## Slide 3: Possible operating scenarios
The mode with greatest power saving is OFF!
If off won’t do -- Associate with a network and then:
  Take advantage of characteristics of contention free period – reduce power in slots not assigned to a device. (RPS)
  Take advantage of higher layer inactivity - reduce power by skipping several beacons and superframes. (EPS)

## Slide 4: The enemies of power saving
Constant high throughput requirements.
Time to progress from startup to data movement.
Failure by higher layers to correctly structure requirements for service
Real characteristics of PHY and MAC
Poor environmental conditions resulting in lost packets and use of lower transmission rates

## Slide 5: RPS Operation
PNC may be an RPS device
Stay awake for
  Beacon
  CAP
  Assigned receive slot
  Assigned send slot with activity
Consider receive slot as empty after 25% of duration
Slot location
  Higher layers make realistic RPS QoS requirement known to device
  PNC required to make best effort to locate assigned slot nearest beacon
Contention
Access
Period
Beacon
Contention Free Period
Assigned
Slot
Assigned
Slot
Period of Reduced Power Opportunity
Notes: Slot location is a consideration. It would be an advantage for a RPS device to have a single cycle of activity rather than multiples. Real systems are expected to require time to return from a reduced power state.
A realistic RPS QoS requirement is key to obtaining desired results. Higher layers inform the RPS device of power restrictions and also of a matching scenario of information expected to be exchanged while in an RPS mode of operation.

## Slide 6: Rundown of EPS slides
Skipped superframes
Beacon content for EPS support
Data exchange with a EPS receiving device
Association timeout
Repeater service in EPS

## Slide 7: EPS Operation – skipped superframes
Beacon
Contention Free Period
Assigned
Slot
Beacon
Opportunity to reenter EPS
Beacon
PNC Generated Superframes
Wake to beacon –
no traffic
Indicated
Wake to beacon -
Traffic Indicated
Receive/ack data

## Slide 8: Beacon Content for Support of EPS
EPS information element (new)
  EPS devices each have a block (multiple sources require additional blocks)
  RPS PNC provides all piconet devices a block
Agent between sending and receiving devices (yellow) –
Current (1 bit) – indicates new data
Acked (1 bit) – indicates that an ack on previous data was received
More (1 bit) – indicates that at least one additional packet is queued behind the current packet.
Active (1 bit) – set by sending dev to indicate that it is actively updating the current, acked, and more and fields. If reset the three fields have no meaning and they are no longer valid.
Indicator gauge for association timeout (blue) –see later slide
Current
Seq. No.
Association
Timeout Gauge
Acked
Seq. No.
1 Octet
Active
Update
More
follows
Reserved
Sender controlled
PNC controlled
Destination Device ID
1 Octet

## Slide 9: Sender-PNC-EPS device diagram
Source
PNC
EPS Destination
Traffic Command
Traffic Ack
Beacon is
Second chance
Message in
Assigned slot
(short retry timer)
Receive Beacon
Receive traffic
Ack traffic
Missed Beacon
Missed Beacon
Missed traffic
Missed traffic
Traffic Command
Traffic Ack
Update Beacon
Wake
EPS
EPS
Update Beacon
Message
Repeat
Message
Repeat
B
B
B
B

## Slide 10: Association Timeout Operation
Based on aAssociationTimeoutPeriod parameter (7.3.5 in 0.4 draft). Originated by higher layer
Communicated to PNC by all devices
Related to all devices via gauge in beacon
device responsibility to re-initialized
Applies to active, RPS, and EPS devices
Allows PNC to be an RPS device and not listen to every slot
OK
Retry
Aggressive
retries
00
01
10
11
Gauge
operation
Disassociated

## Slide 11: Repeater Considerations
Use repeater in normal manner as piconet coverage enhancer.
Add use of repeater for EPS sender to EPS receiver operation.
EPS sender to active or RPS destination should not use repeater service (except as coverage enhancer)

## Slide 12: Where is the Beacon?
Consideration of Beacon change (new superframe length) –
  Don’t change the superframe length if not truly beneficial to traffic requirements
  If it does change, the EPS device stays on to find the beacon – if once in a long while event, not a problem.
Clock drift calculation and leading of nominal beacon time is EPS device responsibility

## Slide 13: QoS Aspects for RPS/EPS
Higher layers determine the latency of the EPS device waking for a beacon
Higher layers don’t ask for more than needed
Divide into multiple streams for persistant low rate control and non-persistent QoS data

## Slide 14: MAC to PHY communications
Taking James Gilb suggestion
Table of power save options in PHY sent to MAC. Content is time to return to normal operation.
MAC chooses the appropriate table index for each power down command to PHY.
MAC sends power on command to return the PHY to normal mode.