## Slide 1
Slide <number>
<footer>
<date/time>May 2001
Project: IEEE 802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [TG3 TG4 Joint MAC Discussion]
Date Submitted: [12July01]
Source: [John Barr] Company [Motorola]
Address [1303 E. Golf Road, Schuamburg, IL 60196]
Voice:[+1 847 576-8706], FAX: [+1 847 576-6758], E-Mail:[John.Barr@Motorola.com]
Re: [01277r3P802-15_TG3-July01-Meeting-Objective-and-Agenda.xls]
Abstract: [TG3 TG4 Discussion Slides]
Purpose: [Facilitate discussion between TG3 and TG4 MAC proposers.]
Notice: This document has been prepared to assist the IEEE 802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by 802.15.

## Slide 2: IEEE 802.15 Working Group for Wireless Personal Area Networks
TG3 TG4 Joint MAC Discussion
July 2001, Portland, OR
USA
802.15

## Slide 3: Agenda
Compare/Contrast TG3-TG4 MACs
Any common features?
LLC approach
Possible joint work

## Slide 4: References
01/272r3 – TG4 Unified MAC Proposal
01/229r2 – TG4 Motorola PHY Proposal
D0.5P802-15-3 – Draft Standard
01/223r3 – TG3 Publicity Presentation
01/188r1 – TG4 Mediation Device Operation
01/189r0 – TG4 Cluster Tree Networks
01/157r4 – TG4 Criteria Document

## Slide 5: Data Packet Structure
PRE
SFD
LEN
MFL
CRC
Link Layer PDU
ADDRESSING
Preamble sequence
SFD, one for each packet type
Length for decoding simplicity
Flags specify addressing mode
Addresses according to specified mode
CRC-8/16, depending on the LPDU size

## Slide 6: Optional Super Frame Structure
15ms
Network
beacon
Contention
period
Beacon
extension
period
Slot 3
Slot 2
Slot 1
Allocated
slot
Transmitted by distribution nodes. Contains network information,
super frame structure and notification of pending node messages.
Space reserved for beacon growth due to pending node messages
Access by any node using CSMA-CA
Reserved for nodes requiring guaranteed bandwidth.

## Slide 7
IEEE 802.15.4 MAC
NWK A
IEEE 802.15.4 LLC
IEEE 802.2
LLC, Type I
IEEE 802.15.4
915/2400 MHz
PHY
IEEE 802.15.4
868/915 MHz
PHY
NWK B
NWK C
Application Convergence Layer (ACL)
Maintained by
IEEE 802.15.4
Maintained by
ZigBee
Working Group
Low Rate Stack Architecture
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 8: IEEE 802.15.3 MAC Layer Overview
Contention Access Period
(CAP)
Guaranteed Time Slots
(GTS)
BEACON
BEACON
...
...
Superframe
WPAN
Parameters
Small command/control functions
Duration can change depending on Isochronous demands
Pre-assigned start times allow Sleep modes
Isochronous data streams:
Standard definition MPEG2, 4.5 Mbps
High definition MPEG2, 19.2 Mbps
MPEG1, 1.5 Mbps
DVD, up to 11 Mbps
CD Audio, 1.5 Mbps
AC3 Dolby digital, 448 Kbps
MP3 streaming audio, 128 Kbps
Asynchronous data transfers:
Image files
MP3 music files
(All multi megabyte files)
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 9: Conclusions
Target markets are quite different.
Bridging methods may be appropriate
Investigate common interfaces in the LLC
Identify system requirements where combination would apply
Set aside time at joint August 28-9 ad-hocs to address ideas
Make sure TG3 and TG4 coexist
Is there any MLME or PLME commonality?
Can TG3 adopt the TG4 network concepts?