## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Slot Cycle TDMA Overview
Date Submitted: [16 January 2001]
Source: [Mark E. Schrader] Company [Eastman Kodak Company]
Address [4545 East River Road, Rochester, New York 14650-0898]
Voice:[716-781-9651], FAX: [716-781-9733], E-Mail:[mark.e.schrader@kodak.com]
Re: []
Abstract: An access method based on TDMA is shown that manages access to a WPAN through cycles of time slots that are self timed by the joined stations. The method uses a Coordinator for join and periodic resynchronization via a beacon. The method uses minslots and variable length data slots, whose quantized size is specified in the PLCP header. The system is straight forward, efficient, and adaptable to various hidden node mitigation techniques.
Purpose: This is presented as basis for understanding the SC-TDMA protocol and a basis for writing the full WPAN specification Clause 9,
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: 802.15.3 MAC Clause 9
Sub-clause: Slot cycle TDMA

## Slide 3: Outline
Overview of Slot Cycle TDMA
Comparison to standard TDMA with respect to QoS
Message structure differences
Example sequences
Self timing methodologys
Hidden node problem issues

## Slide 4: Slot Cycle TDMA Overview
It is a Time Division Multiple Access method.
Primary mode is peer-to-peer.
One station at any one time is a coordinator.
Join & Unjoin are via the coordinator.
The coordinator assigns time slot cycles based on requested QoS.

## Slide 5: Slot Cycle TDMA Overview continued...
Time slots are timed by each joined station simultaneously, with the coordinator serving as beacon generator/synchronizer.
Each station transmits during its assigned slot cycle (or cycles).
Stations listen before transmitting in their slot cycle.
An unused slot cycle, minislot, has minimal length.

## Slide 6: Slot Cycle TDMA Overview continued...
A utilized slot cycle is variable length, depending on the message sent and the ACK/reply required.
The coordinator broadcasts a periodic beacon.
Beacon signals the contention period for a join request or small peer-to-peer transmission.

## Slide 7: Join Process & Timing
Unjoined station responds to beacon with a request to join.
Coordinator will ack, otherwise unjoined station uses random backoff and retry to re-request.
Coordinator responds in its next beacon with the slot cycle data for join accept, or a join decline if the requested QoS is not available.

## Slide 8: Join Process & Timing continued...
Joined station uses: total slots per cycle, total cycles in assigned slot, and time quantization value, Tq, to time the minislots, utilized slots (Async. or Isoc. data), and the beacon.
Tq is an integer number of symbol periods.

## Slide 9: Compare Slot Cycles with Standard TDMA

## Slide 10: QoS With Standard TDMA

## Slide 11: QoS With Standard TDMA continued...
Summary:
As new stations are added to a fixed TDMA system, existing isochronous mode stations must be assigned additional slots in order to have their QoS requirements met.

## Slide 12: Slot Cycle TDMA
Cycles
Slots

## Slide 13: Slot Cycle TDMA
Cycles
Slots

## Slide 14: Primary Slot Cycle Types
BEACON: Not a slot cycle. A broadcast by the master at fixed intervals, superceding all slots.
MINISLOT: An unutilized slot cycle. It is only about 3% to 6% as long as a slot in which data is sent. Also called an access window.
ISOCHRONOUS DATA SLOT: Always has a QoS constraint and may or may not require an ACK.

## Slide 15: Primary Slot Cycle Types continued...
ASYNCHRONOUS DATA SLOT: Signifies a slot cycle with time for an ACK from the recipient. QoS is assumed not as critical as isochronous.

## Slide 16
PLCP
RxTx
ACK
PLCP
SIFS
Payload
PLCP
RxTx
SIFS
PLCP
JREQ or CPData
Asynchronous
Isochronous
Beacon
PLCP
RxTx
SYNC
HNT
Mslot
Minislot
ACK
PLCP
Message Structures
Payload
Notes: PLCP is PLCP preamble + PLCP header HNT is time to DIT/CSO for hidden nodes, CPData is small, fixed size payload.
HNT
HNT

## Slide 17: Example Slot Cycle Sequence
3
1
2
Cycle 4
3
1
2
Cycle 5
1
2
3
1
2
3
1
2
3
1
2
3
1
1
2
3
Cycle 6
Join
Beacon
Minislot
Payload
Isoc. Payload
Cycle 10
Cycle 7
Cycle 9
Cycle 1
Payload
Cycle 8
Preamble
1
3
2
2
3
2
2
1
1
1
Cycle 1
Cycle 2
3
Cycle 3
3

## Slide 18: Self Timing Overview
Time is quantized. The basic unit of time, Tq, is symbol clock divided by a power of 2 (TBD).
The interval from Beacon to the first access window is a constant multiple of Tq, used by all joined stations for synchronization.
The Minislot width, Taw, is a constant known to all stations. Taw is counted modulo Nslots.

## Slide 19: Self Timing continued...
Each station assigned a slot, k, counts occurrences of slot k modulo Mk, the total number of cycles assigned to that slot by the coordinator.
The multiple of Tq received in the PLCP header is used to time the duration of the current slot cycle to the beginning of the next access window.
Each beacon, Minislot, Isoc. message time or Async. message time is an integer multiple of Tq.

## Slide 20
Elements Related to Self Timing
3
3
2
2
2
1
1
1
Cycle 1
Cycle 2
3
Cycle 3
1
2
Cycle 4
3
3
1
2
Cycle 5
1
2
3
1
2
3
1
2
3
1
2
3
1
1
2
3
Cycle 6
Join
SYNC
Minislot
Payload
Cycle 10
Cycle 7
Cycle 9
Cycle 1
Cycle 8
PLCP
1
2
3

## Slide 21: Slot Cycle Required PLCP Header Fields
Source and destination ID numbers, or addresses (TBD).
Current slot and cycle number (TBD).
Delay time (in Tq) from PLCP header to the next access window.

## Slide 22: Hidden Nodes
Two joined stations that cannot hear each other are “hidden nodes”.
Not hearing the message will corrupt self timing because the PLCP of the sender will not be heard by nodes hidden from it.
A station may try to transmit at the wrong time interfering with others.

## Slide 23: Hidden Nodes continued...
Listen before send will minimize the probability of interference in well utilized networks because the Taw is very small compared to data transmission time. The network is mostly busy.

## Slide 24: In Search of Sync.
Synchronization can be regained
via the beacon
the sequence of slot cycle values in the message headers,
or an exchange with the coordinator that can be added at the beginning of the access time.

## Slide 25: DIT (RTS) - CSO (CTS)
Joined station sends “Declare Intent to Transmit”, DIT, containing source and destination ID, and delay time for self timing
Coordinator replies with “Confirm Slot Ownership”, CSO echoing the source and destination ID, delay time.
Joined stations time the slot using the coordinator’s CSO transmission.

## Slide 26: Visualizing Slot Cycles
A Circle Diagram

## Slide 27: > Slot Cycle Duration = πd <
2
4
3
5
6
7
1
8
For the single ISOC station case: The latency from the time that ISOC data is queued to the time when it can be sent is always less than or equal to, the slot cycle duration (πdk). The maximum latency is the case when the current slot cycle is fully utilized except for the ISOC slot, which a Minislot.
ISOC Slot
ISOC Slot
ISOC Slot

## Slide 28: Single ISOC Station Latency
The only latency for an ISOC data transmission is the remaining time in the current slot cycle.
The variation in the time for a slot cycle (w/ ISOC Minislot) is the upper bound for the variation in the ISOC latency.
The slot-size history does not matter.

## Slide 29: Visualizing Slot Cycles
An Arrow Diagram

## Slide 30: Possible Slot Cycle Sequences
A Cycle of only Minislots
Utilized Slot(s) < Maximum Size
All Utilized Slots = Maximum Size
Beacon Interval
Each arrow is a complete cycle of all slots

## Slide 31: How is a Station’s QoS Determined?
QoS Depends On:
  Number of slots
  Number of cycles in the slot
  (Minimum) size of the ISOC payload
  Maximum size of the Non-ISOC payloads

## Slide 32: Two Slot Case With One ISOC Station
ASYNC 1
ASYNC 2
ASYNC 3
ASYNC 4
ASYNC 5
ASYNC 7
ASYNC 6
ISOC 1
ASYNC 1
ASYNC 2
ASYNC 3
ASYNC 4
ASYNC 5
ISOC 1
ISOC 1
ISOC 1
ISOC 1
ISOC 1
Time

## Slide 33: QoS for 2 Slot Case
QoS Depends On:
  Number of Slots, Ns = 2
  Number of Cycles in the Slot k, Mk
  Max. size of the ASYNC payload, PAx
  Min. size of the ISOC payload, PIn
PIn may be equal to PAx

## Slide 34
Case 1. ISOC data rate (constrained by PIn, fI, fb ) =
fI = fbPIn / ( PAx + HA + PIn + HI ) [bits/second]
Where ( PAx+ HA+ PIn+ HI ) is the length of a Cycle in bits (also the ISOC packet interval).
 PAx = PIn ( fb / fI - 1 ) - ( HA + HI )
PIn is the minimum length of the ISOC packet required for the requested QoS,
PAx is the maximum length of the ASYNC packet to maintain the requested QoS constrained by PIn.

## Slide 35
2. Constraining: ISOC packet rate to a specified value fp = fb / L, and using this to drive the packet lengths, along with the ISOC data rate, fI , we have:
( PAx+ HA+ PIn+ HI ) = L [bits / ISOC packet interval]
Substituting L into a previous equation, namely fI = fbPIn / ( PAx + HA + PIn + HI ), results in:
 PIn = ( fI / fb ) L = fI / fp
 PAx = L ( 1 - fI / fb ) - ( HA + HI ) or
PAx = ( fb - fI ) / fp - ( HA + HI )

## Slide 36
Where 1/ fp is the ISOC packet inter arrival time.

## Slide 37
ISOC 2
ISOC B
ASYNC 2
ISOC 1
ISOC A
ASYNC 1
ISOC 3
ISOC C
ASYNC 3
ISOC 1
ISOC D
ASYNC 4
ISOC 3
ISOC A
ASYNC 6
ISOC 2
ISOC E
ASYNC 5
ISOC 1
ISOC B
ASYNC 7
ISOC 2
ISOC C
ASYNC 1
ISOC1 inter arrival time
ISOC 1
ISOC 2
ISOC A
ISOC B
ISOC C
ISOC E
ASYNC 1
ASYNC 2
ASYNC 3
ASYNC 4
ASYNC 5
ASYNC 7
ASYNC 6
ISOC D
ISOC 3

## Slide 38
2
B
2
1
A
1
3
C
3
1
D
4
3
A
6
2
E
5
1
B
7
2
C
1
Fast ISOC Inter Arrival Time for “1”
Slow ISOC Inter Arrival Time for “A”
ASYNC Inter Arrival Time for “1”

## Slide 39: QoS will be straight forward if:
1. ISOC data rates must be met for all ISOC channels, but packet inter arrival times can be less than the maximum.
2. Slow ISOC data rates are simple, (1,2,3,4, etc.) multiples of a single rate.
3. Each member of an ISOC QoS (greens) requires a fixed payload size defined by the Coordinator.
2. All ASYNC packets have the same maximum size.

## Slide 40: Coordinator ISOC Calculations
QoS cannot be provided if the data rate requested is less than that available in the current slot cycles that the coordinator can provide.
Fundamentally, there is (fb / Ns)(1/ Mi) bandwidth available in each slot cycle of slot i, where Ns is the number of slots, Mi is the number of cycles in the slot, and fb is the base bit rate, if equal packet sizes are assumed.

## Slide 41
Stations join one at a time, so calculations are incremental.
Packet sizes can be used to fine tune the bandwidth allocations.
Bandwidth is automatically returned to the network via a minislot for low levels of utilization.
The efficiency of the network can be degraded for fixed sized packets for exact inter arrival times.

## Slide 42: ASYNC Joins
Managing the ASYNC Joins:
  assign a slot cycle,
  specify the maximum packet size,
  add reserved slots required to limit ASYNC bandwidth,
  increase total cycle value Mi for that slot
If ASYNC has a QoS minimum, then deny service if slot maximum is exceeded.

## Slide 43: Dynamic Simulation

## Slide 44: Dynamic Simulation Objectives
Show a difficult case: 3 video streams, 1 audio, 1 bulk transfer with lots of data to send.
Show one method of allocating bandwidth
Present dynamic simulation data and results

## Slide 45: Simulation Inputs Overview
Symbol rate = bit rate = 22 Mbps
3 video streams at 6 Mbps rate.
1 audio stream at 1.2 Mbps rate.
The initial start time of each video stream and the audio stream is random using an exponential distribution.

## Slide 46
The ASYNC stream utilizes whatever bandwidth it can get to send 500,000 byte transfers (frames).
The ASYNC inter frame times are random and exponentially distributed with a mean of 1 second.
Each simulation was run for 30 seconds of network time for each run.

## Slide 47: Simulation Parameters

## Slide 48: Bandwidth Allocation in 1 Mbps Units
R1
R2
R3
R4
R5
R6
R7
R8
R9
R10
ASYNC
VIDEO 1
VIDEO 2
VIDEO 3
AUDIO 1
AUDIO 1
VIDEO 3
VIDEO 3
VIDEO 2
VIDEO 2
VIDEO 1
VIDEO 1
R1 to R10 are reserved slots that are never allocated. They will always be minislots.
The ASYNC’s rate is limited by the Slot Cycle Allocation.
Because of BW quantization, audio is given more bandwidth than it will use. Some of its bandwidth is returned to the other stations, mostly the video.

## Slide 49: Simulation Results
Graphical Output

## Slide 50: Next: Medium Level View Timing Diagram
View 400 ms starting at 5.4 seconds
Top three traces show the video
Trace 4 shows the audio
Bottom trace shows the bulk transfers.
Frame sequence can be seen and individual packet structure can still be partially seen.

## Slide 52: Next: Low Level View Timing Diagram
View 50 ms starting at 5.4 seconds.
Top three traces show the video.
Trace 4 shows the audio.
Bottom trace shows the bulk transfers.
This shows the interleaving of individual packets.

## Slide 54: Simulation Summary Results
Simulation time = 30 seconds
Video frames transferred = 899,898,898
Audio frames transferred = 299
Bulk Transfer frames transferred = 9
Audio or video frames missed = 0, for simulation runs using 25,000 Byte video frames and runs using 5,000 Byte video frames.

## Slide 55: Incorrect Allocating of Bandwidth
Video 1
R1
R2
R3
R4
R5
R6
R7
R8
R9
R10
ASYNC
Video 2
Video 3
Audio 1
~ 21 Mbps
~ 1 Mbps
This looks OK at first, but the simulation showed that sometimes the audio or a video stream gets more than its share of BW.
Several frames were missed.