## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: IEEE802.15.3: Data scrambling
Date Submitted: 8 March, 2001
Source: Dr. Tim Schmidl Company: Texas Instruments
Address: 12500 TI Boulevard, MS 8632, Dallas, TX 75243
Voice: +1.214.480-4460, FAX: +1.972.761.6967, E-Mail: schmidl@ti.com
Re: Proposal for data scrambling method
Abstract: This proposal presents a method for data scrambling.
Purpose: To present a method for data scrambling that can be used in the 802.15.3 standard.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Data Scrambling
Data scrambling is used to break up redundancy in the input data and to minimize DC bias
Header and payload are scrambled (but not preamble)
Frame synchronous scrambling is used, starting immediately after the preamble
Data scrambling is performed by modulo-2 adding source data with a known bit sequence which may be generated with a shift register
Data descrambling is performed by modulo-2 adding received data with the known bit sequence

## Slide 3: Data Scrambler and Descrambler
Data in
Data out
D
D
D
...
D
XOR
XOR

## Slide 4: Initialization of Shift Register
Fixed or variable initialization of shift register
  802.11b uses fixed initialization
  Bluetooth uses variable initialization based on master clock, which is known to all devices in a piconet. Initialization changes each packet.
  If header is scrambled and variable initialization is used, then initial value of shift register must be based on information known to all devices in the piconet prior to transmission. Alternatively, header is not scrambled and seed can be sent as part of the header.
There are pathological cases in which the interaction of the source data with the data scrambler produces an output with DC bias or a high degree of redundancy
Changing the initialization of the shift register on a packet-by-packet basis means that the pathological case may exist on one packet, but not on the retransmission of the packet

## Slide 5: Generator Polynomial
Primitive polynomials are generally used in data scramblers
  802.11b uses a polynomial of degree 7, which generates 127 bits
  g(x) = x^7 + x^4 + 1
Packet sizes will generally be about 512 bytes (4096 bits), but can be as large as 2048 bytes (16384 bits)
  In pathological cases the input can have a periodicity, which can appear at the output
Can increase the degree of the generator polynomial for longer scrambling sequence
  x^11 + x^2 + 1 2047 bit scrambling sequence
  x^15 + x^14 + 1 32,767 bit scrambling sequence