## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: IEEE802.15.3: A proposal to include Guaranteed Time Slots in the MAC Contention Free Period
Date Submitted: 2 March, 2001
Source: Dr. William Shvodian Company: XtremeSpectrum
Address: 8133 Leesburg Pike, Suite 700, Vienna, Virginia 22182
Voice: +1.703.749-0230 X7129, FAX: +1.703.749.0249, E-Mail: bshvodian@xtremespectrum.com
Re: [ ]
Abstract: This proposal presents adding support for guaranteed transmission time slots into the proposed 802.15.3 MAC to enable both Isochronous streams and a power efficient mode for handling channel access.
Purpose: To provide an improvement to the current version of the 802.15.2 MAC CFP
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that these viewgraphs becomes the property of IEEE and may be made publicly available by P802.15, however, the substance of the subject matter contained in the viewgraphs remains the property of XtremeSpectrum Inc

## Slide 2: Overview
Discuss the need to address MAC power conservation and complexity issues
Present a modified Contention Free Period (CFP) for the 802.15.3 MAC

## Slide 3: Slot Cycle TDMA Issues
Power management:
  All terminals must listen at all times in order to receive and to know when to transmit.
  The coordinator must listen at all times and transmit all CTS messages (called CSO in 01061r0P802-15_TG3-SC-TDMA.ppt)
  RTS/CTS (DIT/CSO) is required even for isochronous slots
Complexity:
  Coordinator: Must calculate SC-TDMA assignments for all asynchronous and isochronous streams to ensure QoS requirements are met
  Stations: Must participate in distributed algorithm to determine when to transmit and receive.
CTS comes from the Coordinator. This does not serve the usual purpose of ensuring that the target heard the RTS. The coordinator may be within range of the transmitter, but the intended target may not be.
Overlapping piconets: SC-TDMA does not inherently provide the capability to allocate periods of a superframe for silence. A silent interval could be useful to allow for coexistence with adjacent WPANs, each transmitting in the other’s silence interval.
A minislot, which is the lack of an event, is used to convey information – virtual token pass.

## Slide 4: Power Management References
Stemm et al. showed that in a typical WLAN usage scenario by far the most power (about 90 percent) is drawn by listening to the radio channel1
Example 802.11b Wireless LAN power usage
1) M. Stemm et al., “Measuring and Reducing Energy Consumption of Network Interfaces in Hand Held Devices.” Proc. MoMuC-3, Princeton, NJ, Sept. 1996.
Typical Current | Transmit | Receive | Sleep
Intel | 300 mA | 170 mA | 10 mA
Sony | 280 mA | 180 mA | 15 mA
Lucent | 330 mA | 230 mA | 9 mA

## Slide 5: Importance of Power Management for IEEE 802.15.3
802.15.3 PAR
  7. Purpose of Proposed Project: [To provide a standard for low complexity, low cost, low power consumption (comparable to the goals of 802.15.1)and, high data rate wireless connectivity among devices within or entering the Personal Operating Space (POS). The data rate will be high enough, 20 Mbps or more (see 13a), to satisfy a set of consumer multimedia industry needs for WPAN communications. The project will also address the Quality of Service capabilities required to support multimedia data types.]
IEEE P802.15 WPAN High Rate Study Group Functional Requirements, Standards Development Criteria
  The 802.11 Standard does not address the power consumption envelope of the WPAN class of devices listed in section 1a.

## Slide 6: Modified CFP
Allow for time slots with guaranteed start time at the beginning of each superframe (after the CAP), then use the remaining bandwidth for Slot Cycle TDMA
This was agreed on at the 802.15.3 ad hoc MAC meeting in Boulder on Feb 8-9, 2001.
Notes: `

## Slide 7: Modified CFP
Variable Time Slots
Guaranteed Time Slots
Contention
Access
Period
Beacon
Contention Free Period
1
2
4
5
1
2
3
4
1
2
4
Mini slots
Guaranteed Time Slots (GTS) are fixed assignment times
Real time traffic and power sensitive devices utilize GTS for power efficiency
Variable Time Slots (VTS) are bounded time periods rather than single packets
VTS bandwidth is shared among power insensitive users with asynchronous traffic utilizing SC-TDMA
First station in the VTS portion of the SC period may rotate through for fairness, specified in Beacon

## Slide 8: Use of GTS and VTS slots
Real time constant rate traffic will use Guaranteed Time Slots (GTS). “Isochronous” traffic with fixed assignment slots get guaranteed bandwidth with bounded latency and latency variation
Real Time variable bit rate traffic will use GTS when power savings is critical. Real time variable bit rate traffic may use SC-TDMA if bandwidth efficiency is more important than power usage
Power sensitive devices with asynchronous traffic can be assigned Guaranteed Time Slots.
Asynchronous traffic from less power sensitive devices will use SC-TDMA Variable Time Slots (VTS).

## Slide 9: Modified CFP (cont.)
Variable Time Slots
Guaranteed Time Slots
Contention
Access
Period
Beacon
Contention Free Period
1
2
4
5
1
2
3
4
1
2
4
Mini slots
Devices only have to be awake to transmit or receive during a fraction of the superframe. This provides efficient battery powered operation.

## Slide 10: Advantages of this Modified Approach
Guaranteed Time Slots are fixed time
  Supports low power mode
  Bounds packet delay variation
Guaranteed Time Slots slots do not require RTS/CTS
Coordinator doesn’t need to know Variable Time Slot packet sizes or throughput a priori, yet all remaining bandwidth is used efficiently and fairly
Only terminals with Variable Time Slot streams need to listen to the VTS slots.
Coordinator only needs to do scheduling of Guaranteed Time Slots. However, VTS (SC-TDMA) slot durations can be allocated for each terminal individually or all terminals can use the same time duration like token ring
Simplifies the assignment calculations and assignments as compared to SC-TDMA with mixed isochronous and asynchronous slots
Adjacent piconet coordination possible

## Slide 11: Adjacent piconet coordination
Un-assigned GTS slots can be used to allow multiple piconets to time division share a radio channel in a coordinated manner
This feature supports to goal of coexistence with 802.11b by allowing multiple 802.15.3 piconets the ability to time share a channel.
Contention
Access
Period
Beacon
Contention Free Period
1
2
5
1
2
3
4
Unassigned GTS Slot
Contention Free Period
1
2
4
Unassigned GTS Slot
Contention
Access
Period
Beacon
Contention Free Period
1
3
4
5
Unassigned GTS Slot
Piconet 1
Piconet 2
Superframe n
Superframe n+1

## Slide 12
Dynamic Reallocation of GTS Bandwidth
Show how GTS can supply dynamic allocation of bandwidth for VBR and asynchronous traffic and signaling traffic
  Random access requests
  Fixed assignment requests
  Piggybacked requests

## Slide 13
GTS with Fixed Assignment Reservations
Guaranteed Time Slots
Contention
Access
Period
Beacon
Contention Free Period
1
2
4
5
Guaranteed Time Slots (GTS) are fixed assignment times
Each Terminal is assigned a fixed assignment reservation slot
Beacons contain the assignments
Higher overhead than piggyback requests, but better fairness
Coordinator only has to listen to a finite part of the superframe to make reservation requests
3
Assigned Reservation Slots
Unassigned Slot

## Slide 14
GTS with Fixed Assignment Reservations
Guaranteed Time Slots
Contention
Access
Period
Beacon
Contention Free Period
1
2
4
5
Guaranteed Time Slots (GTS) are fixed assignment times
Terminals use Slotted Aloha or CSMA/CA for requests
Best for a network with a large number of users because fixed bandwidth is not needed for (not a WPAN)
3
Random Access Reservations
Unassigned Slot

## Slide 15
GTS with Piggyback Reservations
Guaranteed Time Slots
Contention
Access
Period
Beacon
Contention Free Period
1
2
4
5
Guaranteed Time Slots (GTS) are fixed assignment times
Each Terminal is assigned a fixed assignment reservation slot
Lower overhead than Fixed Assignment Reservation slots, but less fairness (reservations at the start of the superframe are disadvantaged)
3
Reservation in Header
Unassigned Slot

## Slide 16
Summary of dynamic allocation of GTS bandwidth
GTS provides the ability to dynamically allocate all bandwidth and provided needed QoS for isochronous CBR and VBR streams, with remaining bandwidth assigned to asynchronous traffic
CBR streams can be assigned bandwidth for the duration of a call, without requiring requests every superframe
The current GTS baseline supports the use of fixed assignment reservations at the end of the superframe or piggybacked reservations during an assigned slot
Terminals request bandwidth assignment can change once per superframe
Overhead for reservations is offset by the lack of overhead for DIT/CSO

## Slide 17: Summary
Modify the Contention Free Period to allow Guaranteed Time Slots
  Provide Guaranteed Time Slots for isochronous streams and power sensitive devices
  Provide Variable Time Slots for those devices with variable rate streams and less stringent power concerns
  Provides the potential for TDMA support for adjacent piconet coordination
  This approach provides high performance, good QoS and high battery power efficiency
GTS alone can be used to provide dynamic bandwidth allocation