## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Nokia MAC Proposal for IEEE802.15 TG4]
Date Submitted: [09 March, 2001]
Source: [Juha Salokannel] Company [Nokia]
Address [Visiokatu 1, FIN-33720, Tampere, Finland]
Voice:[+358 3 272 5494], FAX: [+358 3 2727 5935], E-Mail:[juha.salokannel@nokia.com]
Re: [Revision1]
Abstract: [Submission to Task Group 4 for consideration as the Low Rate MAC for 802.15.4]
Purpose: [Overview of MAC proposal for evaluation]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Nokia MAC Submission to IEEE 802.15 Task Group 4
Presented by
Heikki Huomo and Juha Salokannel
Nokia
Note: See notes below some pages in Notes Page View
Notes: Here are the notes!

## Slide 3: CONTENTS
Nokia System View
Design Objectives
Key Points
Device Classes
Medium Access Scheme
Device Discovery
Data Transfer and Packet Structure
Duty Cycle example

## Slide 4: Environment - Technology
Slide <number>
Heikki Huomo/Juha Salokannel, Nokia
March 2001
Web Server Dimensions
CMOS Performance
Power Efficiency Trends
Devices

## Slide 5: The Web of Trillion Devices
2...3G Wireless
Bluetooth
IrDA
WPAN
RFID
1K Operators -- 1M E-businesses -- 1B People -- 1000B Devices
Zero-Conf
Service (XML, RDF)
Discovery
IPv6 Addressing
& Framing
TCP
UDP
HTTP
WLAN
106
109
1012
103
Personal Trusted Device

## Slide 6: The lock of my house
Ulko-oven lukko
The lock @ your front door
LOCKED since 2.5 hours. Last user: Pertti. See use history.
Brought to you by
www.securihome.com
at 10:23 27-Feb 2000.
The lock @ your front door
LOCKED since 2.5 hours. Last user: Pertti. See use history.
Brought to you by www.securihome.com
at 10:23 27-Feb 2000.
Not just a lock, but part of an e-business (huge value/bit)

## Slide 7: Tell me more about this painting
The museum installs radio tags to paintings. Users receive the tag IDs in the terminals, which then translate the ID into local/global web pages.
The tag may be a beacon that announces the id periodically, or a passive device that wakes up on terminal’s demand. Very low power demands (parasitic?) would allow permanent embedding.
The ID could be an URL, HP Cooltown-style.

## Slide 8: My Universal Privilege Device
Announces my access privileges to things & services. Maybe identity & authentication as well.
At home, I am the superuser. At office, a humble worker :-)
Only works on me. Talks to the various login controls and hooks me up with minimum hassle.

## Slide 9: Lego-like stuff with embedded electronics
This kid here hacked a motion capture and automated navigation system into his PAN enabled PowerTransformer hero. Basic stuff that any 8-year kid can do with a PC and microIP Lego blocks.
Price is not a constraint since Santa Claus is paying :-)
Neither are batteries, they will only last a day.
But the action must happen by the millisecond to sustain his fast reactions!

## Slide 10: Mobile Commerce
stores can install radio tags to items, smart shelves, scales
detect when items are taken from shelf to shopping cart. Store can do dynamic inventory.
shelf scanners have radio tags and can communicate wirelessly with an access point providing personalized sales items.

## Slide 11: Design Objectives
Very low power consumption
Easy implementation
Only to provide a generic multiple access, device discovery and data transfer services for upper layers
Scalability
(M)Any device can contact any device in range
Optimized for low bit rates and low duty cycles

## Slide 12: Key Points
Three device classes
  Scalable for different type of devices
CSMA/FDMA Multiple Access schemes
  CSMA/CA for ad hoc operation
  FDMA; special initialisation frequencies
Device discovery based on device advertising
  Each device broadcasts its availability for the others
  Direct Point to Point topology
Security issues not covered
  Left for upper layer

## Slide 13: Device classes
Maximal scalability for devices of different size, cost, applications and power consumption requirements
Notes: Mini devices can operate with all device classes
Pico and Beacon devices can not communicate with each other since they are operating in different frequency channels

## Slide 14: Usage Targets for different device classes

## Slide 15: Medium Access Scheme FDMA part
Predefined separate frequency channels for Pico and Beacon devices
  device discovery, inquiry and data transfer in these channels if one of the devices is a Pico or Beacon device
Predefined device discovery channels (SAC)
  device discovery and inquiry between Mini devices
The other frequency channels are allocated for unicast data transmission between mini devices (Data Channels)

## Slide 16: Medium Access Scheme FDMA part
2400
2401
2402
2403
2481
2482
2483
2480
Pico
SAC1
SAC2
DataCh#76
SAC0
Beacon
Example of Frequency Channel allocation for device classes

## Slide 17: Medium Access Scheme CSMA/CA part
Air interface transmission (excluding Identification Information PDU in the beacon channel) is preceded by carrier sensing and collision avoidance protocol.
The used parameters vary in the different channels
The parameter values are for further study

## Slide 18: Device Discovery
Each device broadcasts periodically information about its availability for the others by sending id_info PDU.
With this PDU the broadcasting device informs that it can be contacted during the next e.g. 1ms
  Mini devices also include the used unicast channel index into id_info PDU.
  Beacon and Pico devices use their own frequency channels all the time
The devices initialising the data exchange 1) starts to scan for id_info PDUs, 2) after detecting the id_info with the correct address it can begin the connection.
Notes: The broadcasting nature (comparing to alternative listening nature) of all devices is chosen based on some expectations:
  - The TX and RX power consumption are close to each other, thus it does not make much difference.
  - The long TX period in device discovery is avoided (replaced with long listening period)
  - By listening channels the device can find out what kind of devices are available

## Slide 19: Device Discovery and Data Transfer
Notes: Both devices inform periodically about themselves by sending id_info PDU in SAC (Service Advertisement Channel). The left device is activated (from periodic advertisementing) by user and it starts to listen to SAC0 to find out if the needed device is in range. The listening in SAC0 lasts max. 1 second. In the example the left device can hear the second id_info PDU. In the PDU the used data channel (X) of the right device is told. The right device tunes immediately after sending the id_info to the channel X to listen. The left device sends a data PDU to right device and vice versa. Afterwards, both devices come back to the basic cycle (sleep-send id_info-listenonChX-sleep...).

## Slide 20: Device Discovery and Data Transfer
Notes: From mini point of view, communication with Beacon device is similar to communication with another mini device, but the whole communication happens on one (Beacon) channel.
The operation with Pico devices is similar, but takes place on Pico channel and Pico is expected to have long sleep periods like the Mini has.

## Slide 21: Device Discovery and Data Transfer
Notes: The data communication of more than one PDU is initiated with CONNECTION_REQUEST PDU and acknowledged with CONNECTION_RESPONSE PDU. The connection is terminated with TERMINATE PDUs or if connection timer expires.
The ARQ is based on simple Stop-and-Wait. Once one packet is sent, the sender waits until an acknowledgement has been received or a timer has expired. If the timer expires the sender may send the packet again.

## Slide 22: Packet Structure
Three Baseband packet types:
  Beacon Channel id_info PDU
  "short" for id_info PDU
  "long" for other PDUs
Notes: Coding of "long" PDUs:
Coding of S/I field:
0 = service advertising
1 = inquiry

## Slide 23: Duty Cycle
An example of duty cycle for mini device
Notes: With the short activity during longer time period, the power consumption is kept low.