## Slide 1: IEEE 802.15.1 WPAN™ “Standardization” of Bluetooth™
Tom Siep
Member Group Technical Staff
Texas Instruments
Bluetooth is a trademark Telefonaktiebolaget L M Ericsson, Sweden
WPAN is a trademark of the IEEE

## Slide 2: Overview
802.15.1 Status
Creating the Draft Standard
  Architecture of WPANs
  WPANs vs. WLANs
  802.15.1 LLC SAPs
  SDL
Future IEEE/Bluetooth collaboration

## Slide 3: Project 802.15.1 Status
Presented to Working Group and then IEEE 802 Executive Committee September00
Delayed for Bluetooth V1.1 publication
Confirmation Letter Ballot started 9Feb01, ended 11Mar01: PASSED, 46/4/1 or 92% affirmation
Comment Resolution at March01 IEEE meeting in Hilton Head, SC.: all comments processed
Next step: editing; 10 day confirmation ballot ~2April01
LAN/MAN 802.15 Sponsor Ballot(s) during the Summer or Fall
RevCom will submit Final Draft Std for approval upon successful completion of the Sponsor Ballot

## Slide 4: The Process of Creating an IEEE Standard
You are here

## Slide 5: Bluetooth Specification (SIG version)
RF
Baseband
Audio
Link Manager
L2CAP
Data
Other
TCS
RFCOMM
SDP
Applications
Control
Notes: <number>
<footer>
<header>
<date/time>

## Slide 6: Bluetooth Specification (IEEE version)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 7: IEEE Project 802 Standards
Software
Internet Protocol (IP)
x.400 and X.500 Email
Transport Control Protocol (TCP)
Hardware

## Slide 8: More Detail of IEEE P802 Structure

## Slide 9: How Does That Relate to Bluetooth?

## Slide 10: Constructing the Draft

## Slide 11: WPAN Architecture
Wireless personal area networks are different than WLANs in several functional areas:
  Control of the media
  Range
  Power
  Number of participants
  Ownership of devices
  Nature of devices
  Lifetime of network
  Relative cost
These differences are a result of the topological differences between the two types

## Slide 12: Topologies: Stars, Rings, Trees
WLANs
WPANs
Token Ring

## Slide 13: WLANs verses WPANs (WARNING:gross simplifications)
WLAN is outwardly looking
  Interacts with wired infrastructure (LANs)
  Network timeframe hours to days
  Portable devices
  “Wires are expensive”
WPAN is inwardly looking
  Interacts with personal objects
  Network timeframe seconds to hours
  Highly mobile devices
  “Wires get in the way”

## Slide 14: WPAN frames

## Slide 15: WLAN Frames

## Slide 16: 802.15.1 SAPs (1 of 4)
MA-UNITDATA request ( source_address, destination_address, routing_information, data, priority, service_class )

## Slide 17: 802.15.1 SAPs (2 of 4)
MA-UNITDATA indication ( source_address, destination_address, routing_information, data, reception_status, priority, service_class )

## Slide 18: 802.15.1 SAPs (3 of 4)
MA-UNITDATA-STATUS indication ( source_address, destination_address, transmission_status, provided_priority, provided_service_class )

## Slide 19: 802.15.1 SAPs (4 of 4)

## Slide 20: 802.15.1 SDL
Derived a picture of what the structure of the BT spec is in IEEE terms.
Helped to uncover holes in existing spec
Enables bench testing and validating of components
Provides a common language between the SIG and the IEEE
Generation of TTCN from SDL is possible

## Slide 21: Future Bluetooth/IEEE Collaboration
IEEE 802.15 continues to work with the Bluetooth Special Interest Group
  Submission of Errata
  “Early” updates of the Spec from the SIG – current version of Draft includes v1.1 Bluetooth Specification
  Plans for future revisions of
    Version 1.x
    Future versions
There now is an overlap of “ownership” of the two documents.

## Slide 22: Backup Slides
(likely not shown)

## Slide 23: IEEE: An Overview
Established in 1884 (AIEE & IRE)
Membership was 360,00 Dec99; 66% USA & 33% Non-USA
Produces 30 percent of the world's published literature in electrical engineering, computers and control technology,
Holds annually more than 300 major conferences
Has more than 800 active standards with 700 under development.

## Slide 24: IEEE P802 LAN/MAN
IEEE Project 802 Local and Metropolitan Area Network Standards Committee
Accredited by ANSI, Sponsored by IEEE Computer Society
  Ethernet, Token Ring, Wireless, Cable Modem Standards
  Bridging, VLAN, Security Standards
Meets three times per year (400 individuals, 15% non-US)
Develops equivalent IEC/ISO JTC 1 standards
  JTC 1 series of equivalent standards are ISO 8802-nnn
IEEE URLs
  802 http://www.ieee802.org/
  802.15 http://www.ieee802.org/15/

## Slide 25: IEEE 802 Standards Principals
Due Process through established rules and procedures
Consensus highly desired, near unanimity is generally the rule
Openness where all individuals, world-wide, have access to the process
Balance maintained by having balloting group include both developers and users
Right to Appeal both procedural and technical issues at any time during the process

## Slide 26: Scatternet

## Slide 27: Hidden Node Problem