## Slide 1: IEEE P802.15 Working Group for Wireless Personal Area Networks
Interference Aware Bluetooth Scheduling Techniques
Nada Golmie
National Institute of Standards and Technology
Gaithersburg, MD 20899
USA

## Slide 2: Objectives
Update the January scheduling proposal 01/63r0.
  Implementation details
  Additional traffic type results
  Extensions to maximize channel utilization.
Observations based on performance evaluation results for interference based environments:
  Which HV packet type to use for BT voice? Is HV3 better than HV1?
  What packet length to select? Does fragmentation help?
  Is FEC useful?
Recommendations

## Slide 3: Recap of Interference Aware Scheduling
Interference Estimation Phase
  Maintain a Frequency Usage Table
  Mark “Used” frequencies
  Slave updates master’s Frequency Usage Table
Master Delay Policy
  schedule packet transmission at the master and ensure that both master to slave and slave to master packets are received in “unused” frequencies.

## Slide 4: Step by Step Algorithm
Slave’s End.
  For every packet received, update BERf which is an average value of the BER per frequency.
  Every update interval, U, refresh the Frequency Usage Table by marking the frequencies, and
  Send a status update message to the master.
Master’s End.
  For every packet received update BERf
  Every update interval, U, refresh Frequency Usage Table by marking frequencies, and
  Delay transmission until slave and master’s receiving frequencies are available.

## Slide 5: Frequency Usage Table
Construct a table of the available frequencies based on the BER measurement at the receiver.

## Slide 6: Scheduling Policy at Bluetooth Master
Master checks both its available frequencies and the slave’s available frequencies before sending a packet to the slave.

## Slide 7: LMP Interference Status PDU
Define LMP_Interference_Status Message

## Slide 8: Simulation Scenario
IEEE 802.5-TG2/ 00388r0
(1,0)
(0,15)
(0,d)
(0,0)
WLAN AP
Tx Power 25 mW
WLAN Mobile
Tx Power 25 mW
Bluetooth Master
TX Power 1 mW
Bluetooth Slave,
Tx Power 1 mW
Data
ACK
Data
Impact of WLAN
Interference
on Bluetooth
Performance
Impact of Bluetooth
Interference on WLAN
Performance
Data
ACK
Traffic Distribution
Offered Load 50 % Of Channel Capacity
Packet Size 8000 bits
Interarrival 1.86 ms
Statistics Collection Points
W
L
A
N
B
T
Offered Load 30 % Of Channel Capacity
DM1 Interarrival 2.91 ms
DM3 Interarrival 8.75 ms
DM5 Interarrival 14.58 ms

## Slide 9: Performance Measurements
Measurements are performed at BT Slave Device:
  Probability of packet loss (Baseband)
  Mean access delay (L2CAP)
Measurements performed at the WLAN (mobile) device:
  Probability of Packet (ACK) Loss.

## Slide 10: Effect of Scheduling on BT

## Slide 11: Effect of Scheduling on BT

## Slide 12: Effect of BT Scheduling onWLAN

## Slide 13
Scheduling technique is effective in reducing packet loss for all packet types.
Mostly effective for reducing delays of multi-slot packets.
It is neighbor-friendly and eliminates interference on other systems.
It saves power since no transmission is wasted in bad channels.
How about FCC rules?
Summary of Scheduling Advantages

## Slide 14
FCC,”Title 47, Code for Federal Regulations,” Part 15, October 1998 state
  1) “Frequency hopping systems operating in the 2400-2483 MHz (..) shall use 75 hopping frequencies. (..) The average time of occupancy on any frequency shall not be greater than 0.4 seconds within a 30 second period.”
  2) “The incorporation of intelligence within a frequency hopping spread spectrum system that permits the system to recognize other users within the spectrum band so that it individually and independently chooses and adapts its hopsets to avoid hopping on occupied channels is permitted. The coordination of frequency hopping systems in any other manner for the express purpose of avoiding simultaneous occupancy of individual hopping frequencies by multiple transmitters is not permitted.”
Bluetooth uses 79 hopping frequencies; therefore the average time of occupancy on any one frequency is equal to:
30/79 = 0.37 seconds.
Since we are not changing the hopping pattern the average time of occupancy on any single frequency is still less than 0.4 seconds.
In case the rules, specify that 75 channels need to be used within 30 seconds, then during a 30 second period, bad frequencies are probed at least once by a POLL/NULL message exchange between the master/slave.
What are the relevant FCC rules?

## Slide 15
One of the drawbacks in avoiding “bad” frequencies is that channel utilization is limited to 57/79 = 72%.
For single slot packets, the utilization is limited to 72%.
However, since multi-slot packets use one frequency, the idea is to find good frequencies and use them to transmit DM3 or DM5 packets.
Scheduling Extensions to Maximize Channel Utilization

## Slide 16
Master and Slave devices implement the following packet encapsulation rules in addition to the delay scheduling policy implemented by the master;
Let fx denote the receiving frequency associated with slot x and S(fx) and D(fx) denote the source and destination receiving frequencies respectively.
Packet encapsulation rules:
    if S(f1) and D(f5)
    select DM5
    else if S(f1) and D(f3)
    select DM3
    else if S(f1) and D(f1)
    select DM1
Packet Encapsulation Rules

## Slide 17
Miscellaneous coexistence observations … based on simulation performance results

## Slide 18: Choice of HV Packet does not affect BT

## Slide 19: HV3 is”Friendlier” to WLAN

## Slide 20: DM vs. DH Packets: Is FEC Useful?

## Slide 21: Effect of Fragmentation on “Other” System

## Slide 22
HV3 is friendlier than HV2 and HV1 to WLAN.
Longer packets have a higher probability of collision than shorter packets.
Fragmentation may degrade the performance of the interfering system.
FEC has limited performance benefits; mainly it improves the packet loss probability for low interference scenarios.
Summary of Observations

## Slide 23
Use interference aware scheduling for BT
It can only improve the performance of BT in an interference environment:
  reduces packet loss for all types of packets
  reduces delay for multi-slot packets.
  eliminates interference on other system.
Recommendations