## Slide 1
An Intelligent Frequency Hopping Scheme for Improved Bluetooth Throughput in an Interference-Limited Environment
Anuj Batra, Kofi Anim-Appiah, and Jin-Meng Ho
Texas Instruments Incorporated
12500 TI Blvd, MS 8653
Dallas, TX 75243
214.480.4220
batra@ti.com

## Slide 2: Outline of Talk
Background
Throughput for Bluetooth 1.1
Adaptive Frequency Hopping Schemes:
  Repeated channel frequency hopping sequence
  Intelligent frequency hopping sequence
Implementation via the Look-Ahead Algorithm
Reduced Adaptive Frequency Hopping
Channel Quality Assessment and Resynchronization

## Slide 3: Background
Wireless Ethernet (802.11b) and Bluetooth are the two most popular technologies in the 2.4 GHz ISM band
Wireless Ethernet:
  Single carrier (spread spectrum) system
  BW = 17 MHz for one network, BW = 51 MHz for 3 networks
  Supports data rates of 1, 2, 5.5, 11 Mbps
Bluetooth:
  Frequency-hopping spread spectrum system
  Hops at a rate of 1600 Hz over 79 1-MHz wide channels
  Occupies 79 MHz of the available 83.5 MHz in ISM band
  Maximum data rate for Bluetooth is 1 Mbps

## Slide 4: Coexistence
Since wireless Ethernet and Bluetooth devices overlap in frequency, mutual interference is a major concern.
Coexistence tests have shown that this interference devices can a major impact on the throughput (see 802.15-01/084r0).
Modifications to both wireless Ethernet and Bluetooth are necessary to reduce the impact each has on the other.
Examples:
  Adaptively change the Bluetooth hopping sequence based on the channel conditions.
  Implement power control in both devices.

## Slide 5: Adaptive Frequency Hopping
Focus of this talk: adaptive frequency hopping
Interference can be minimized by adaptively changing the hopping sequence based on channel conditions.
The ideal approach is to avoid interference altogether by using a reduced set of channels.
  Problem: need FCC rules change, which may take up to 2 years.
  Current rules require that FHSS systems hop uniformly over a minimum of 75 channels.
Next best approach is to intelligently design a sequence that maximizes throughput (minimizes packet loss) while still using all 79 channels uniformly.

## Slide 6: BT Throughput in Interference
Consider a fully-loaded piconet: one master, one slave.
Bluetooth packet can be:
  Successfully decoded if the channel is clear (good channel).
  Destroyed if interference is present on channel (bad channel).
Thus, the probability of successful transmission is given by:

## Slide 7: Aggregate Throughput
Both the ACL and SCO links can be expressed in terms of a finite state machine (FSM).
The aggregate throughput can be determined from the steady-state probabilities of the FSM.
Assume master transmits DM-M and slaves transmits DM-S.
SCO link:
ACL link:
Maximum throughput for ACL link:

## Slide 8: Throughput Curves for an SCO Link
Note: 5% packet loss  4 bad channels

## Slide 9: Throughput Curves for an ACO Link
 | TACL/TMAX
1 AP | 70.0%
2 APs | 44.7%
3 APs | 24.0%
Solid Line: Original HS
Dotted Line: Maximum

## Slide 10: Reason for Degradation in Throughput
Q: Why does the Bluetooth throughput degrade so much when interference is present?
A: Degradation occurs because of transitions in the hopping sequence from a good channel to a bad channel. These transitions result in:
  Retransmission of data due to lost ACKs (ARQ protocol).
  Wasted resources due to slaves being idle during good channels.
These effects can be minimized and the throughput can be increased by rearranging the underlying hopping sequence to have several good channels in a row and several bad channels in a row.

## Slide 11: Solution 1: Repeated Channel HS
Idea: Master and slave transmit on same frequency.
SCO link:
  Aggregate throughput does not change.
  Master and slave lose an equal number of packets; the link is symmetrical  provides level of QoS for voice link.
  RC-FH is optimal for HV1 traffic.
ACL link:
  Aggregate throughput increases by a factor of 1/p  1.
Low complexity (minimal changes to hardware), reasonable performance.

## Slide 12: Throughput Curves for an ACL Link
 | TACL/TMAX | TRC/TMAX
1 AP | 70.0% | 89.2%
2 APs | 44.7% | 78.5%
3 APs | 24.0% | 67.7%
Solid Line: Original HS
Solid Line with circles: RC-HS
Dotted Line: Maximum

## Slide 13: Solution 2: Intelligent FHS
Q: Can we improve the throughput even further by increasing the block lengths of both the good and bad channels?
A: Yes!
Consider the following hopping sequence with fixed block lengths:
Aggregate throughput can be maximized by maximizing the number of packets transmitted during block of good channels and minimizing the packets transmitted during the block of bad channels.
Note RG and RB must be even because of Bluetooth protocol.

## Slide 14: Intelligent FHS
Note:
  During blocks of good channels: 100% of packets are received.
  During blocks of bad channels: 0% packets are received.
  Define “Dead Time” = DT = 625 s · RB.
To comply with FCC regulations, need addition restriction:
Process for selecting:
  “Dead Time” requirement for application dictates value of RB.
  Given , RG must satisfy FCC constraint.
  If RG = 0, then must use a larger value of RB.

## Slide 15: Intelligent FHS for SCO Link
Focus is on HV2 and HV3 packets.
Assume a fully-load link, where HV-V packets are being transmitted.
The optimal values for the block lengths are given by:
The aggregate throughput is then given by:

## Slide 16: Throughput Curves for HV2 with IFHS
For less than 40 bad channels, 100% throughput with IFHS!

## Slide 17: Packet Loss Curves for HV2 with IFHS
For less than 40 bad channels, 0% packet loss with IFHS!

## Slide 18: Throughput Curves for HV3 with IFHS
For less than 54 bad channels, 100% throughput with IFHS!

## Slide 19: Packet Loss Curves for HV3 with IFHS
For less than 54 bad channels, 0% packet loss with IFHS!

## Slide 20: Intelligent FH for ACL Link
Assume a fully-loaded link, where the master-to-slave packet is DM/H-M and where the slave-to-master packet is DM/H-S.
The optimal values for the block lengths are given by:
The aggregate throughput is then given by:

## Slide 21: Throughput Curves for ACL Link
 | TACL/TMAX | TRC/TMAX | TIFHS/TMAX
1 AP | 70.0% | 89.2% | 98.3%
2 APs | 44.7% | 78.5% | 95.4%
3 APs | 24.0% | 67.7% | 84.6%
Solid Line: Intelligent FHS
Solid Line with circles: Original HS
Dotted Line: Maximum
Note: NB = 10

## Slide 22: Throughput Curves for ACL Link
 | TACL/TMAX | TRC/TMAX | TIFHS/TMAX
1 AP | 70.0% | 89.2% | 98.8%
2 APs | 44.7% | 78.5% | 95.5%
3 APs | 24.0% | 67.7% | 92.0%
Solid Line: Intelligent FHS
Solid Line with circles: Original HS
Dotted Line: Maximum
Note: NB = 15

## Slide 23: Multiple Slaves within Piconet
Previous results generalize to a piconet with multiple slaves.
Multiple SCO links:
  2 HV2 streams, 3 HV3 streams  1 HV1 stream  Use RC-FHS
  2 HV3: Can optimize RG and RB as before:
Combination of SCO link and ACL link:
  Use the parameters derived for a single SCO link.
Multiple ACL links:
  Block lengths can be optimized if packet sizes are known a priori.
  If packet sizes are not known, then make block length for good channels as long as possible so that the “dead time” can be tolerated by all the applications.

## Slide 24: Implementation Issues
To implement the Intelligent FHS, the master must:
  Compile a list of good and bad channels.
  Determine the block lengths for both the good and the bad channels. Note that the lengths will be a function of traffic type.
  Communicate this information to the slaves in the piconet via a reliable broadcast message.
  Determine a start time and possible ending time for the use of the Intelligent FHS.
  Communicate whether the devices will be silent or will transmit during the block of bad channels (more friendly to wireless Ethernet networks if the Bluetooth devices are silent).
Also need an efficient way to re-arranging the original HS:
  A: “Look-ahead algorithm”.
  Algorithm is described in more detailed on the next slide.

## Slide 25: Look-Ahead Algorithm

## Slide 26: Buffer Mechanism for Algorithm
Good Channels
Bad Channels

## Slide 27: Summary of Look-Ahead Algorithm
For the Good Window:
  look ahead in the original hopping sequence until a good channel is found; this is done by comparing the channels produced by the original hopping sequence with the list of good and bad channels
  use this frequency in the next slot interval
  repeat this process until the good window has been exhausted
For the Bad Window:
  look ahead in the original hopping sequence until a bad channel is found; this is done by comparing the channels produced by the original hopping sequence with the list of good and band channels
  use this frequency in the next slot interval
  repeat this process until the bad window has been exhausted

## Slide 28: Reduced Hopping Sequence
Suppose minimum number of channels is reduce to NC.
Both the RC-FHS and IFHS can produce a reduce HS.
  Natural extension of current algorithms.
  Can produce a sequence that avoids the interference altogether!
Changes for RC-FHS:
  Must broadcast list of channels that will be used.
  Need to use Look-Ahead algorithm to skip unused channels.
Changes for IFHS:
  Parameter  changes:
  Compile a list of good, bad, and “don’t use” channels, which then must be broadcasted to all the slaves in the piconet.

## Slide 29: Channel Quality Assessment
Measure RSSI at receiver:
  If RSSI is large and the header is not valid  interferer on channel.
  If the header is valid, then can measure SNR for that channel.
Listen to the channel during the absence of a transmission:
  If energy is above some threshold  interferer on the channel.
  Can use this value to estimate the interferer’s power level.
Actively scan channels before the start of a piconet.
Average these values over a finite amount of time:
  Use 79 accumulators for the 79 channels.
  If value is above a threshold, declare the channel bad.
  Use a forgetting factor so bad channels are periodically revisited.

## Slide 30: Resynchronization
If every device in the piconet has the same list of good and bad channels, then synchronization can be maintained.
In case synchronization is lost: can have a period where the Intelligent FHS is used and then revert back to original hopping sequence. During original HS, make sure everyone has the correct list. After some time, restart the Intelligent FHS.

## Slide 31: Conclusions
Proposed a non-collaborative coexistence mechanism.
Proposed two new frequency hopping schemes: Repeated Channel FHS, and Intelligent FHS to be used with enhanced Bluetooth devices.
These sequence minimizes the Bluetooth packet loss by grouping good and bad channels together.
Ideas work for all kinds of interferers: from 1-MHz wide to 3 wireless Ethernet networks.
Implementation via Look-Ahead Algorithm is easy and straightforward.
New hopping sequences are more friendly towards wireless Ethernet networks: improves throughput in terms of packets/second.