## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Media Access Control proposal for the 802.15.4 Low Rate WPAN Standard]
Date Submitted: [March 2001]
Source: [Phil Jamieson] Company: [Philips Semiconductors]
Address: [Cross Lake Lane, , Redhill, Surrey RH1 5HA, United Kingdom]
Voice:[+44 1293 815 265], FAX: [+44 1293 815 493], E-Mail:[phil.jamieson@philips.com]
Re: [ MAC layer proposal submission, in response of the Call for Proposals ]
Abstract: [This contribution is a highly flexible MAC proposal for a Low Rate WPAN intended to be compliant with the P802.115.4 PAR. It is intended to support both master-slave and virtual peer-to-peer communications for low data rate networks. It is designed to support ultra low power consumption for battery operated nodes at very low implementastion cost. The network is capable to support 254 nodes and one master with 16 devices communicating at the same time. The number of devices in the network can be increased by using IEEE addresses.]
Purpose: [Response to IEEE 802.15.4 TG Call for Proposals]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: MAC solution for Low Data Rate Application
Phil Jamieson
Philips Semiconductors

## Slide 3: Contents
Success Factors
Targeted Markets
PURL Protocol
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 4: Success Factors
Low cost
Data type support
Unlicensed band
Unrestricted geographical use
Global implementation
Governmental regulations

## Slide 5: Low Cost
The added cost of the RF communication capability must be at or below existing consumer price points for end user solutions currently servicing these markets. (interactive wireless joystick would be expected to cost the same as an existing IR or wired joystick)
In Home Automation systems, the added cost needs to be comparable to the most efficient cost of installing a wire to a specific device.

## Slide 6: Data Type Requirements
An aggregate data link service of at least 115 kbps is needed to support the following data types:
  Very low data volume (<10 bytes) control applications
  Asynchronous data link at a rate up to 115.2 kbps (RS232)
  Voice recognition at a peak aggregate rate of up to 64 kbps
  Critical latency applications, such as interactive gaming
  Any combination of the above data types subject to aggregate capacity limitations
Notes: Page <number>
        <footer>
<header>
<date/time>
This is pretty old - I think we should refine this.

## Slide 7: Unlicensed Band & Unrestricted Geographical Use
Unlicensed Band
  The user is not required to apply for any licenses to operate the product implementing this specification.
Unrestricted Geographical Use
  Within a geographical (or political) region, there should not be any restrictions on its use.
  Users would expect to be able to purchase the device implementing this RF technology at one part of the geographic region and use it in another part.
  The geographic region can be as localized as a country (e.g. USA or Japan) or a geo-political area such as European Union where the standards are uniform.

## Slide 8: Global Implementation & Governmental Regulations
Global Implementation
  A desirable consideration is to have one specification (and implementation) that can be sold and used internationally with minimum product variation.
Governmental Regulations
  The specification will need to comply with the appropriate regulations in force at the time for the geographical or political region (includes regulations relating to safety, energy, radiation, etc.)

## Slide 9: Target Markets
Low Data Rate Radio Devices

TV

VCR

DVD

CD

Remote

Mouse

Keyboard

Joystick

Gamepad

Security

HVAC

Lighting

Closures

PETs

Gameboys

Educational

Monitors

Diagnostics

Sensors
Industrial & Commercial
Consumer Electronics
Personal Healthcare

Monitors

Sensors

Automation

Control
Toys & Games
Home Automation
PC Peripherals

## Slide 10: PURL Drivers
Extremely low cost
Ease of installation
Reliable data transfer
Short range operation
Excellent battery life
Simple but flexible protocol

## Slide 11: Network Topology
Virtual links
Master node
Slave node
Communications flow
Transmit only node
IEEE slave node
Notes: Page <number>
        <footer>
<header>
<date/time>
An example network topology in the area of home (living room) control. A set-top-box is acting as the master with a remote, TV, DVD, lamp and curtains enumerated on the network. This has no functionality since the slaves can only talk to the master. What the consumer actually wants is to be able to control the TV, DVD, lamp and curtains using the remote. In this case there needs to be some virtual peer-to-peer links between the remote and the other devices on the network. The mechanism of creating these links is known as pairing.

## Slide 12: PURL Node Architecture
PURL On-air Protocol Stack
PURL PHY
Radio
PURL Node
PURL API
PURL MAC
PURL DLC
Host Transport
Host Interface PHY
Host Stack
PURL Transport
PURL Interface PHY
Host Application
Host User Interface
Host
Local User Interface
APL (with application layer protocol)
PURL NWK (Master only)
Notes: Page <number>
        <footer>
<header>
<date/time>
The architecture here illustrates that, if desired, the master can be attached to a host (PC or STB). In this case the master node would need to implement some bridging protocol with which to transfer PURL API commands across another, probably wired, connection technology, such as USB or RS232.

## Slide 13: The Master Device
Transmits network beacons
Sets up a network
Manages slave devices
Stores slave device information
Routes messages between paired slaves
Receives constantly

## Slide 14: The Slave Device
Is generally battery powered
Searches for available networks
Transfers data from its application as necessary
Determines whether data is pending
Requests data from the master
Can sleep for extended periods

## Slide 15: Time Frame Structure
Time, ms
t + tf
t
Basic time frame:
Network beacon
Contention period
Time, ms
t
t + tf
Slotted time frame:
Allocated slot
Notes: Page <number>
        <footer>
<header>
<date/time>
The basic frame shows the contention period during which devices must utilise the CSMA-CA mechanism before transmitting.
The slotted frame still has some portion of contention for those devices which do not have an allocated slot.

## Slide 16: Data Transfers
Network
Beacon
Data
Packet
Data
Handshake
Uplink transfer:
Data
Request
Data
Packet
Data
Handshake
Network
Beacon
Downlink transfer:
From
Slave
From
Master
Message
Transfers
Notes: Page <number>
        <footer>
<header>
<date/time>
Uplink transfers - the slave device listens for the network beacon which identifies the contention period, transmits its packet and the master handshakes it.
Downlink transfers - the master encodes in the network beacon that a particular slave may have a message. When the slave wakes up it listens for the beacon, notices that it may have a message, requests the data, the master sends the appropriate packet and the slave handshakes it.
The key issue here is that the slave has control of the transfers, i.e. it is not a poll/reply system which would mean the slaves would have to know when they need to wake up or would need long wake up sequences.

## Slide 17: PURL Features Summary
Up to 254 (+ master) bound network nodes. Unlimited using extended addressing.
  Matrix, #1
Example devices that can be supported: sensors, home automation, smart badges, toys, etc.
  Matrix, #2
Automatic network configuration, dynamic slave device addressing
  Matrix #3
Service discovery
  Matrix #4
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 18: PURL Features Summary, Cont…
Bi-directional links
  Matrix #5
Synchronous and Asynchronous
  Matrix #6 (Asynchronous needed)
Payload size 0-63 bytes
  Matrix #7
Star master/slave topology,
  Matrix #10
Virtual peer-to-peer links (pairing)
  Matrix #11

## Slide 19: PURL Features Summary, Cont...
Full handshaking for packet transfers
Power management features
Programmable sleep periods for slave devices
  Matrix #18
CSMA-CA channel access mechanism
15ms frame structure
  Matrix #9
TDMA slots can be allocated
12kbps & 115kbps (actual) data throughput
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 20: Appendix
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 21: Network Evolution
Master
Slave 1
Slave 6
Slave 5
Slave 4
Slave 3
Slave 2
Notes: Page <number>
        <footer>
<header>
<date/time>
An example network topology in the area of home (living room) control. A set-top-box is acting as the master with a remote, TV, DVD, lamp and curtains enumerated on the network. This has no functionality since the slaves can only talk to the master. What the consumer actually wants is to be able to control the TV, DVD, lamp and curtains using the remote. In this case there needs to be some virtual peer-to-peer links between the remote and the other devices on the network. The mechanism of creating these links is known as pairing.