## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: IEEE802.15.3: Need for baseline mode
Date Submitted: 9 March, 2001
Source: Dr. Tim Schmidl Company: Texas Instruments
Address: 12500 TI Boulevard, MS 8632, Dallas, TX 75243
Voice: +1.214.480-4460, FAX: +1.972.761.6967, E-Mail: schmidl@ti.com
Re: Document pointing out the need for a baseline mode
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Need for a Baseline Mode
When the 802.15.3 group was formed, Bluetooth 1.x was assumed to be the baseline mode
If Bluetooth 1.x is used as the baseline mode
  Connection to a piconet can be performed using the Bluetooth 1.x inquiry and paging modes.
  Measuring interference to find a good frequency band for the piconet can be performed in Bluetooth 1.x mode.
  Standby and low power modes such as sniff, hold, and park modes can be entered in Bluetooth mode.
  If a piconet collapses due to interference or loss of some members, fallback mode can be Bluetooth mode.
  Fast time to market for 802.15.3 since Bluetooth 1.x is already defined and Bluetooth modules are available.

## Slide 3: If Bluetooth 1.x is not baseline mode ...
The 802.15.3 group could invent a new mode with similar functionality to Bluetooth 1.x.
  Reinventing Bluetooth 1.x will lead to a significant delay in bringing products to market.
The 802.15.3 group could use similar connect and power saving modes as 802.11b.
  Access point (AP) transmits a beacon, and mobile stations (STA) search for the beacon and then attempt to associate with the AP.
  How is 802.15.3 different from 802.11b?

## Slide 4: Conclusion
Want to make 802.15.1 (Bluetooth) as the mandatory baseline mode for 802.15.3.
  Will allow rapid development of 802.15.3 standard, and it will maintain the basic characteristics of a WPAN.
  Will allow devices to only scan (and not actively transmit) and wait for an inquiry or page.
    No need to continually transmit a beacon, which would increase interference
    When devices connect and decide to transmit at high rate, they can switch to the high rate mode
  Allows 802.15.1 and 802.15.3 to be interoperable