## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: PHY Proposal for the 802.15.4 Low Rate Standard
Date Submitted: 12 March, 2001
Source: Pat Kinney Company: Invensys
Address: Forrest Hills, PA
Voice 412-225-8242, E-Mail:pat.kinney@ieee.org
Re: Call for Proposals for Low Rate PHYs
Abstract: Proposal for a Low Cost, Low Rate PHY
Purpose: For consideration as the PHYof the 802.15.4 standard.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: 802.15.4 Low Rate PHY Proposal Overview
Pat Kinney
Invensys Metering Systems
pat.kinney@ieee.org

## Slide 3: Objectives
Very Low Cost
  Minimal complexity of implementation
  Minimal filters, tolerant of VCO noise
  Good candidate for SOC
Performance
  Robustness to interference, multipath,
Low current drain
  Very fast acquisition times (5-10 chips)
  minimal correlator decorrelator

## Slide 4: Features of this Proposal
Ability to alter data rate for range
Very low complexity for modulator and demodulator
Exceptionally fast acquisition times
Spread spectrum allows possibility of higher transmit powers

## Slide 5: Implementation Overview
Spread Spectrum
Frequency Range: 2.4 GHz
  other bands are possible
Modulation method: QPSK
Data Rate: 10, 170 kb/s
  other data rates are possible
Transmit Power Level: 1 mW
  higher is possible, but as per 15.247

## Slide 6: Implementation Overview
Spread Spectrum
  Direct Sequence
  Transmitted Reference
    Two channels, I&Q, carry the information
    I channel carries spread data
    Q channel carries the spreading function
    Receiver merely multiplies the I against the Q
  All data rates utilize same occupied BW
    lower data rate has higher processing gain
    30 & 500 c/b
    additional process gains are possible

## Slide 7: Architecture
Rcvr FE
Xmit BE
Spreader
MAC
Host
Interface
Despreader
Frequency
Generators
PN
Generator
PMD
PLCP
Demodulator
Antenna
Modulator
MAC

## Slide 8
PN Generator
Programmable feedback
Programmable restart interval
Programmable restart vector
~2% of ASIC area
Feedback select
Restart control
PN Code
Control
8-bit shift register

## Slide 9
Modulator/Spreader
Manchester
Encoder
0
1
TX Data
PN Code
Delay
TXI
TXQ
Programmable delay (½ to 7½ chips)
Optional Manchester encoder
~4% of ASIC area
Control

## Slide 10
Despreader
RXI
RXQ
A
B
Programmable delay (½ to 7½ chips)
~23% of ASIC area
Control
Delay
Delay

## Slide 11
Demodulator


A
B

Clock
Recovery
RX Data
RXDCLK
Optional Manchester decode
~40% of ASIC area
Control

## Slide 12: PLCP Block Diagram

## Slide 13: PHY Parameters

## Slide 14: Summary
Very Minimal Complexity
Ability to trade off range for data rate
Very short acquisition times