## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [TG3-OQPSK-Tutorial]
Date Submitted: [12 March 2001]
Source: [James P. K. Gilb] Company [Mobilian]
Address [11031 Via Frontera, Suite C, San Diego, CA 92127]
Voice:[1-858-217-2201], FAX: [1-858-217-2301], E-Mail:[gilb@ieee.org]
Re: []
Abstract: [This document provides a very rudimentary overview of the OQPSK modulation format and how it is related to QPSK and MSK. It also provides a motivation for a differential mode of signaling.]
Purpose: [To convey information to the PHY committee and other interested parties.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: What is OQPSK
OQPSK - Offset Quadrature Phase Shift Keying
Same as QPSK, except either the I or Q is delayed by 1/2 of a symbol
  Used as the reverse link for IS95 (CDMA) standard
  No pilot for reverse link, so it is differentially coherently detected.
  Reverse link started out QPSK, but ACPR requirements forced a change to OQPSK
    Forward link had more DC power available and average power of multiple outgoing calls decreased peak-to-average

## Slide 3: QPSK v. OQPSK
When the data is unfiltered, both are constant envelope signals
  Filtering the baseband data, however, increases the peak to average ratio
    More so with QPSK due to 180 degree phase shifts
    OQPSK does not allow 180 degree phase shifts.
  This makes the signal more susceptible to spectral regrowth in the analog and RF parts of the radio.
  While they are technically phase shift modulations, they can also be seen as frequency shift modulations.

## Slide 4: OQPSK Characteristics
One ADC can be easily shared between I & Q at twice the clock rate
  saves power and cost (analog portion of ADC drives current drain, sampling rate is 2nd order effect).
  In this case, the offset in sampling is a feature, not a bug
One DAC can also be shared at twice the clock rate
  can save power and cost.

## Slide 5: OQPSK vs. QPSK Constellations
Constellation points
Transition paths
OQPSK
QPSK

## Slide 6: OQPSK vs. QPSK /4 shift
Constellation points
Transition paths
OQPSK
QPSK
Note: phase reference to the carrier is an arbitrary choice for coherent modulation and not relevant for differential encoding