## Slide 1: IEEE P802.15 Working Group for Wireless Personal Area Networks
Dialog with FCC
Nada Golmie
National Institute of Standards and Technology
Gaithersburg, MD 20899
USA

## Slide 2: Outline
Background
Coexistence Performance Evaluation of WPANs and WLANs in the 2.4 GHz band.
  Simulation models (MAC, PHY, Channel)
  Results
Coexistence Mechanisms
Current Status
Questions to the FCC

## Slide 3: Industry Related Coexistence Activities
The IEEE 802.15 Coexistence Task Group 2 is formed (January 2000) to develop:
  a model of coexistence between WPAN and WLAN devices,
  an IEEE recommended practice, and
  possibly modifications to IEEE 802.11 and 802.15 specifications that allow the proper operation of these protocols in a cooperating way.

## Slide 4: Industry Related Coexistence Activities
The Bluetooth SIG is also working on the coexistence issue
  Performance evaluation (simulation, experimental data)
  Liaison activity with IEEE 802.15 TG2 and publication of results
  Recently established Bluetooth SIG Radio 1.X Improvement Working Group to implement coexistence-related changes to the standard.

## Slide 5: Task Group 2 Focus
Performance evaluation and modeling of WPAN and WLAN interference
  conduct experiments
  develop simulation models for the Bluetooth, WLAN MAC, PHY and RF channel.
  collect simulation, analytical and experimental data
Establish coexistence mechanisms
  classify coexistence mechanisms into 2 categories
    collaborative
    non-collaborative
  evaluate the proposed the coexistence mechanisms

## Slide 6: System Simulation Modeling

## Slide 7: Channel Modeling
Additive White Gaussian Noise, multipath fading
Path loss model
Received power and SIR depend on topology and device parameters:

## Slide 8: PHY Modeling
DSP based implementation of transceivers
Design using typical parameters (goal is to remain non-implementation specific)
Bluetooth
  Non-coherent Limiter Discriminator receiver,
  Viterbi receiver with channel estimation and equalization
IEEE 802.11
  Direct Sequence Spread Spectrum (1,2 Mbits/s)
  Complementary Code Keying (5.5, 11 Mbits/s)
  Frequency Hopping (1,2 Mbits/s)

## Slide 9: MAC Modeling
MAC behavioral implementation for Bluetooth and IEEE 802.11 (connection mode)
Frequency hopping
Error detection and correction
  Different error correction schemes applied to packet segments (Bluetooth)
  Frame Check Sequence (FCS) (802.11)
Performance statistics collection
  Access delay
  packet loss
  residual error
  throughput

## Slide 10: Simulation Scenario
IEEE 802.5-TG2/ 00388r0
(1,0)
(0,15)
(0,d)
(0,0)
WLAN AP
Tx Power 25 mW
WLAN Mobile
Tx Power 25 mW
Bluetooth Master
TX Power 1 mW
Bluetooth Slave,
Tx Power 1 mW
Data
ACK
Data
Impact of WLAN
Interference
on Bluetooth
Performance
Impact of Bluetooth
Interference on WLAN
Performance
Data
ACK
Traffic Distribution for WLAN and BT (LAN)
Offered Load 30 % Of Channel Capacity
Packet Size Geometric Distr. Mean 368 bytes
Statistics Collection Points

## Slide 11: Impact of Interference on Packet Loss

## Slide 12
Collaborative:
  TDMA solution for scheduling Bluetooth and 802.11 packets on the same device.
  Frequency nulling
Non-collaborative:
  Adaptive frequency hopping
  Varying packet size, data rates, encapsulation
  MAC scheduling
  Transmit power control
Coexistence Mechanisms

## Slide 13: Effect of Scheduling on BT
IEEE 802.15-01/00143r0

## Slide 14: HV3 is ”Friendlier” to WLAN
IEEE 802.15-01/00143r0

## Slide 15
Current Status
Modeling:
  Completed performance evaluation of Bluetooth and 802.11 for 1 and 11 Mbits/s
  Performance analysis and validation of simulation results.
Coexistence mechanisms:
  submission of coexistence proposals
  evaluation of techniques submitted to TG2
  voting on coexistence mechanisms.

## Slide 16
FCC,”Title 47, Code for Federal Regulations,” Part 15, October 1998 state
  1) “Frequency hopping systems operating in the 2400-2483 MHz (..) shall use 75 hopping frequencies. (..) The average time of occupancy on any frequency shall not be greater than 0.4 seconds within a 30 second period.”
  2) “The incorporation of intelligence within a frequency hopping spread spectrum system that permits the system to recognize other users within the spectrum band so that it individually and independently chooses and adapts its hopsets to avoid hopping on occupied channels is permitted. The coordination of frequency hopping systems in any other manner for the express purpose of avoiding simultaneous occupancy of individual hopping frequencies by multiple transmitters is not permitted.”
Current FCC rules

## Slide 17
Bluetooth uses 79 pseudo-random hopping frequency pattern
Therefore the average time of occupancy on any one frequency is bounded by:
30/79 = 0.37 seconds.
Bluetooth Current Specifications

## Slide 18
Questions to the FCC (1)
BT Scheduling:
  Bluetooth device “learns” about the environment so that it decides not to transmit in “bad” channels.
  Since we are not changing the hopping pattern the average time of occupancy on any single frequency is still less than 0.4 seconds.
  Is this allowed under current FCC rules?
  Since the rules specify that 75 channels need to be used within 30 seconds, then during a 30 second period, bad frequencies can probed at least once by a POLL/NULL message exchange between the master/slave.
  Is this allowed under current FCC rules?

## Slide 19
Questions to the FCC (2)
Adaptive Frequency Hopping:
  Change of Bluetooth hopping pattern so that it avoids channels that are occupied by other devices such as WLAN (802.11b Direct Sequence)
  Reduced hopping set to n frequency channels (n < 75) and transmitted power can be reduced accordingly.
  In Europe and Japan as few as 20 hopping channels may be used allowing for flexibility.
  Change is adaptive so that device has to “learn” about the environment.
  Change will allow for increased efficiency and reduced spectral usage.
  Is this allowed under current rules?

## Slide 20
Questions to the FCC (3)
Adaptive Frequency Hopping:
  If it is not allowed, how do we go about changing the rules?
  Is the public benefit clear to you?
  What is the timeline associated with changing the rules?