## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Adaptive Frequency Hopping, a Non-collaborative Coexistence Mechanism
Date Submitted: 12th, March, 2001
Source: Hongbing Gan, Bijan Treister, et al. Company: Bandspeed Inc.
Address: 7000 West William Cannon Drive, Austin, TX78735
Voice: 512 358 9000, FAX: 512 358 9001, E-Mail: h.gan@bandspeed.com.au
Re: Submission of a coexistence mechanism, revisions of the document 802.15-00/367r0
Abstract: [The documentation presents a non-collaborative coexistence mechanism - Adaptive Frequency Hopping.
Purpose: [This is a submission to IEEE 802.15.2 of a Recommended Practice for a Non-collaborative Coexistence Mechanism.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Adaptive Frequency Hopping A Non-collaborative Coexistence Mechanism Hongbing Gan, Bijan Treister, Vitaliy Sapozhnykov, Yong Xiang Efstratios (Stan) Skafidas, et al. Bandspeed Inc. 7000 West William Cannon Drive, Austin, TX 78735 Tel: 512 358 9000 Fax: 512 358 9001

## Slide 3
Outline
IEEE 802.15.1 and 802.11b coexistence scenario
Bandspeed’s adaptive frequency hopping coexistence mechanism
  Benefits
  Implementation steps
Simulation results of the coexistence mechanism
Summary of the coexistence mechanism
Meeting the evaluation criteria
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 4
IEEE 802.15.1 and 802.11b Coexistence Scenario
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 5
802.11b
0 1 2 ……... 21 22 23 24 25 …. 50 51 52 ……….. 77 78
802.15.1 Channels
Proposed 802.15.1 hopping over the Clear Channels
Coexistence Scenario
0 1 2 ……... 21 22
(Occupied by 802.11b)

## Slide 6
802.11b
0 1 2 … 21 22 23 24 25 …. 45 46 47 48 50 51 52 …… ….. 77 78
802.15.1 Channels
Proposed 802.15.1 hopping over the Clear Channels
Coexistence Scenario
Proposed 802.15.1 hopping over the Clear Channels
(Occupied by 802.11b)

## Slide 7
802.11b
0 1 2 21 22 23 24 25 … 45 46 47 48 49 …… . 71 72 73 ... 78
802.15.1 Channels
Coexistence Scenario
Proposed 802.15.1 hopping over the Clear Channels
Proposed 802.15.1 hopping over the Clear Channels
(Occupied by 802.11b)

## Slide 8
Adaptive Frequency Hopping Coexistence Mechanism
Benefits of the coexistence mechanism
Implementation steps of the coexistence mechanism
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 9
Benefits of the Coexistence Mechanism
Non-collaborative
Significant performance improvement for both 802.15.1 WPAN and 802.11b WLAN
Very simple, very easy to implement
Low memory requirement
Fully interoperable with Bluetooth devices not supporting the mechanism
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 10
Benefits of the Coexistence Mechanism
True coexistence, automatically avoids bad channels completely
Very few extensions to current 802.15.1 standard
Avoids interference from microwave oven, etc.
Automatically avoids fading channels
Coexisting with other systems such as 802.15.3
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 11
Implementation Steps of the Coexistence Mechanism
1. Monitoring channels
2. Classifying channels as ‘Clear’ or ‘Occupied’
3. Collecting slaves’ channel classifications
4. Referendum of each channel
5. Finalizing the adaptive hopping mapping sequence
6. Implementing adaptive hopping
7. Switching between adaptive and regular hopping
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 12
1. Monitoring Channels
Method of monitoring:
Packet Loss Ratio vs. Channel
Monitoring the channels to classify as
‘Clear’ or ‘Occupied’.
(Other options are possible, see Appendix 1)

## Slide 13: 2. An Example of Channel Classification by Packet Loss Ratio
Correlation Failure
CRC Failure
Total Packets
HEC Failure
Channel Class
Packet Loss Ratio
Threshold
Total Packet Loss
Channel 0
58
8
100
0
Occupied (0)
66%
15%
66
Channel 2
65
8
100
0
Occupied (0)
73%
15%
73
IEEE 802.11b occupies channel 0-22
00000 00000 00111 11111 11111 11111 11111 11111 00000 00000 01111 11111 11111 11111 11111 1111
0 …. 2223 ….. 78 1 ….. 2123 ……. 78
Channel
Even-number channels
Odd-number channels
Class
Channel 30
2
0
100
0
Clear (1)
2%
15%
2
Notes: Where does the number come from?

## Slide 14: 3. Collecting Slaves’ Channel Classification
Available_Channel_Request
Master
Slave
Slave_Available_Channel ( )
00000 00000 00111 11111 11111 11111 11111 11111 00000 00000 01111 11111 11111 11111 11111 1111
Even-number channels
Odd-number channels
Why? Because a slave may be close to 802.11b

## Slide 15: 4. Referendum of Each Channel
Channel 0
0
7
0
0
0
0
0
0
0
0
0
Channel 2
0
7
0
0
0
1
0
0
1
0
0
Channel 30
1
7
1
1
1
8
1
1
1
1
1
After the Master collects channel class from all slaves, a referendum is carried out to select which channels to use
Channel Class: Master
Pass Mark
Channel class: Slave 2
Channel class: Slave 4
Channel class: Slave 1
Voting Score
Pass = 1, No pass = 0
Channel class: Slave 7
Channel class: Slave 5
Channel class: Slave 6
Channel class: Slave 3
Example: There are seven slaves, all supporting adaptive hopping, the Voting Score is simply the sum of the value of Class, the Pass Mark set to 7.
Notes: Master priority

## Slide 16: 5. Finalizing the Adaptive Hopping Mapping Sequence
The Pass Mark depends on:
How many slaves are supporting adaptive hopping
Choice of some minimum of number of channels (e.g. 15)
The particular implementation
00000 00000 00111 11111 11111 11111 11111 11111 00000 00000 01111 11111 11111 11111 11111 1111
Even-numbered Channels
Odd-numbered Channels
Adaptive Hopping Mapping Sequence
Master
Slave
The Master has the right to veto !!

## Slide 17: 6. Implementing Adaptive Frequency Hopping
Selection
Kernel
0
0
.
.
0
2
4
6
.
28
.
26
24
32
30
.
.
1
1
1
1
1
.
.
25
24
23
27
26
.
.
Original Hopping Channels
0
0
Adaptive Hopping
Mapping Sequence
Clear Channel Bank
channel 6
channel 2
channel 24
channel 30
bad channel, redirect
bad channel, redirect
channel 30
Notes: Uniformly

## Slide 18
Regular Bluetooth hopping sequence
Example of proposed 802.15.1 AFH sequence
20
60
53
62
55
66
6
64
8
68
57
70
59
74
10
72
12
76
23
60
53
62
55
66
24
64
25
68
57
70
59
74
26
72
27
76
Regular Bluetooth hopping sequence used when master addresses normal Bluetooth devices.
AFH used when master addresses proposed 802.15.1 devices.

## Slide 19: 7. Switching between Adaptive and Regular Hopping
Master regularly forces all slaves back to regular hopping sequence, because
The piconet may have left the 802.11b region
To re-scan all channels

## Slide 20
Simulation Results of the Coexistence Mechanism
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 21: Simulation Block Diagram
The simulation is performed using Synopsys Cossap Bluetooth Reference Design Kit
Notes: Need work out the Packet Loss Ratio (Vitaliy)
Need work out the performance improvement of WLAN (Vitaliy)
Also we need DM1 and DM5 packet type

## Slide 22: Simulation Parameters
Packet Type: DH1
Packet Length: 366 bits
Number of packets simulated: 5,000
Signal to White Noise Ratio: 10, 12.5, 15, 17.5, 20, 22.5, 25 dB
Relative TX power to WLAN: 0.1
WLAN Duty Cycle: 100%
WPAN Duty Cycle: 50%
Channel Model: Frequency-selective indoor channel (from experiments)
Notes: To be provided by Vitaliy

## Slide 23: DH 1 Packets corrupted by IEEE 802.11b
(Volts)
Notes: Mention carrier f

## Slide 24
Comparison of BER Performance of Adaptive and Regular Hopping, with WLAN occupies Channel 0-22
Notes: Need add Packet Loss Ratio
Need add WLAN performance
Add

## Slide 25
Comparison of BER Performance of Adaptive Hopping with WLAN and Regular Hopping without WLAN
The results show that Adaptive Hopping performs better than Regular Hopping EVEN without WLAN, by avoiding fading channels
Notes: Need add Packet Loss Ratio
Need add WLAN performance
Add

## Slide 26
Demonstration of Bandspeed Coexistence Performance Simulator
(Developed by Mr. Bijan Treister)
Assumes worst case scenario
Includes no channel, so if two systems transmit at the same time a collision occurs.
Interferers transmit random sized packets
Notes: Need add packet Loss Ratio vs. Channel Indicator

## Slide 27
Summary of the Coexistence Mechanism
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 28
1. Channels are monitored by Packet Loss Ratio vs. Channel
2. The channels are classified as ‘Clear’ or ‘Occupied’
3. The Master requests slaves’ channel classification
4. A referendum is conducted to select the channels to use
5. The adaptive hopping mapping sequence is finalized and sent to slaves
6. Based on the mapping sequence, the system replaces ‘Occupied’ channels with ‘Clear’ channels
7. Regularly reverts to original hopping sequence to monitor ‘Occupied’ channels
Summary of the Coexistence Mechanism
Notes: Hello Vitaliy
You are here or are you ?

## Slide 29
How the Coexistence Mechanism Meets the Evaluation Criteria
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 30
1. Collaborative or Non-collaborative
  Non-collaborative
2. Improved WLAN and WPAN performance
  Significant performance improvement for both WLAN and WPAN (See simulation results)
3. Impact on Standard
  No changes or extensions to IEEE 802.11 standard.
  Only a few extensions to IEEE 802.15.1 Specifications to implement the mechanism (see appendix)
4. Regulatory Impact
  Legal for Type 3 devices , requires change of FCC laws for Type 1 and 2 devices (see Appendix)
5. Complexity
  Very simple, very easy to implement, low memory usage

## Slide 31
6. Interoperability with systems that do not include the coexistence mechanism
  Fully interoperable.
7. Impact on interface to Higher layers
  No impact on 802.11 interface to higher layers
  No impact on Bluetooth interface to higher layers.
8. Applicability to Class of Operation
  Supports all the Bluetooth profiles
9. Voice and Data support in Bluetooth
  Supports both ACL (data) and SCO (voice) packets.
10. Impact on Power Management
  No impact, beneficial to power management

## Slide 32: Additional Benefits
Avoids interference from microwave oven, etc.
Avoids fading channels, further enhancing system performance
Coexists with other systems such as 802.15.3

## Slide 33
Appendix
Additional channel monitoring methods
Message sequence chart for implementation of the coexistence mechanism
Definitions of new commands
Why FCC laws should be changed
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 34
Additional Channel Monitoring Methods
Scanning the background RSSI versus Channel
A probing packet, whose payload contains known bits such as the access code, used to calculate the error bits.
FEC coding can help calculate the error

## Slide 35: Message Sequence Chart for implementation of the mechanism
Master
Slaves
LMP_Available_Channel_Request
The master keeps its own Channel Classification Table
LMP_Slave_Available_Channel ( )
Slaves
LMP_Slave_Available_Channel ( )
(Slaves not supporting adaptive hopping will return LMP_not_accepted, with reasons as unknown LMP PDU)
Timeout 1

## Slide 36
Master
Slaves
LMP_Adaptive_Hopping_Request ( )
LMP_Accepted
Master carries out the referendum to select which channels to use, the Master then generates the adaptive hopping mapping sequence and make adaptive hopping request
LMP_Not_Accepted
Slaves may or may not accept adaptive hopping
Slaves
Based on the mapping sequence, the selection kernel replaces ‘Occupied’ channels with ‘Clear’ channels from the ‘Clear channel bank’
LMP_Regular_Hopping
LMP_Accepted
Timeout 2
Start Timeout 1 in previous page

## Slide 37: Definition of New Commands
  Adding four LMP commands:
  LMP_Available_Channel_Request
  LMP_Slave_Available_Channel
  LMP_Adaptive_Hopping_Request
  LMP_Regular_Hopping

## Slide 39: FCC Laws
15.247a1) “Frequency hopping systems shall have hopping channel carrier frequencies separated by a minimum of 25 kHz or the 20 dB bandwidth of the hopping channel, whichever is greater. The system shall hop to channel frequencies that are selected at the system hopping rate from a pseudorandomly ordered list of hopping frequencies. Each frequency must be used equally on the average by each transmitter. The system receivers shall have input bandwidths that match the hopping channel bandwidths of their corresponding transmitters and shall shift frequencies in synchronization with the transmitted signals.”
15.247a1ii) “Frequency hopping systems operating in the 2400-2483.5 MHz and 5725-5850 MHz bands shall use at least 75 hopping frequencies. The maximum 20 dB bandwidth of the hopping channel is 1 MHz. The average time of occupancy on any frequency shall not be greater than 0.4 seconds within a 30 second period.”

## Slide 40: Why the FCC Laws should be changed
It is beyond any coexistence scheme to operate effectively if one is forced (by law) to transmit evenly on all channels.
It makes more sense for coexistence if devices are allowed to intelligently decide to avoid regions of the ISM band to increase their own throughput, and that of fellow networks.
Adaptive hopping will be the only foreseeable measure which will enable devices in the ISM region to coexist with existing radiators and new radiators.
Without changes to the FCC laws, personal office spaces / homes will be prone to interference from adjacent networks.
Frequency reuse will be almost impossible with high power networks in the vicinity not adhering to adaptive hopping.