## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Physical Layer proposal for the 802.15.4 Low Rate WPAN Standard]
Date Submitted: [March 2001]
Source: [Benno Ritter] Company: [Philips Semiconductors]
Address: [1109 McKay Dr. M/S48, San Jose, CA, 95131, U.S.A.]
Voice:[+1 (408) 474 5116], FAX: [+1 (408) 474 7247], E-Mail:[benno.ritter@philips.com]
Re: [ PHY layer proposal submission, in response of the Call for Proposals ]
Abstract: [This contribution is a PHY proposal for a Low Rate WPAN intended to be compliant with the P802.115.4 PAR. The PHY is designed for ultra low cost and low power consumtion networks which are battery powered. The option to implement different output power levels allows to cover a single family dwelling with a robust communication link.]
Purpose: [Response to IEEE 802.15.4 TG Call for Proposals]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: PHY Proposal for Low Data Rate Application
Benno Ritter
Philips Semiconductors

## Slide 3: Contents
Air Interface Physical Layer
System Realization
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 4: Air Interface Physical Layer
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 5: Frequency Bands
2.4GHz ISM band
  Channel spacing: 3MHz
  F = 2404 + 3k MHz with k = 0, 1, …, 25
  Common band:
    USA & Europe (excluding Spain)
    2.449MHz – 2.470MHZ
    k = 15, …, 22; equals 8 channels
Other bands could be supported
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 6: Direct Sequence
Spread spectrum regulations allow higher transmit power
  Longer range
  Transmit power: -4 to +20dBm
Direct sequence
  Faster acquisition than frequency hopping
  Complexity in digital domain (cheaper)
  Processing gain of 10.4dB
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 7: Modulation
GFSK
  Constant envelope  (cheap) non-linear PA
  Spectral efficiency
  Modulation index; h = 0.5  10%
  Pre-modulation filter; BT = 0.5
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 8: Bit Rates
200kbps (raw)
21.875kbps low bit rate option:
  Trade data rate for extra range via coding
  Over air bit rate remains 200kbps
  Hadamard Error Correction Coding
    achieves reliable link at low SNR
  Longer preamble and SOP
    reliable synchronisation at low SNR
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 9: Range Estimation
Using Firefly TRD/RSI propagation model
Approx. x2
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 10: Range Estimation

## Slide 11: Modulation
Transmitted spectrum:

## Slide 12: Physical Layer Characteristics
Rx | 
Sensitivity Level@ 200Kbps | -95dBm
Adjacent channel interference | -25dB
Radio freq. Tolerance |  100KHz 40ppm
Max input level | -20dBm (10-3>BER)
Rx/Tx switching time | <250us
Tx | 
Output Power | -4dBm to +20dBm
Spectral mask @1.65MHz offset | 20dBc
Spectral mask @2MHz offset | 28dBc
Spurious emission | Compliant to ETSI 300 328 spec.
BER assumed < 10-3

## Slide 13: Simulated Performance

## Slide 14: System Realisation
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 15: Applications :- Slave Device
Light Switch
Thermostat
Accessory Control
Security Sensor
Computer Keyboard
Radio
Radio
Radio
Radio
Radio
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 16: Block Diagram
RF IC
Control
Transmit Data
Receive Data
BASEBAND
Application
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 17: Development Platform
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 18: Target Applications 1
Desktop PCs and Home Entertainment Systems (Home Theatre TV)
  Computer peripherals;
  HID devices
Video conference equipment
  Remote control
Video gaming equipment
  Multi-player PC & video games
  Playing a PC DVD game in front of a TV monitor
Remote controls for audio and video equipment
PC Enhanced & stand alone toys
  In-room coverage
  Home+yard coverage

## Slide 19: Target Applications 2
Home appliances and general consumer electronic devices
  Existing home security systems, electrical & heating systems
  Wireless door and opening monitoring, system control
  Glass breakage monitoring (sensors)
  Wireless Keypads
  Child Monitor
  Smoke and flame detectors
  Fire Pull stations
  Personal transponders
  Lighting and remote control of appliances in the home;
    Blinds
    Shades
    Fireplaces
    Pool/Spa equipment
    Garage door openers
  Voice Control
  Home Comfort Control
New device categories that have not yet been developed, such as news tablets, and keyboards with built-in displays

## Slide 20: Air Interface Summary
Direct Sequence
2.4GHz band (and other)
200kbps
-4 to +20dBm
GFSK, h = 0.5, BT = 0.5
Low data rate option: 21.875kbps
Notes: Page <number>
        <footer>
<header>
<date/time>