## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Outline presentation of Low Data Rate CMOS solution]
Date Submitted: [March 13, 2001]
Source: [Hans van Leeuwen] Company [STS Smart Telecom Solutions B.V.]
Address [Zekeringstraat 40, 1014 BT, AMSTERDAM, The Netherlands]
Voice:[+31 20 420 4200], FAX: [+31 20 420 9652], E-Mail:[hans.vanleeuwen@sts.nl]
Re: [Presentation of a low data rate transceiver proposal]
Abstract: [Presentation of a low data rate transceiver PHY and thin MAC proposal; proven, manufacturable, low data rate DSSS solution for use in European and US license exempt bands]
Purpose: [General information for selection process, discussion about 10kbps data rate use and introduction to a demonstration in July]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Outline presentation of a Low Data Rate solution
a low data rate transceiver PHY and thin MAC proposal; proven, manufacturable, low data rate DSSS solution for use in European and US license exempt bands

## Slide 3: Position in the wireless information chain

## Slide 4
Conformance issues (Ch 2)
UMC very low
signal robustness
interference & susceptability
coexistence
interoperability
manufacturability
time-to-market
regulatory impact, fitting to ISM bands
maturity
scalability
location awareness: meters

## Slide 5
Conformance issues (Ch 2)
UMC very low
signal robustness
interference & susceptability
coexistence
interoperability
manufacturability
time-to-market
regulatory impact, fitting to ISM bands
maturity
scalability
location awareness: meters

## Slide 6
Conformance issues (Ch 3, MAC)
transparent upper layer protocols
ease of use
delivered data throughput
data types (bursty data)
topologies (M-S, P-P, …)
max active connections
adhoc network
portal
realiability
power management types (sleep, user , rx, tx)
security

## Slide 7
Conformance issues (Ch 3, MAC)
transparent upper layer protocols
ease of use
delivered data throughput
data types (bursty data)
topologies (M-S, P-P, …)
max active connections
adhoc network
portal
realiability
power management types (sleep, user , rx, tx)
security

## Slide 8
Conformance issues (Ch 4, PHY)
size & form factor
frequency band
simultaneous operating systems
signal acquisition method
range (power output & sensitivity)
PER/BER
multipath immunity
power consumption

## Slide 9
Conformance issues (Ch 4, PHY)
size & form factor
frequency band
simultaneous operating systems
signal acquisition method
range (power output & sensitivity)
PER/BER
multipath immunity
power consumption

## Slide 10: Starting design requirements
868 ETSI, 915 FCC, (2400 ETSI/FCC)
low power (power down options)
high interference supression
transceivers or transmitters
easy adaptive to application by non RF engineer
PHY and MAC (partly) in a single chip
flexible by register settings
variable packet length (10 Byte as default)
low BOM cost: 2001 $5 for trx ,later 2$ tx, 3$ txrx

## Slide 11: ETSI
868.0 -868.6 or 868.7 - 869.2 Mhz
2 available DSSS channels (bands): 600, 500Khz
spurious -36dBm outside the bands
-57dBm at FM, TV and Telecom frequencies
max power output 25mW
1% or 0,1% duty cycle

## Slide 12
FCC
902 - 928 Mhz
500KHz RF BW
-20 dBc for side lobes
process gain > 10dB
power output below 6mW: easy approval
100% duty cycle
no specific channel requirement
frequency agility is preferred

## Slide 13: ETSI/FCC/..
2400 - 2483MHz
< 10mW
no spreading, no data rate requirements
above 10mW: > 250kbps aggregate bitrate, 10dB process gain

## Slide 14: Drivers
LOW COST
get a small data packet across is important, NOT the speed
low power
range
high interference suppression

## Slide 15
4 major design issues of low data rate DSSS
  fast acquisition
  large frequency inaccuracy
  strong interferers
  low current consumption

## Slide 16: Thin MAC
FIFO
Frame building (PLCP)
PHY interface
MLME
Rx_Signal
Tx_Signal
MAC + Application
Actuator
Sensor

## Slide 17: Air Frame

## Slide 18: Proposed PHY
868MHz
  10/20kbps, 31/15 chips direct sequence spreading
902MHz
  10/20kbps, 31/15 chips, 1MHz channels (interference avoidance)
2400MHz
  10/20kbps, 31/15 chips, 1MHz channels

## Slide 19: PHY

## Slide 20: Example 1, RKE
automotive requirement
10ms sync time for frequency and code synchronization
10ms data transmission (100bit rolling code @ 10kbps)
15/200ms duty cycle receiver (immediate response)
includes full sync-detection cycle
on-time transmitter 200ms
receiver average current consumption ~1mA

## Slide 22
Example 2, Skate Watch
Even less power consumption
2s duty cycle receiver
less parameter freedom: freq & code position known
synchronised tx & rx
2 ms pre-amble on: sync time
3.2ms data transmission (32bit @ 10kbps)
on-time transmitter <10ms

## Slide 23
Example 3, AMR
Long range
5s duty cycle measurement
download data to gateway on demand
beacon
2 ms pre-amble on: sync time
3.2ms data transmission (32bit @ 10kbps)
on-time transmitter 20ms

## Slide 24: Discuss:
AMR part of 802.15.4?
mobile receiver (master)
battery powered system
data throughput is not important, but getting the message across is
TCP/IP in the sensor/slave?
can this be done otherwise?

## Slide 25
Current implementation
0 dBm power output
~ -100 dBm sensitivity
10kbps air data rate
31 chips spreading
-20dB interference suppression
sync in 2 - 12 ms
1 ~ 2mA average (200ms response time, PHY&MAC, 12ms sync time)
44 pin MLT package

## Slide 26
Protocol choices
Rx always on, Sensor shortest Tx on-time:
    20 ms pre amble
    monitoring, alarm etc
Rx duty cycling, Tx uses longer pre-amble:
    200 ms
    battery master, switch, RKE
Master Beacon, slave Rx duty cycling, network keeps synchronised:
    2 ms
    networks

## Slide 27
Single Chip, 10kbps, DSSS, 900MHz transceiver, thin MAC, CRC, uC interface, RS232

## Slide 28: Time to market
current implementation now
engineering samples in May
demonstration projects from June
first quantities in 2001

## Slide 29: Manufacturability
0,35 CMOS, 44pin MLT (7x7 mm)
1/2” PCB with very few external components
easy to design in by digital engineers
low cost X-tal
wide SAW filter (optional, but advisable)
low cost uC

## Slide 30: Conclusions
the thin layer MAC allows to bolt on any extended protocol (standard ……)
scalable PHY
manufacturable, at low cost and ready for market in 2001