## Slide 1
IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Collaborative Coexistence Mechanism: Mobilian META + Symbol
Date Submitted: March 12, 2001
Source: Steve Shellhammer & Jim Lansford
Company: Symbol Technology, Inc. & Mobilian Corp.
Address1: One Symbol Plaza, Holtsville NY 11742
Address2: 7431 NW Evergreen Parkway, Suite 220, Hillsboro, OR 97124
Voice1: (631) 738-4302, FAX: (631) 738-4618, E-Mail: shell@symbol.com
Voice2: (405) 377-6170, Fax: (425) 671-6099, E-Mail: Jim.Lansford@mobilian.com
Re: Submission of a Coexistence Mechanism in response to IEEE 802.15-00/009r4
Abstract: This is a proposal to P802.15.2 for a collaborative coexistence mechanism between Bluetooth and 802.11b; it combines two prior submissions made separately that both time-multiplex access to the wireless medium
Purpose: This is a submission to IEEE 802.15.2 of a Recommended Practice for a Collaborative Coexistence Mechanism.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributors acknowledge and accept that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: IEEE P802.15 Working Group for Wireless Personal Area NetworksTM
Collaborative Coexistence
Mechanism Submission:
Mobilian’s META + Symbol’s TDMA

## Slide 3: Mobilian’s Proposal: META
Mobilian’s META
  Tightly coordinated queuing and scheduling algorithm
  Dynamically adapts to traffic and optimizes for traffic type
    Can optimize for SCO links
    Can maximize WLAN throughput when no SCO links
  Manages traffic of single station and single piconet
    Can sense one other piconet and adapt to it
    Other devices do not need META
  Manages user bubble (<2 meters)
  Can share common antenna
Simulator can accurately predict performance
Silicon in development

## Slide 4: Symbol’s Proposal
Symbol’s TDMA
  Macro-level time multiplexing
  Manages all piconets that have TDMA mechanism
  Orthogonality assures that no interference can occur, regardless of density
  Does not support SCO links
  Embedded BT device must be piconet master
  Coordinates traffic over an entire AP’s coverage area
Performance can be analyzed deterministically
Systems in development

## Slide 5: Mobilian’s META
Dynamic algorithm schedules traffic
Knowledge of time-frequency collisions is key
  Simultaneous transmission or reception allowed
  Tx simultaneous with Rx allowed if not in-band (requires good LNA)
  Critical for SCO operation-WLAN can work around in-band collisions
This figure does not show polls/nulls, which often dominates Bluetooth traffic
Time
802.11 beacon interval
(Packet widths are not to scale…)
BT
WLAN

## Slide 6: Simulation Program Update
Bluetooth Nodes: +20dBm
AP: 802.11b (+20dBm)
STA: META (+20dBm)

## Slide 7: Simulation Tool vs. Experimental Results
0
1
2
3
4
5
6
7
8
0
10
20
30
40
50
60
70
80
90
100
Received Signal Power (-dBm)
Throughput (Mb/s)
BT=OFF (measured)
BT=1m (measured)
BT=OFF (simulated)
BT=1m (simulated)
Simulation Tool accurately models experimental WLAN / BT performance
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 8: Conference Room Usage
Many stations, each with independent piconets
Bluetooth speakerphone
As before, aggregate throughput is shared among all users
Back to Single
User Scenario
Conference Room Scenario

## Slide 9: Office Usage Model
Cluster of users in cubicles, each of which has an independent piconet
Throughput is aggregate throughput measured from Access Point
Back to Single
User Scenario
Office Scenario

## Slide 10: Individual User
BT headset operating from same laptop as Wi-Fi station
Individual Scenario

## Slide 11: WLAN Throughput in an Office Scenario
Cluster of users in cubicles, each of which has an independent piconet
Throughput is aggregate throughput measured from Access Point
0
1
2
3
4
5
6
7
8
1
10
100
Distance from AP (m)
WLAN Throughput (Mb/s)
no interference
non TR
Office Scenario

## Slide 12: Symbol’s TDMA
Time
802.11 beacon interval
BT-WLAN boundary
(possibly delimited by CTS)
Traffic scheduling by fixed intervals or by offered load
CTS command can force WLAN nodes non-hidden nodes
to cease operation
Can manage unlimited number of piconets
BT
WLAN

## Slide 13: Implementation Requirements

## Slide 14: Benefits of Approaches
Both will operate in the same device, through a common antenna
Both techniques can be built into same device
  TDMA is good for high piconet density
  META is for BT SCO, and gives better throughput, especially when few piconets are nearby
For reference, see…
  00360r0P802-15_TG2-Mobilian_coexistence_proposal
  01025r0P802-15_TG2-TDMA-80211-Bluetooth

## Slide 15: Conclusions
For a Collocated Coexistence Mechanism the best choice is some type of TDMA to ensure orthogonality, independent of interference power levels and filter performance.
Both Mobilian and Symbol proposals use TDMA, but with different objectives and usage models
Merger of these two proposals covers virtually all usage models
Both proposals are being built into commercial products