## Slide 1
IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Summary of Mobilian+Symbol Joint Proposal
Date Submitted: March 13, 2001
Source: Steve Shellhammer & Jim Lansford
Company: Symbol Technology, Inc. & Mobilian Corp.
Address1: One Symbol Plaza, Holtsville NY 11742
Address2: 7431 NW Evergreen Parkway, Suite 220, Hillsboro, OR 97124
Voice1: (631) 738-4302, FAX: (631) 738-4618, E-Mail: shell@symbol.com
Voice2: (405) 377-6170, Fax: (425) 671-6099, E-Mail: Jim.Lansford@mobilian.com
Re: Submission of a Coexistence Mechanism in response to IEEE 802.15-00/009r4
Abstract: This is a closing summary of the Mobilian+Symbol Proposal for Collaborative Coexistence
Purpose: This summary highlights the key issues in the joint proposal.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributors acknowledge and accept that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: IEEE P802.15 Working Group for Wireless Personal Area NetworksTM
Collaborative Coexistence
Mechanism Submission:
Mobilian’s META + Symbol’s TDMA
Summary for Voting

## Slide 3: Examination of the issues
Addressing open issues
  Fairness of the approaches
  Switching between modes
  Actual implementation performance
Summary

## Slide 4: What about fairness?
Mobilian proposal
  BT SCO always gets right of way
  Data traffic takes turns (just like a 4-way stop) but META can be instructed to prefer one over the other (priority road)
Symbol proposal
  Acts exactly like a traffic light…TDMA
TI Proposal
  BT SCO always gets the right of way
  If two packets come to intersection, light flips a “weighted” coin to decide which goes first-increases latency
WLAN Traffic
BT Traffic
The traffic models can be compared to an intersection….
BUT---META is an overpass!! Allows simul-taneous BT-WLAN Rx or Tx…MUCH higher throughput

## Slide 5: What about mode transitions in the merged proposal?
If no Symbol AP present, META devices manage their local bubble
If Symbol AP present, META devices will always follow its lead
  Symbol AP’s only go into TDMA mode in high concentration areas, under command of AP management SW
    This is application specific, and is either/or
  If Symbol AP doesn’t tell STA to do TDMA, it does META
    This is the normal mode

## Slide 6: The Mobilian Approach is real…
Mobilian’s coexistence technology has been demonstrated in a hardware implementation
Source:
Mobilian TrueRadio™ Demo – COMDEX 2000
Demo Set-up:
* Notebook PC with collocated BT & 802.11b
* BT node ~ 1 m away
* 802.11b AP ~ 15 m away in walled office environment
802.11b; BT=OFF
802.11b with TrueRadio™; BT=ON
802.11b; BT=ON

## Slide 7: Conclusion
The Mobilian+Symbol approach is well researched, simulated, and documented
It solves the coexistence problem using TDMA, and works for any number of piconets
Thank you for your support

## Slide 8: Backup

## Slide 9: Simulation Program Update
Bluetooth Nodes: +20dBm
AP: 802.11b (+20dBm)
STA: META (+20dBm)

## Slide 10: Conference Room Usage
Many stations, each with independent piconets
Bluetooth speakerphone
As before, aggregate throughput is shared among all users
Back to Single
User Scenario
Conference Room Scenario

## Slide 11: Office Usage Model
Cluster of users in cubicles, each of which has an independent piconet
Throughput is aggregate throughput measured from Access Point
Back to Single
User Scenario
Office Scenario

## Slide 12: Individual User
BT headset operating from same laptop as Wi-Fi station
Individual Scenario

## Slide 13: WLAN Throughput in an Office Scenario
Cluster of users in cubicles, each of which has an independent piconet
Throughput is aggregate throughput measured from Access Point
0
1
2
3
4
5
6
7
8
1
10
100
Distance from AP (m)
WLAN Throughput (Mb/s)
no interference
non TR
Office Scenario

## Slide 14: Symbol’s TDMA
Time
802.11 beacon interval
BT-WLAN boundary
(possibly delimited by CTS)
Traffic scheduling by fixed intervals or by offered load
CTS command can force WLAN nodes non-hidden nodes
to cease operation
Can manage unlimited number of piconets
BT
WLAN

## Slide 15: Mobilian’s META
Dynamic algorithm schedules traffic
Knowledge of time-frequency collisions is key
  Simultaneous transmission or reception allowed
  Tx simultaneous with Rx allowed if not in-band (requires good LNA)
  Critical for SCO operation-WLAN can work around in-band collisions
This figure does not show polls/nulls, which often dominates Bluetooth traffic
Time
802.11 beacon interval
(Packet widths are not to scale…)
BT
WLAN

## Slide 16: Benefits of Approaches
Both will operate in the same device, through a common antenna
Both techniques can be built into same device
  TDMA is good for high piconet density
  META is for BT SCO, and gives better throughput, especially when few piconets are nearby
For reference, see…
  00360r0P802-15_TG2-Mobilian_coexistence_proposal
  01025r0P802-15_TG2-TDMA-80211-Bluetooth