## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Nokia PHY submission to Task Group 4]
Date Submitted: [09 March, 2001]
Source: [Mauri Honkanen] Company [Nokia]
Address [Visiokatu 1, P.O.Box 100, FIN-33721 Tampere, Finland]
Voice:[+358 7180 35356], FAX: [+358 7180 35935], E-Mail:[mauri.honkanen@nokia.com]
Re: [Original document]
Abstract: [Submission to Task Group 4 for consideration as the Low Rate PHY for 802.15.4]
Purpose: [Overview of PHY proposal for evaluation]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Nokia PHYsical layer submission to IEEE 802.15 Task Group 4
Presented by
Mauri Honkanen
Nokia

## Slide 3: Contents
Requirements
Operation frequency band and channel structure
Bit rate, modulation and performance
Link budget
Interference
Implementation examples
Conclusions

## Slide 4: General PHY requirements
Minimized RF and BB complexity
Very low cost
Strongly minimized power consumption
Relaxed performance requirements
Unlicensed operation frequency band
FCC and ETSI compliant
Mature, low risk approach

## Slide 5: Key points
Proposed PHY optimized for lowest complexity and lowest power consumption
Device classes introduced for different applications
  Communication between different classes is possible
Any available, wide enough frequency band can be used (default 2.45 GHz ISM band)

## Slide 6: Power consumption and operation time
Assumed duty cycle 1%
Idle time power consumption assumed to be 1/1000 of power consumption in active mode.

## Slide 7: Implications of power consumption requirements
Transceiver should consume about 10-25 times less power than current Bluetooth approaches to be feasible for button batteries
  It is possible with very low duty cycles (<< 1%)
  In active mode the whole transceiver including digital processing should consume only ~4 mW with small button cell and ~12 mW with large button cell
  Idle time dominates power consumption due to low duty cycles
  Synthesizer is also critical

## Slide 8: Operation frequency band
Default is 2.45 GHz ISM band
  Unlicensed and global
  Congested resulting in interference
  Quite high frequency from minimum implementation and propagation point of view
Optional bands: 902-928 MHz in US and 433.050 - 434.790 MHz in Europe
  Smaller propagation loss, potentially less interference
  Only regionally available
Any wide enough band available for short-range devices can be used

## Slide 9: Channel structure #1 in 2400-2483.5 MHz
83 channels, center frequencies at 2400.5 + k x 1 MHz, where k = 0...82
    Located between Bluetooth channels to suppress interference from and to Bluetooth
2400
2401
2402
2403
2481
2482
2483
2480
Bluetooth channels
Channels of the
proposed system
IEEE 802.11b channel
in North America and Europe
IEEE 802.11b channel
in Europe

## Slide 10: Channel structure #2 in 2400-2483.5 MHz
83 channels, center frequencies at 2401 + k x 1 MHz, where k = 0...82
    Better compatibility with Bluetooth
    Outermost channels benefitially located
2400
2401
2402
2403
2481
2482
2483
2480
Bluetooth channels
Channels of the
proposed system
IEEE 802.11b channel
in North America and Europe
IEEE 802.11b channel
in Europe

## Slide 11: Device classes
Device classes dependent on applications
Smaller TX power => smaller operating space and power consumption
Fixed frequency => simpler implementation
Generally, sensitivity is not a crucial item from power consumption point of view

## Slide 12: Bit rate and modulation
Maximum physical layer bit rate 200 kbps
    Data rate scalability achieved with lower activity, shorter packets and possible repetition coding
    Long symbol duration results in small ISI in indoor channels
    200 kbps aggregate capacity considered adequate from application point of view
2GFSK modulation with modulation index h = 2...3 and BT = 0.5
    Constant envelope for low power TX architecture
    Spectrum efficiency sacrificed for minimum complexity and low power RX implementation
    Relaxed requirements for phase noise, I/Q imperfections and frequency drift

## Slide 13: Modulation spectrum
2GFSK modulation with modulation index h = 2.5, BT = 0.5

## Slide 14: Performance in AWGN channel
C/NBER = 1e-3 = 13 dB
C/NBER = 1e-3 = 13.5 dB
2GFSK, modulation index h = 2.5, BT = 0.5,
f-3 dB, highpass = 50 kHz, f-3 dB, lowpass = 300 kHz

## Slide 15: Performance in flat fading Rayleigh channel

## Slide 16: Channel coding
By default no channel coding of any kind utilized
    Coding does not help much when the transmitted frame is overlapped by high power interference in both frequency and time
    Increases baseband complexity
    No need to extend range by means of coding
    Real-time services are not in focus
Reliability ensured by upper layer retransmissions
If needed, repetition coding can be used
    Simple implementation

## Slide 17: Link budget at 2.45 GHz
Fading margin of 16 dB ensures that C/N = 13 dB or better in 97% of
the channels at range of 1/3/10 m.

## Slide 18: Interference susceptibility
2.45 GHz ISM band will be congested
Low power system cannot compete with TX power
Relaxation in interference susceptibility accepted to alleviate RX linearity requirements
    RX linearity requirements similar to Bluetooth (IIP3 = -15...-20 dBm) would not result in low-power RX, since RX linearity directly affects power consumption
    In case of co-channel interference, strong adjacent channel interference, blocking or intermodulation, packets are retransmitted

## Slide 19: Interference susceptibility example: RX IIP3  -30 dBm
How far away should a simultaneous transmission occur not to block the receiver?
RX (IIP3 
-30 dBm)
Bluetooth TX
transmitting
at 0 dBm
TX
IEEE 802.11b
WLAN TX
transmitting
at 20 dBm
Another TX of the
proposed system
transmitting
at -10 dBm
0 m
0.3 m
1 m
10 m

## Slide 20: Frame structure
Preamble should be long enough to assist frequency and symbol synchronization
  Preamble format and length to be defined later
Header and payload left to be defined in the MAC layer
Preamble
16...40 bits
Header + payload + CRC etc. (defined by MAC layer)

## Slide 21: TX implementation example

## Slide 22: RX implementation example

## Slide 23: Conclusions
Nokia IEEE 802.15.4 physical layer proposal comprising
  200 kbps maximum data rate, scalability achieved by means of packet sizing
  Operation range from 1 to 10 meters
  2GFSK modulation with large modulation index
  Two channel arrangements for 2.45 GHz ISM band, though the system is not limited to that band
Spectrum efficiency, link performance and interference tolerance sacrificed for minimum power, minimum complexity implementation